## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [TSCH-MAC PIB attributes for macTimeslotTemplate]
Date Submitted: [9 July 2014]
Source: [Patrick Kinney] Company [Kinney Consulting LLC]
Address [Chicago area, IL, USA]
Voice:[+1.847.960.3715], E-Mail:[pat.kinney@ieee.org]
Re: [Justification for changes to TSCH default value]
Abstract: [Changes to TSCH default values for different bands]
Purpose: [To assist in the comment resolutions to TSCH]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
Revision to 802.15.4-2011 with roll-ups of:
802.15.4e-2012
802.15.4f-2012
802.15.4g-2012
802.15.4j-2013
802.15.4k-2013
802.15.4m-2014
802.15.4p-2014
And corrigenda as per 15-12-0367, changes requested by ETSI, and clarifications to such entities as timing for Acknowledgment frames, et al.
802.15.4-2015

## Slide 3: TSCH Overview (for more details see 15-11-484-03)
Process Automation applications with a particular focus on equipment and process monitoring
Operation
  All devices in the same network synchronize slotframes
  All timeslots are contained within a slotframe cycle
  Timeslots repeat in time: the slotframe period
  Device-to-device communication within a timeslot includes packet Tx/Rx & ACK Tx/Rx

## Slide 4: TSCH Overview
Typical application segments are:
Process automation facilities for the following:
  Oil and gas industry
  Food and beverage products
  Chemical products
  Pharmaceutical products
  Water/waste water treatments
Automation Systems such as:
  Smart grid networks
  Lighting networks
  Factory automation

## Slide 5: TSCH Overview
The TSCH mode uses time synchronized communication and channel hopping to provide network robustness through spectral and temporal redundancy.
Time slotted communication links increase potential throughput by minimizing unwanted collisions that can lead to catastrophic failure and provides deterministic, yet flexible, bandwidth for a wide variety of applications.
Channel hopping extends the effective range of communications by mitigating the effects of multipath fading and interference.
TSCH is also topology independent; it can be used to form any topology from a star to a full mesh.
TSCH MAC primitives can be used with higher layer networking protocols to form the basis of reliable, scalable, and flexible networks.

## Slide 6: MAC behaviors unique to TSCH
The TSCH mode introduces no unique commands specific for this mode; however, IEs are used extensively.
TSCH uses EBs containing the TSCH Synchronization payload IE, TSCH-Slotframe and Link payload IE, TSCH Timeslot payload IE, and Channel Hopping payload IE to advertise the presence of a TSCH PAN and allow new devices to synchronize to it.
Devices maintain synchronization by exchanging acknowledged frames within defined timeslot windows and providing timing corrections in the acknowledgment via the ACK/NACK Time Correction IE.
Communication resources are broken up into timeslots that are organized into repeating slotframes

## Slide 7: TSCH areas within the 802.15.4 rev draft
TheTSCH-Slotframe structure behavior is cited in 5.2.7, PAN formation is cited in 5.3.6, synchronization is stated in 5.5.3, the IEs are described in 6.5.3.2, 6.5.3.3, 6.5.3.4, and the primitives are declared in 7.2.20.

## Slide 8: TSCH link example for a 3-timeslot slotframe
Nodes A and B communicate during timeslot 0, nodes B and C communicate during timeslot 1, and timeslot 2 is not being used. Every three timeslots, the schedule repeats, but note that ASN increments continuously. The pairwise assignment of a directed communication between devices in a given timeslot on a given channelOffset is a link.

## Slide 9: Time Slotted Channel Hopping (TSCH)
Physical channel, CH, in a link is made according to the following formula:
  CH = macHoppingSequenceList [(macASN + channelOffset) % macHoppingSequenceLength]
Use of a channelOffset allows for different channels to be used at a given macASN for a given macHoppingSequenceList. There are macNumberOfChannels channelOffsets that will result in a unique channel for that combination of macASN and macHoppingSequenceList.

## Slide 10: TSCH Issues
Priorities
  Need a mechanism to favor deterministic links over other types of links
TSCH PIBs
  Upper ranges (0xffff) for macTsMaxTx & macTsTimeslotLength are insufficient to describe maximum values for sub GHz PHYs such as SUN
Defaults
  CCA values not correct for ETSI 300 328 (2450 band)
  Defaults are not appropriate for 915 band
Editorial
  Timeslot ID field should be set to the value of macTimeslotTemplateId
  Figure 147—add Ack Wait field before RXTX and after RX Wait
  5.3.6 – correct references in bulleted items

## Slide 11: Proposed TSCH-MAC PIB attributes for macTimeslotTemplate
Attribute | Type | Range | Description | Band Defaults | 
 |  |  |  | 2450 | 915
macTimeslotTemplateId | integer | 0x00–0xef | Identifier of Timeslot Template | 0 | 0xf0
macTsCCAOffset | integer | 0x0000–0xffff | The time between the beginning of timeslot and start of CCA operation, in μs | 1800 | 1800
macTsCCA | Integer | 0x0000–0xffff | Duration of CCA, in μs | 128 | 5000
macTsTxOffset | integer | 0x0000–0xffff | The time between the beginning of the timeslot and the start of frame transmission, in μs | 2120 | 2800
macTsRxOffset | integer | 0x0000–0xffff | Beginning of the timeslot to when the receiver shall be listening, in μs | 1120 | 1800
macTsRxAckDelay | Integer | 0x0000–0xffff | End of frame to when the transmitter shall listen for acknowledgment, in μs | 800 | 800
macTsTxAckDelay | Integer | 0x0000–0xffff | End of frame to start of acknowledgment, in μs | 1000 | 1000
macTsRxWait | Integer | 0x0000–0xffff | The time to wait for start of frame, in μs | 2200 | 2800
macTsRxTx | Integer | 0x0000–0xffff | Transmit to Receive turnaround, in μs | 192 | 1000
macTsMaxAck | Integer | 0x0000–0xffff | Transmission time to send an acknowledgment, in μs | 2400 | 6000
macTsMaxTx | Integer | 0x00000–0xfffff | Transmission time to send the maximum length frame, in μs | 4256 | 103040
macTsTimeslotLength | Integer | 0x00000–0xfffff | The total length of the timeslot including any unused time after frame transmission and acknowledgment, in μs | 10000 | 120000

## Slide 12: Summary
Roll-up of six PHY amendments show that many amendments are using newly introduced behaviors from the MAC amendment such as enhanced beacons, information elements, enhanced acknowledgments
TSCH, dominating industrial sensor networks, is the foundation used by the IETF 6tisch effort to standardize new higher layer protocols
TSCH timings must change per band to accommodate data rates, regulatory, etc.
Numerous mistakes in TSCH text must be corrected