## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Security Threats in IEEE 802.15.8 PAC
Date Submitted: [14 July 2014]
Source: [Byung-Jae Kwak, Kapseok Chang, Moon-Sik Lee]1,
[Sangseok Yun, Sanghun Im, Jeongseok Ha]2
Company: [ETRI, Daejeon, Korea]1, [KAIST, Daejeon, Korea]2
Address: [218 Gajeong-ro, Yuseong-gu, Daejeon, Korea]1, [291 Daehak-ro, Yuseong-gu, Daejeon, Korea]2
Voice: [+82-42-860-6618], [+82-42-350-7524]
E-Mail: [bjkwak@etri.re.kr]1, [ssyun@kaist.ac.kr]2
Re:
Abstract: Discussion of the possible threats in IEEE 802.15.8 PAC from physical layer point of view.
Purpose: Discussion
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Security Threats in IEEE 802.15.8 PAC
July 2014

## Slide 3: Introduction
This document presents potential security threats of distributed synchronization mechanism
Distributed synchronization mechanism is vulnerable to malfunction and malicious attack
  Just 1 malicious node can mess up the entire synchronization process
Some physical layer security techniques can be used to prevent these threats effectively

## Slide 4: Security Issues
Confidentiality
  Messages sent over wireless links must be encrypted
Authentication
  Origin of messages received over wireless links must be verified
Integrity
  Integrity of messages received over wireless links must be verified
Non-repudiation
  User cannot deny having received nor sent
Access control
  Access to the network should be provided only to legitimate entities
Availability*
  The information must be available when it is needed
Security Issues
Confidentiality
Authentication
Non-
repudiation
Integrity
Access control
Availability

## Slide 5: Security Threats in IEEE 802.15.8 PAC
Synchronization
  Malicious timing reference signal
Discovery/Peering
  Battery drain attack
Communication
  Eavesdropping

## Slide 6: Synchronization
Firefly Synchronization
Timing offset
Synchronized

## Slide 7: Synchronization
Kuramoto metric
: average phase
: phase of node

## Slide 8: Simulation Results
# of legitimate node vs. malicious node
  10 vs. 0, 9 vs. 1, 8 vs. 2
Attack model
  Static attack : Malicious nodes never adjust their phases with others. They just transmit timing reference signal according to their own clocks
  Dynamic attack : Malicious nodes change their phases randomly after transmitting timing reference signal

## Slide 9: Without Malicious Nodes

## Slide 10: With 1 Malicious Node: static attack

## Slide 11: With 1 Malicious Node: worst case
When attacker’s phase is slower than network slightly

## Slide 12: With 1 Malicious Node

## Slide 13: With 2 Malicious Nodes: static attack

## Slide 14: With 1 Malicious Node: dynamic attack

## Slide 15: With 2 Malicious Nodes: dynamic attack

## Slide 16: Conventional Techniques
EBS scheme [1]
  It can deal with up to 1 malicious node
  Just one node is not enough for security
FTA-RFA scheme [2]
  It can deal with up to malicious nodes
  However, the network should be connected network

## Slide 17: Physical Layer Security Technique
Ignore pulses from malicious nodes using some features of physical layer
How do you recognize timing reference signal from a malicious device?
  Ex: Signalprints
    Location-specific channel response
    Received signal strength indication

## Slide 18: Malicious Node Elimination
Network synchronized after elimination

## Slide 19: Malicious Node Elimination
Network synchronized after elimination

## Slide 20: Conclusion
Disturbance from just 1 node can perturb entire network’s synchronization
Conventional approaches are not suitable for IEEE 802.15.8 PAC model
Physical layer security techniques can successfully eliminate malicious node’s attack with low complexity
Every user should have the ability to detect and eliminate an attack from malicious nodes for network stability
Some countermeasures to attacks in physical layer (not limited to the synchronization attack) should be dictated/enforced by standard due to the distributed nature of PAC

## Slide 21: References
[1] P. Yadav, J. A. McCann, “EBS: decentralized slot synchronization for broadcast messaging for low-power wireless embedded systems,” ACM COMSWARE 2011, Verona, July, 2011
[2] R. Leidenfrost, W. Elmenreich, C. Bettstetter, “Fault-tolerant averaging for self-organizing synchronization in wireless ad hoc networks,” IEEE ISWCS 2010, York, Sep., 2010