## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Summary of L2R Preliminary Proposals
Date Submitted: July 2014
Source: Clint Powell, Powell Wireless Commsulting, LLC
Contact: Clint Powell, Powell Wireless Commsulting, LLC
Voice: +1 480-586-8457, E-Mail: cpowell@ieee.org
Re: TG10 (L2R) Closing Report for May 2014
Abstract: Summary of Preliminary Proposals Heard at May 2014 Mtg.
Purpose: For 802.15/802.1 Joint Session
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.
Notes: Jul 12, 2010
Page 1

## Slide 2
802.15 TG10 (L2R)
  Draft a recommended practice for Layer 2 Routing of Dynamically Changing 802.15.4 Mesh Networks.
Notes: Jul 12, 2010
Page 2
----- Meeting Notes (17/01/2011 11:38) -----
Replace 1st paragraph with context for TVWS

## Slide 3
Heard 4 Preliminary Proposals
  Preliminary Proposal #1 - doc. # 15-14-0279-01
  Preliminary Proposal #2 - doc. # 15-14-0286-00
  Preliminary Proposal #3 - doc. # 15-14-0284-01
  Preliminary Proposal #4 - doc. # 15-14-0291-00
Summary of L2R Preliminary Proposals Heard at May 2014 Mtg.
Notes: Jul 12, 2010
Page 3

## Slide 4
Preliminary Proposal #1 - doc. # 15-14-0279-01
Rabarijaona, et al.
Hierarchical Mesh Tree Routing
The D2D function in 15.4m allows devices associated to the same coordinator to send packets to each other directly bur does not provide routing capability to distant nodes
Uses concept of Parent, Brother, Child nodes
Main Topics Covered
  Formation
  Maint. & Update
  Routing (MP2P) Multi Point to Point
  Routing (P2MP) Point to Multi Point
  High Reliability Option
  Data Aggregation Option
Requires:
  HMT Routing IE in the header
  Data Aggregation IE in the payload
SINR used for metric, but flexible to use other metrics
Simulated Results Given for both 11x11 and 33x33 node networks
Notes: Jul 12, 2010
Page 4

## Slide 5
Preliminary Proposal #2 - doc. # 15-14-0286-00
Sato, N., Fukui, K.
L2R Preliminary Proposal
Main Topics Covered
  Routing establishment consists of upward / downward route establishments
  HOP-by-HOP retry
  BS (Base Station) switch consideration
  Upward Routing Estab.
    Hello frame sent to neighbor
    Incoming link cost
    Outgoing link cost
    Mutual link cost computed from Incoming and Outgoing
  Downward Routing Estab.
    Route record frame sent to parent
    A node can send a merged route record if the node receive a route record from its child
    PAN coord. sends frame using source routing
      Address routing is included in header
  HOP-by-HOP retry
    Propose provides retransmission so that it retries after longer period than MAC currently provides
    In retry, a node can change next hop, selecting from candidate parents when it failed to transmit to the parent
  Change Routing
    Change in next hop parent if failure to current parent
Hop Count used for metric, but flexible to use other metrics
Simulated Results Given for both 11x11 and 33x33 node networks
Notes: Jul 12, 2010
Page 5

## Slide 6
Preliminary Proposal #3 - doc. # 15-14-0284-01
Lee, S., et al.
Preliminary Proposal of L2 Routing for IEEE 802.15.4m TMCTP
Main Topics Covered
  Overview of 802.15.4m TMCTP
    Extended cluster tree PAN
    Super-PAN Coord. (SPC)
    Support of multi-channels for clusters
  Advantage of L2R in TMCTP
    Enabling multi-PAN and multi-channel (MPMC) aware routing
    Suitable for applying the concept of proactive routing
  Multiple-PAN and Multi-channel (MPMC) aware routing approach
    Multiple PANs associated to establish inter-PAN route
    Multi-channel aware route establishment
    Is suitable for applying the concept of proactive routing
      SPC based topology initiation and route recovery
      Pros of having an SPC from a routing point of view
Currently only applicable to beacon only networks
Will look at extending proposal to support non-beacon networks as well
Will potentially use Hop Count and SINR for metrics, , but flexible to use other metrics
No Simulated Results Given at this point - will have/generate them for Final Proposal
Notes: Jul 12, 2010
Page 6

## Slide 7
Preliminary Proposal #4 - doc. # 15-14-0291-00
Joo, S.-S., et al.
Layer 2 Routing Preliminary Proposal to Call for Contributions
Main Topics Covered
  Link Network
    Components - PAN, FFD, RFD
    Topology - mesh (incl. star, cluster and full mesh)
    PHY/MAC link - support a variety of data rates
  Concepts used:
    Link
      Between 2 neighbors
    Virtual Link
      Between 2 devices multiple hops away
    Link Path
      Comprised of links and virtual links from a source to a destination device, a routed link-path, link network
    Link Network
      Performed in 2 stages - link connection and link network
    Virtual Link and Link Path
      Examples using a link network DSME MAC
        Cluster-Tree based Addressing
        Mesh Link on Cluster Tree
Notes: Jul 12, 2010
Page 7

## Slide 8
Preliminary Proposal #4 - doc. # 15-14-0291-00
Joo, S.-S., et al.
Layer 2 Routing Preliminary Proposal to Call for Contributions
    Multiple Grades of Mesh
      Dedicated Link
      Shared link
      Directional Link
    Cluster-Tree Mesh Routing Example Shown
      Routing
      Start/Join/Leave
      Data Forwarding
Proposal not limited to just using DSME MAC (from 15.4e), but stkandard MAC as well
Will potentially use Hop Count and packet length for metric metrics, but flexible to use other metrics
No Simulated Results Given at this point - will have/generate them for Final Proposal
Notes: Jul 12, 2010
Page 8

## Slide 9
Final Proposals Being Heard
4 Proposals Submitted
Full Proposals and Partial Analysis Results Being Presented (remaining/complete results to be given in Sept. Mtg.)
July 2014 Mtg.
Notes: Jul 12, 2010
Page 9