## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Summary of Merger Status on Samsung-ETRI Merged MAC Proposals]
Date Submitted: [15 July 2014]
Source: [Seung-Hoon Park, Kyungkyu Kim, Anil Agiwal, Youngbin Chang, Hyunseok Ryu, Daegyun Kim and Won-il Roh]1,[Byung-Jae Kwak, Kapseok Chang, Moon-Sik Lee]2, [Junhyuk Kim, June-Koo Kevin Rhee]3, [Seong-Soon Joo, In-Hwan Lee, Hyo-Chan Bang]4
Company [Samsung Electronics]1, [ETRI]2,4, [KAIST]3
Address [416, Maetan-3Dong, Yeongtong-Gu, Suwon-Si, Gyeonggi-Do, 443-742, Korea], [Daejeon, Korea]2,3,4
Voice:[+82-10-9349-9845]1, FAX: [+82-31-279-0813]1, E-Mail:[shannon.park@samsung.com]1,[{bjkwak, kschang, moonsiklee}@etri.re.kr]2, [kim.jh@kaist.ac.kr, rhee.jk@kaist.edu]3 ,[ssjoo@etri.re.kr]4
Re: [.]
Abstract: [Summary of progress on merger status within Samsung-ETRI proposals]
Purpose: [Merger progress]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Summary of Merger Status on Samsung & ETRI MAC Proposals
May, 2014

## Slide 3: Merger Participants
Samsung (Seung-Hoon Park, et. al.)
ETRI (BJ Kwak, et. al.)
ETRI (SS Joo, et. al.)

## Slide 4: Overall Summary
Common design of fully distributed Synchronization and Discovery for any type of PDs and traffics
Low power consumption for Discovery and Peering
Traffic-aware low duty cycle of communication
Flexible design for channel access including contention-based and contention-free channel access
Highly efficient contention-free channel access scheme

## Slide 5: Key Discussion Points
Superframe structure
  Comprises multiple sync intervals
  Group members exchange superframe properties such as period, etc. during peering procedure
Synchronization
  How to make a Rx PD to confirm whether neighboring Tx PDs are synchronized?
  Synchronization accuracy (granularity): frame or symbol boundary
Discovery
  Discovery is based on connection-less (a.k.a. broadcast)
  Identification for discovery is came from higher layer
  Discovery Rx PD should listen all discovery resources.
  Discovery Tx PD may adjust discovery signal transmission periodicity.

## Slide 6: Key Discussion Points
Peering
  Duty cycling with a cycle under synchronization cycle and a cycle per synchronization cycle is established during peering procedure.
Communication
  Control messages for CFP (Request/Response) are transmitted based on contention-access scheme
  Resources for CFP can be utilized as secondary access for other PDs which do not participate CFP negotiation.

## Slide 7: Frame Structure
Synchronization Slot
Discovery Slot
Peering Slot
Communication Slot
  CAP (Contention Access Period)
  CFP (Contention Free Period)

## Slide 8: Synchronization
Synchronization for Scalable Network
  Distributed synchronization
    Master-slave synchronization should be avoided
      PDs between two different synchronized group happen
    It is matched well to flat architecture (no hierarchy)
  Synchronization should be done before peer discovery
    Peer discovery prior to link connection (peering)
    Broadcast-based synchronization mechanism is required

## Slide 9: Synchronization
Synchronization Reference Signal (SRS)
  Transmitted during the synchronization slot
  Contains timing offset (backoff time) information
How to transmit
  Energy sensing prior to transmit
    Robust in the presence of interference from other beacons or other networks (e.g., WLAN)
  Transmitted with random back-off

## Slide 10: Peer Discovery
Design Considerations
  Discovery Information (DI)
    Came from application or middleware
      Plain ID: Application ID (PACbook), or User ID (Bob@PACbook), or etc
      Coded DI: generated by middleware or retrieved from server
    Discovery matching
      PD A is matched by other PDs storing DI representing PD A

## Slide 11: 3. Peer Discovery
What is Peer Discovery?
  A peer represents an application-specific entity, not a device
PAC Module
Middleware
App A
App B
PAC Module
Middleware
App B
App C
API
API
Peer Discovery Information
PD 1
PD 2
Bob@PACbook
Robert@PACbucks
Bob@PACbook
Bob@PACbook  App A
Ken@PACbook  App A
Sniper@Pgame  App C
Bob@PACbook

## Slide 12: Discovery Message
Supported discovery types
  Advertisement, Publish/subscribe, Query/reply
  SSF (Self Spatial Filtering) aka LnL (Look-and-Link)
  Emergency messages
Discovery message content
  Driven from higher layer
  Middleware standards: e.g. UUID (16 bytes)
  Plain texts: e.g. Human readable ID
Discovery Slot
  It is comprised of multiple Discovery Blocks (DBs)

## Slide 13: Peering
The role of Peering
  A procedure to connect to discovered peer
    Triggered by application automatically or by user manually
    No MAC-level triggering
  Link establishment for unicast/multicast link
    Between a TX PD and RX PD(s)
    Exchange of information for setup
      TX/RX ID (MAC address), capability, or etc
    Determine link related parameters
      Link ID, QoS class, link range, duty cycle, or etc
  Messages
    Peering, re-peering, de-peering messages

## Slide 14: Peering
Design Consideration for Peering Slot
  Small radio resource comparing to Discovery Slot
    Peering happens sparsely
  Handling of multiple peering response to peering requests
  Channel access scheme
    Contention-based access (same as CAP access)

## Slide 15: Communication
Communication Slot
  Comprising CAP and CFP
    CAP (Contention Access Period)
    CFP (Contention Free Period)
  CAP for both peered and un-peered data communication
  CFP for only peered data communication

## Slide 16: CAP
Features of CAP
  For both peered and un-peered data communication
  Support of broadcast data transmission within un-peered PDs
  CSMA/CA based on EIED algorithm [4]
  Details in 15-14-0249

## Slide 17: CFP
Features of CFP
  Only accessed by peered PDs
  Signaling reduction using Link ID
    No necessity of sending multiple MAC addresses of both TX PD and RX PD(s)

## Slide 18: CFP
CFP comprises
  Scheduling Request/Response Sub-slots
  Resource Blocks (RBs) (using CSMA/CA in a RB)
※ If scheduling request/response is not decoded,
RBs can be utilized for secondary CAP packets