## Slide 1: Proposed MAC Frame Structure
July, 2014

## Slide 2: Samsung-ETRI
A frame comprises of synchronization slot, discovery slot, peering slot, and communication slot
A frame period is same as synchronization interval
Distributed synchronization

## Slide 3: Discussion
Groupcasting in peering slot (control? or data?)
  Sharing peering slot by control and data
    Difficult in channel access point of view
  Peering can include controls for unicast, multicast, groupcast, and broadcast.
  TBD: which control messages in peering slot
  Point: any PD listens peering slot
  Discovery: resource efficient to send short messages
    MAC address is not delivered in discovery slot
    Discovery message can be compact since not need to send flags.
  Peering: optimized to exchange signals within discovered PDs
    MAC address and more information can be transmitted in peering slot

## Slide 4: Discussion
Peering slot reuse for data
  Indication of usage (from ETRI, BJ)
    If nobody use peering slot, it changes to a part of CAP
    How to handle hidden node problem?
      Multiple level of sensitivity?
  Which kind of data?
    How long is the size of data?
      If peering resource is not sufficient, the size of data should be limited.

## Slide 5: Discussion
Emergency case
  Authentication
  Priority
  Fast & short message delivery
  Is it handled separately from general discovery and/or peering?
    Consider emergency message as one of items
    TBD whether it is transmitted in the same discovery/peering or not

## Slide 6: Discussion
Synchronization
  If PD detects the existing synchronization signal, it refers the timing of the sync-signal,
  Otherwise, it starts to send synchronization signal with the own timing

## Slide 7: Terminology
Slot
  It is confused from a conventional term of slot
  Alternatives?
    Period, (time) duration, (time) region, interval, etc…
  Official IEEE term is recommended.
    For testing IEEE committees

## Slide 8: Discussion
Configuration of Superframe
  Superframe comprises of multiple sync. intervals
  Opt1. implicit: choose one among multiple pre-defined configuration sets
  Opt2. explicit: exchange information for configuration within groups
    TBD: how to exchange information with proper overhead
    TBD: how to solve hidden and exposed node problem or
  Parameters for configuration
    Superframe period
    The period for duty cycling
    Load balancing
    Others
  Recommended harmonization
    Explicit (opt 2) as one option among multiple configuration sets

## Slide 9: Design Philosophy
PAC will try to make a simple design to serve services based on mandatory signaling and protocols.
Complicated signaling and protocol messages will be optional.

## Slide 10: Common channel for common mode
What we need to define is signaling and protocol to support transition from a channel to another.
TBD: Whether it is necessary to define specific common channel or not.

## Slide 11: NICT
I-PD (Initiator PD) gives frame boundary and structure
J-PD (Joiner PD) responses to I-PD
Q:
  how to provide low duty cycling to receive temporary beacon?

## Slide 12: NICT + Samsung-ETRI
Issues
  I-PD provides information to initiate group formation
    I-PD does not provide timing reference any more
  Who sends synchronization signal? Only I-PD?
    PDs can take over the role of I-PD turn-by-turn
  Loading of discovery slot and peering slot (revisit later)
    S-E?: D-slot > P-slot, NICT: D-slot < P-slot

## Slide 13: InterDigital
Common Beacon to provide superframe boundary
  Discovery, peering, emergency, negotiation as well.
Frame X beacon to provide frame X boundary
  Per app group
Q:
  Who sends common beacon? Is it centralized coordinator?

## Slide 14: InterDigital + Samsung-ETRI
No common beacon
Frame X beacon may be integrated in CAP
Each App group can negotiate usage of synchronization intervals

## Slide 15: InterDigital + Samsung-ETRI
Common beacon may be included in a certain sync. interval
  App 0 (common)
  TBD: how to know the timing of App 0 beacon
  Issue: common beacon to coordinate frame X beacon reasonable? Possible problem: when multiple common beacon exist

## Slide 16: InterDigital + Samsung-ETRI
Usage of Frame beacon
  Low duty cycling per app group basis (to allow deep (longer) sleep)
  Fine synchronization
  Switching across multiple app groups
Issues
  Should every app group negotiate for this TDMA formation?
  TBD
    Whether different app group can share the resource in the sync interval.
  Flexible frame structure possible?
    Sync interval is fixed (from TGD).
    How to know the timing of common frame?

## Slide 17: InterDigital + Samsung-ETRI
Synchronization interval
  If is sufficiently short, InterDigital can compromise.
    Small granularity helps app groups in the resources management perspective.
  TBD: How short?
    Ref: LTE (10 msec)
    It can be decided by simulation
  Anti-effect from short sync. Interval?
    More transmissions for sync. Signal

## Slide 18: Possible Motion for Consolidation of Consensus
“Frame structure is fixed as including synchronization interval, time offset and duration of each slot(period).”
“Superframe feature is optional, but it can be revisited if it is proved to show reasonable overhead and to solve geo-locational problems.”

## Slide 19: Possible Motion for Consolidation of Consensus
TBD
  Configuration of Superframe

## Slide 20: Ad Hoc Session PM1 Wed. (7/16)

## Slide 21: Possible Motion for Consolidation of Consensus
Frame: the structure is defined as the following periods in order
  Sync. period, Discovery period, Peering period, Contention Access period, and Contention Free period.
  The Duration of a frame is fixed with a value of TBD.
  The duration of each period is fixed and the values are TBD.

## Slide 22: Possible Motion for Consolidation of Consensus
Superframe: will be considered as an optional feature on the condition that the following are proved
  Creating and maintaining superframe can be performed with reasonable overhead.
  Creating and maintaining superframe over a large area is possible, especially in an environment where the shortest path between two random PDs can be a multi-hop path.
  Not having the knowledge about the superframe structure does not affect a PD’s capability of discovery and peering.
  Having superframe structure provides substantial benefit that out weight the overhead required to create and maintain superframe.
  The first frame within a superframe is dedicated as “common frame” (i.e. App 0) for common mode ( to be discussed later) wherein all the PDs wake up and listen.
and to solve geo-locational problems.