## Slide 1: Proposed MAC Frame Structure
July, 2014

## Slide 2: Samsung-ETRI
A frame comprises of synchronization slot, discovery slot, peering slot, and communication slot
A frame period is same as synchronization interval
Distributed synchronization

## Slide 3: Discussion
Groupcasting in peering slot (control? or data?)
  Sharing peering slot by control and data
    Difficult in channel access point of view
  Peering can include controls for unicast, multicast, groupcast, and broadcast.
  TBD: which control messages in peering slot
  Point: any PD listens peering slot
  Discovery: resource efficient to send short messages
    MAC address is not delivered in discovery slot
    Discovery message can be compact since not need to send flags.
  Peering: optimized to exchange signals within discovered PDs
    MAC address and more information can be transmitted in peering slot

## Slide 4: Discussion
Peering slot reuse for data
  Indication of usage (from ETRI, BJ)
    If nobody use peering slot, it changes to a part of CAP
    How to handle hidden node problem?
      Multiple level of sensitivity?
  Which kind of data?
    How long is the size of data?
      If peering resource is not sufficient, the size of data should be limited.

## Slide 5: Discussion
Emergency case
  Authentication
  Priority
  Fast & short message delivery
  Is it handled separately from general discovery and/or peering?
    Consider emergency message as one of items
    TBD whether it is transmitted in the same discovery/peering or not

## Slide 6: Discussion
Synchronization
  If PD detects the existing synchronization signal, it refers the timing of the sync-signal,
  Otherwise, it starts to send synchronization signal with the own timing

## Slide 7: Terminology
Slot
  It is confused from a conventional term of slot
  Alternatives?
    Period, (time) duration, (time) region, interval, etc…
  Official IEEE term is recommended.
    For testing IEEE committees

## Slide 8: NICT
I-PD (Initiator PD) gives frame boundary and structure
J-PD (Joiner PD) responses to I-PD
Q:
  how to provide low duty cycling to receive temporary beacon?

## Slide 9: NICT + Samsung-ETRI
Issues
  I-PD provides information to initiate group formation
    I-PD does not provide timing reference any more
  Who sends synchronization signal? Only I-PD?
    PDs can take over the role of I-PD turn-by-turn
  Loading of discovery slot and peering slot (revisit later)
    S-E?: D-slot > P-slot, NICT: D-slot < P-slot

## Slide 10: InterDigital
Common Beacon to provide superframe boundary
  Discovery, peering, emergency, negotiation as well.
Frame X beacon to provide frame X boundary
  Per app group
Q:
  Who sends common beacon? Is it centralized coordinator?

## Slide 11: InterDigital + Samsung-ETRI
No common beacon
Frame X beacon may be integrated in CAP
Each App group can negotiate usage of synchronization intervals
Common beacon may be included in a certain sync. interval

## Slide 12: InterDigital + Samsung-ETRI
Usage of Frame beacon
  Low duty cycling per app group basis (to allow deep (longer) sleep)
  Fine synchronization
  Switching across multiple app groups
Issues
  Should every app group negotiate for this TDMA formation?
  TBD
    Whether different app group can share the resource in the sync interval.
  Flexible frame structure possible?
    Sync interval is fixed (from TGD).
    How to know the timing of common frame?