## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Frequency Bands allocated in Europe for Short Range Devices beyond 64 GHz
Date Submitted: 17 July 2014
Source: Thomas Kürner Company TU Braunschweig
Address Schleinitzstr. 22, D-38092 Braunschweig, Germany
Voice:+495313912416, FAX: +495313915192, E-Mail: t.kuerner@tu-bs.de
Re: n/a
Abstract: This presentation provides an overview on european frequency allocations for Short Range Devices (SRD) in the frequency bands 64 GHz – 275 GHz
Purpose: Information of TG3d
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Frequency Bands allocated in Europe for Short Range Devices beyond 64 GHz

## Slide 3: Motivation
In frequency allocation tables the application of so-called Short Range Devices (SRD) are defined
Some of the applications considered in TG3d (close proximity P2P, intra-device communcations) can be classified as an SRD.
This documents provides an overview of spectrum allocated to non-specifc SRDs in the frequency range 64 GHz to 275 GHz in Europe [1].

## Slide 4: Overview of Frequency Bands for SRD
Band /GHz | Bandwidth /GHz | Maximum output power
122-122.25 | 0,25 | 10 dBm EIRP/ 250 MHz and -48 dBm/MHz at 30° elevation [3]
122.25-123 | 0,75 | 100 mW (20 dBm) EIRP [2,3]
244-246 | 2 | 100 mW (20 dBm) EIRP [2,3]

## Slide 5: Conclusion
Totally 3 GHz of spectrum for use as SRD is available beyond 64 GHz.
This spectrum is less than what is availabe in the 57-64 GHz band.
For solutions requiring > 10 GHz spectrum other frequency bands have to be identified, e. g. beyond 275 GHz

## Slide 6: References
[1] THE EUROPEAN TABLE OF FREQUECY ALLOCATIONS AND APLICATIONS IN THE FREQUENCY RANGE 8.3 kHz to 3000 GHz (ECA TABLE) –Approved May 2014, www.erodocdb.dk/docs/doc98/official/pdf/ERCRep025.pdf
[2] Electromagnetic compatibility and Radio spectrum Matters (ERM); Short Range Devices (SRD); Radio equipment to be used in the 40 GHz to 246 GHz frequency range; Part 1: Technical characteristics and test methods; http://www.etsi.org/deliver/etsi_en%5C305500_305599%5C30555001%5C01.02.00_20%5Cen_30555001v010200a.pdf
[3] ERC/REC 70-03 http://www.erodocdb.dk/docs/doc98/official/pdf/rec7003e.pdf