## Slide 1: Proposed MAC Motions
July 17, 2014

## Slide 2: Motion 1: Frame
Frame: the structure is defined as the following periods in order
  Synchronization period, Discovery period, Peering period, Contention Access period, and Contention Free period.
  The duration of a frame is also the synchronization interval which is fixed with a value of TBD.
  The duration of each period is fixed and the values are TBD.

## Slide 3: Motion2: Working Assumptions for a Superframe
Superframe: contains multiple frames which will be considered as an optional feature on the condition that the following are proved
  Creating and maintaining Superframe can be performed with reasonable overhead.
  Creating and maintaining Superframe over a large area is possible especially with multi-hop.
  Not having the knowledge about the Superframe structure does not affect a PD’s capability of discovery and peering.
  Having Superframe structure provides substantial benefit that outweighs the overhead required to create and maintain Superframe.

## Slide 4: Motion 3: Synchronization Procedure
Synchronization Procedure includes the following sub-procedures:
  Initial Synchronization procedure
  Maintaining Synchronization procedure
  Re-Synchronization procedure
A PD starts Initial Synchronization procedure if the PD does not have its own reference timing.
  e.g. when the PD powers on, etc.
After successful Initial Synchronization procedure, a PD makes a transition to Maintaining Synchronization procedure.
A PD may make a transition to Re-synchronization procedure from Maintaining Synchronization procedure according to a triggering condition.
  TBD: a triggering condition

## Slide 5: Motion 4: Initial Synchronization
To acquire a reference timing, a PD scans for the existing synchronization signals during a TBD time.
If it detects the synchronized condition, it derives its own timing from the detected synchronization signal.
  The synchronized condition is determined from a synchronization signal or multiple synchronization signals with the same timing detected during the scanning period.
If it detects multiple synchronization signals with different timing during the scanning period, it performs a synchronization procedure based on the timings derived from the detected synchronization signals.
  The synchronization procedure includes at least adjusting its own timing based on the derived timings.
If it fails to detect any synchronization signal, it starts to send synchronization signal with its own timing.

## Slide 6: Motion 5: Maintaining Synchronization
A PD maintains its own timing reference based on measurement of synchronization signals.
Maintaining Synchronization procedure includes at least fine adjustment of timing reference and triggering of Re-Synchronization procedure.
  If unsynchronized condition for fine adjustment is met, it adjusts its own timing based on the detected synchronization signal during Synchronization period.
  If unsynchronized condition for Re-Synchronization is met, it makes a transition to Re-Synchronization procedure.
  TBD: details of unsynchronized conditions

## Slide 7: Motion6: PHY Discovery Signal
Discovery signal is transmitted via UWB, OFDM, or DFT-S OFDM .
DFT-S OFDM or OFDM
  Discovery information bits are mapped onto one or more discovery resource blocks (DRBs). The preambles are included (not shown).
  A Discovery Resource Block comprises one or multiple of time resources or time and frequency resources.
UWB (TBD)
Fairness
  PDs

## Slide 8: Motion7: Information for Discovery
For the purpose of discovery of PDs, the discovery information represents one or more of the following IDs
  Device ID, Device Group ID, Application type ID, Application-specific ID, Application-specific user ID, Application-specific group ID.
The discovery information is not limited to IDs mentioned above.

## Slide 9: Motion8: Discovery Type
The Discovery type is defined by a higher layer.
The MAC messages should support at least the following discovery types:
Advertisement: In Advertisement type discovery, a PD broadcasts its own discovery information and does not expect responses.
Publish/Subscribe: In Publish/Subscribe type discovery, a PD broadcasts its own discovery information and expects responses from PDs that have discovered the broadcast message(s).
Query/Reply: In Query/Reply type discovery, a PD broadcasts the discovery information of the PD or PDs being queried and expects a response or responses from the PD or PDs, accordingly.

## Slide 10: Motion9: MAC Discovery Messages
MAC shall support at least the following discovery messages:
Discovery Request message
Discovery Response message