## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Proposed Resolution regarding TMCTP
Date Submitted: 12 August, 2014
Source: Jaehwan Kim, Young-Ae Jeon, Sangsung Choi (ETRI), and Soo-Young Chang (SYCA)
Company: ETRI, and SYCA,
Address:
Voice: +82-42-860-1572, E-Mail: kimj@etri.re.kr
Re:
Abstract: Proposed resolution to resolve some issues regarding TMCTP raised by Pat Kinney
Purpose: To suggest resolution for the issues regarding TMCTP
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Introduction
Some issues raised by Pat Kinney through emailing on July 29, 2014
  “ ……. In resolving comments, I have discovered that the draft does not invoke TMCTP as: mandatory, mandatory if TVWS is present, optional, optional if TVWS is present. While 4.11.1.3 states "TVWS allows the optional use of a superframe structure in a TMCTP" the first mention of TMCTP in a normative clause is 5.2 page 31. Even 5.14 Starting and maintaining TMCTPs doesn't have any mechanism for turning it on or off, or what a behaviors a device needs to have to participate. There is no way of identifying devices that are capable of operating in the TMCTP mode, e.g. SPC, TMCTP-parent coordinator, TMCTP-child coordinator, so the user cannot adequately specify a TMCTP device, in short it cannot work in the real world. For TMCTP to stay in the draft, it will have to be modified so that the user will know what 15.4 devices to buy and how to enable or disable it. …..”
To resolve these issues, this document was prepared and resolutions are proposed.

## Slide 3: Proposed Resolution
Proposed Resolution
  Add the following row in Table 8 of 6.3.1.2 (p128):
  Add the following sentence before the first sentence of 6.5.3.29 (p187).
Attribute request ID | PIB attribute | IE type | IEs to include
7 | macTMCTPenabled | MLME Payload | TMCTP Specification (6.5.3.29)
    The TMCTP Specification IE shall be included in enhanced beacons that are sent every beacon interval in a TMCTP-enabled PAN.

## Slide 4: Proposed Resolution (cont’d)
Proposed Resolution
  Change the third sentence of the first paragraph of 6.6.1(p190) as indicted:
  Add the following row in Table 136 of 7.4.2.1(p316):
Attribute | Type | Range | Description | Default
macTMCTPcapable | Boolean | TRUE, FALSE | If TRUE, the device is capable of functionality specific to TMCTP | -
macTMCTPenabled | Boolean | TRUE, FALSE | If TRUE, the device is using functionality specific to TMCTP | -
An FFD supporting one of the optional functional groups listed in Table 136 shall support the associated MAC commands in the range 0x0d−0x22 as identified by the associated functional group prefix, e.g., “DSME-”.

## Slide 5: Proposed Resolution (cont’d)
Proposed Resolution
  Insert the following sentence before the first sentence of the first paragraph of 4.11.1.3 as indicted:
The TMCTP-enabled (i.e., macTMCTPenabled is TRUE) PANs use the TMCTP superframe extension structure.

## Slide 6: Proposed Resolution (cont’d)
Proposed Resolution
  Add the following rows in Table D.7 of D.7.3.1 (p652):
Item number | Item description | Reference | Status | Support |  | 
 |  |  |  | N/A | Yes | No
MLF31 | TMCTP capability |  |  |  |  | 
MLF31.1 | TMCTP superframe extension structure | 4.11.1.3, 5.2.2.3, 5.2.9 | MLF31:M |  |  | 
MLF31.2 | TMCTP formation | 5.14 | MLF31:M |  |  |