## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Response to the call for final proposal to TG10]
Date Submitted: [14 September, 2014]
Source: * [Verotiana Rabarijaona, Fumihide Kojima], †[Hiroshi Harada]
Company *[NICT], †[Kyoto University]
Address *[3-4, Hikarino-oka, Yokosuka, 239-0847 Japan], †[36-1 Yoshida-Honmachi, Sakyo-ku, Kyoto 606-8501 Japan]
Voice:[+81-46-847-5075], FAX: [+81-46-847-5089], E-Mail:[rverotiana@nict.go.jp]
Re: [Call for Final Proposals.]
Abstract: [This contribution presents a full proposal for the TG10.]
Purpose: [Final proposal to TG10.]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Hierarchical Mesh Tree Routing
Verotiana Rabarijaona, Fumihide Kojima (NICT), Hiroshi Harada (Kyoto University)

## Slide 3: Outline
Review of the proposal
Proposed IEs
Requirements and simulation scenario
Simulation results
Data aggregation evaluation

## Slide 4: HMT construction, maintenance and update
The neighbor table is built and maintained through periodic EB broadcasts
A node’s depth and the neighbor table is updated according to the changes in the network reflected by the presence/absence of EBs
R
A
B
C
D
E
I
J
L
G
H
K
F
M
N
Depth
0
1
2
3
Parent-child link
Brotherhood link
O
R
A
B
C
D
E
I
J
L
G
H
K
F
M
Depth
0
1
2
3
Parent-child link
Brotherhood link
N

## Slide 5: HMT Routing - Upstream(1)
Based on a link quality metric (BER, success rate, latency, SINR …).
The metric(s) to be used is determined by the root of the tree and spread through EBs
Routing through parents and/or brothers with priority given to the parents through a Link Quality Threshold (LQT) w.r.t the chosen metric:
  If the metric offered by the best parent does not satisfy the LQT, the packet is routed through the best brother.
  If the metric offered by the best brother does not satisfy the LQT, the packet is routed through the device with the best metric between the best parent and the best brother.
The LQT may be set globally by the root, or locally and dynamically by a device to adapt to the local channel conditions
A node holds the list of TAs and RAs of a packet with a given (SN, SA, DA) tuple. In order to avoid loops, a node shall select a next hop that is not in that list. The list shall be erased after a TBD time

## Slide 6: HMT Routing - Upstream(2)
Example of MR routing
R
A
B
C
D
E
I
J
L
G
H
K
F
M
N
Depth
0
1
2
3
3.03
3.89
5.51
6.34
6.8
11.12
7.15
1.6
3.12
4.72
8.34
9.4
6.28
1.21
10.67
3.5
7.65
0.61
0.21
4.05
3.58
2.66
4.09
1.22
LQT = 4
No LQT
10.71
5.24
8.67
5.81

## Slide 7: HMT Routing - Downstream (1)
When a device receives/overhears(if allowed) a packet to forward upstream (i.e. to the root), it includes the address of the source of the packet in the “List of reachable destinations” of the neighbor from which it received the packet (i.e. previous hop.) This list can be classified into 16-bit addresses and 64-bit addresses.
This neighbor table allows memory saving compared to a regular routing table
Neighbor ID | Neighbor Depth | Metric 1 | … | Metric n | List of reachable destinations
Destination | Next hop | Metric
A | A | 7.65
M | A | 7.65
N | A | 7.65
I | A | 7.65
L | A | 7.65
J | A | 7.65
F | F | 0.61
J | F | 0.61
K | F | 0.61
H | F | 0.61
G | F | 0.61
Neighbor ID | Depth | Metric | List of reachable destinations |  |  |  | 
A | 1 | 7.65 | M | N | I | L | J
F | 1 | 0.61 | J | K | H | G | 
Ex: R’s table, assuming 16-bit addresses, 1-byte depth, 4-byte metric
88 bytes
32 bytes
Filled based on received EBs
Filled with the SA of received data frames

## Slide 8: HMT Routing – Downstream (2)
If a device does not have a data packet to transmit for a prolonged period of time, it sends a MP frame with a Destination Announcement IE (Dest-A IE) upstream
When a device needs to forward a packet downstream, it looks up into its neighbor table and finds the neighbor with the best link quality metric through which the destination is reachable, with priority given to the child neighbors through a LQT
If the devices of the network (besides the root) do not have enough memory to maintain the list of reachable destinations (non-storing mode), source routing is used. Each intermediate device on the way upstream appends its own address to the Dest-A IE. The list of intermediate hops is included in a packet to be sent downstream. Each intermediate device removes its address from the list before forwarding the packet.

## Slide 9: HMT Routing - Downstream (2)
Example of R  J routing
R | Neighbor ID | Depth | LQ | List of reachable destinations |  |  |  | 
 | A | 1 | 7.65 | M | N | I | L | J
 | F | 1 | 0.61 | J | K | H | G | 
 | … | … | … | … | … | … | … | …
R
A
B
C
D
E
I
J
L
G
H
K
F
M
N
Depth
0
1
2
3
3.03
3.89
5.51
6.34
6.8
11.12
7.15
1.6
3.12
4.72
8.34
9.4
6.28
1.21
10.67
3.5
7.65
0.61
0.21
4.05
3.58
2.66
4.09
1.22
10.71
5.24
8.67
5.81
A | Neighbor ID | Depth | LQ | List of reachable destinations |  |  |  | 
 | R | 0 | 7.65 |  |  |  |  | 
 | F | 1 | 5.24 | J | K | H | G | 
 | J | 2 | 3.12 | N |  |  |  | 
 | … | … | … | … | … | … | … | …
F | Neighbor ID | Depth | LQ | List of reachable destinations |  |  |  | 
 | R | 0 | 0.61 |  |  |  |  | 
 | A | 1 | 5.24 | L | M | J |  | 
 | J | 2 | 4.72 | N |  |  |  | 
 | … | … | … | … | … | … | … | …
Destination
Best link quality
Selected next hop

## Slide 10: HMT Routing – P2P
When a device D1 has a packet to transmit to another device D2, it looks into its neighbor table if there is a route to D2.
  If there is a route, the packet is forwarded to the neighbor through which D2 is reachable
  If there is no route, the packet is forwarded upstream
  Example of M G routing
R
A
B
C
D
E
I
J
L
G
H
K
F
M
N
Depth
0
1
2
3
3.03
3.89
5.51
6.34
6.8
11.12
7.15
1.6
5.81
3.12
4.72
8.34
9.4
5.24
1.21
10.67
3.5
7.65
0.61
0.21
4.05
3.58
2.66
4.09
1.22
LQT = 4
No LQT
10.71
8.67
6.28

## Slide 11: HMT Routing – Multicast(1)
If a node is subscribed to a multicast group, it informs the network with the Dest-A IE including a Multicast subscription field, containing the multicast address.
When a device receives a Dest-A IE with a Multicast subscription field, the multicast address is added to the list of reachable destinations
A device uses the same algorithm as for P2P routing with the multicast address as the destination address and as the next hop address, i.e. a device forwards a multicast packet only if the multicast address is reachable through one of its neighbors. This avoids flooding the network.
A device forwards a packet only once, except if the packet requires an ACK and ACK was not received from each intended next hop

## Slide 12: HMT Routing – Multicast(2)
Example of multicast routing E 
R
A
B
C
D
E
I
J
L
G
H
K
F
M
N
Depth
0
1
2
3
8.67
3.03
10.71
3.89
5.51
6.34
6.8
11.12
7.15
1.6
5.81
3.12
4.72
8.34
6.28
5.24
1.21
10.67
3.5
7.65
0.61
0.21
4.05
3.58
2.66
4.09
1.22
LQT = 4
Member of the multicast group
9.4

## Slide 13: HMT Routing - Broadcast
If the root of the tree is the source of a broadcast data frame, a device shall forward the packet only if it has children neighbors.
If a device other than the root of the tree is the source of a broadcast data frame, the frame shall be sent to the root first and broadcast downstream as in a.

## Slide 14: High reliability option
If the high reliability (HR) option is on, the AR field must be set to 1. If an acknowledgment is not received after a packet transmission, the packet is forwarded through another neighbor
In particular, the HR option can be used when no LQT is set, i.e. the next hop must be a parent but if the transmission fails, the packet is rerouted through the best of the parents/brothers
R
A
B
C
D
E
I
J
L
G
H
K
F
M
N
Depth
0
1
2
3
8.67
3.03
3.89
5.51
6.34
6.8
11.12
7.15
1.6
5.81
3.12
4.72
8.34
9.4
6.28
5.24
1.21
10.67
3.5
0.61
0.21
4.05
3.58
0.66
1.22
10.71
No LQT
4.09
7.65

## Slide 15: Data aggregation

## Slide 16: HMT Construction IE
Bit: 0 - 6 | 7 - 14 | 15 | Octets: Variable
Length | Element ID | Type = 0 (Header) | IE content
Octets: 1 | 0/2/8 | 0/1 | Bits: 0 | 1 | 2-5 | 6-7 | Octets: variable | … | Octets: 0-variable
Service/ Gateway ID1 | Tree Root ID | Depth | High reliability | Data aggregation 0: not allowed 1: allowed | Number N of metrics | Reserved | Link Quality Metric 12 | … | Link Quality Metric N
Used in EBs or command frames
Bits: 0-3 | 4-7 | 0/Variable | 0/Variable
Link quality metric ID | Priority | Threshold | Value
X
Number of services/
gateway provided/
subscribed/connected to
1 In a Enhanced Beacon Request, if the device knows the service or gateway it is trying to connect to, only the Service/Gateway ID is present. Otherwise the IE content is empty
2 The link quality metrics and the related parameters are up to the implementer and are set in the PIB

## Slide 17: L2R Routing IE
Bit: 0 - 6 | 7 - 14 | 15 | Octets: Variable
Length | Element ID | Type = 0 (Header) | IE content
Slide 17
Octets: 1 | 2/8 | 1 | Variable | Bits: 0 | 1-2 | 3-7
Service/ Gateway ID | Tree Root ID | Depth | Addressing fields | Data aggregation 0: must not be buffered and aggregated, must be forwarded immediately 1: may be buffered and aggregated | Flow 00: Up 01: Down 10: broadcast up1 11: broadcast down | Reserved
Octets: 2/8 2 | 2/8
Final Destination address (d) | Original Source address (d)
Used in data frames
1 Used for a broadcast data frame originated by a device other that the root of the tree. The data frame is forwarded to the root first then broadcast. The flow is switched to 11 (broadcast down) when the data frame reaches the root
2The addressing mode shall be the same as those used in the MHR

## Slide 18: Data aggregation IE
Bit: 0-6 | 7-14 | 15 | Octets : variable
Length | Element ID | Type = 0 (Header) | IE content
Bits: 0-3 | 6-7 | Octets: 1 | … | 1
Number N of aggregated packets | Reserved | Size of the aggregated packet 1 in octets | … | Size of the aggregated packet N in octets
Used in data frames

## Slide 19: Destination Announcement IE
Used in a MP frame sent to the root of the tree.
Bit: 0-10 | 11-14 | 15 | Octets : variable
Length | Element ID | Type = 0 (Header) | IE content
Octets: Variable | 0/2/8 | … | 0/2/8
Multicast subscription | Intermediate hop address 11 | … | Intermediate hop address N
Bits: 0-5 | 6-7 | Octets: 0/2/8 | … | 0/2/8
Number M of multicast group2 | Addressing mode | Multicast address 1 | … | Multicast address M
1 Intermediate hop addresses are used for source routing in a non storing mode network, otherwise, they are not appended at each hop.
2 If the node does not belong to any multicast group M = 0

## Slide 20: Topology construction and upward routes
using EBR and EB exchange including the HMT construction IE
  HMT IE size in EBR: 2 octets
  HMT IE size in EB:
    at least 8 octets or 14 octets depending on the addressing mode, when using 16-bit addresses, with one metric without threshold or value
In the simulation:
  One EB for each device with a 12 octets HMT IE using 16-bit addresses, with the SINR metric and a 4-octet threshold field sent in EBs starting from the root
  Initialization time, including the PAN construction (association procedure)
Data rate | 11 x 11 | 33 x 33 | 100 x 100
100 kbps | 24.2102615 | 44.2342633 | 106.9370197
250 kbps | 10.8344032 | 20.5834262 | 38.2287195

## Slide 21: Routing overhead and downward routes
Routing
Use of L2R routing IE in the header of each data frame
  11 octets or 27 octets depending on the addressing mode
  using source routing: additional N x 2 or 8 octets for N intermediate hops
  using data aggregation: additional 3 + M octets for M aggregated packets
  The content in the L2R routing IE is used to build downward routes
Downward route construction (when needed, source routing or no data frame)
Use of the Destination Announcement IE
  3 octets
  additional N x 2 or 8 octets for N intermediate hops
  additional M x 2 or 8 octets for M multicast subscription addresses
Notes: Should we use the DA IE with the Routing IE or include the SA in the DA IE

## Slide 22: Route update and rerouting
Recovery as a result of outage: local repair
  If the device still has neighbor(s) in the neighbor table, find a parent (neighbor with the lowest depth), update own depth and send a EB with updated depth
  Else
    If the device are still connected to the PAN: passive or active scan for EBR with a HMT construction IE
    else, re-association to the PAN, then passive or active scan of EBs including a HMT construction IE
    Re-Discovery as a result of outage subsiding: local repair
  Re-association to the PAN, then passive or active scan of EBs including a HMT construction IE

## Slide 23: Simulation settings
Non beacon enabled 802.15.4-2011 MAC
  In a beacon enabled network, a device must synchronize with the superframe of the next hop
1 EB/30 min
1 DA IE /30 min for scenarios other than upstream and broadcast
Link quality metric: SINR
Link failure rate and SINR mapping
LFR | SINR
10-6 | 23
10-5 | 19
10-4 | 12
10-3 | 10
10-2 | 6
10-1 | 5

## Slide 24: Simulation results – Upstream (1/2)
Performance criteria | 11 x 11 |  | 33 x 33 |  | 100 x 100 | 
 | No SINR threshold | SINRT = 9 | No SINR threshold | SINRT = 9 | No SINR threshold | SINRT = 9
E2E successful transmission ratio (%) | 98.174 | 99.809 | 85.537 | 99.416 | 59.653 | 97.244
Number of hops |  |  |  |  |  | 
Max Average | 5 1.976 | 7 2.813 | 11 5.173 | 19 8.832 | 28 14.211 | 54 25.899
E2E transmission delay (s) |  |  |  |  |  | 
Min Max 99.99th percentile Average | 0.0163 0.1216 0.0813 0.0372 | 0.0163 0.1414 0.1406 0.0549 | 0.0163 0.2251 0.2155 0.0992 | 0.0163 0.3920 0.3569 0.1692 | 0.0163 0.7671 0.5434 0.2709 | 0.0163 1.5535 1.0314 0.5091

## Slide 25: Simulation results – Upstream (2/2)
Performance criteria | 11 x 11 |  | 33 x 33 |  | 100 x 100 | 
 | No SINR threshold | SINRT = 9 | No SINR threshold | SINRT = 9 | No SINR threshold | SINRT = 9
Battery consumption in 24h in mA (Expected lifetime) |  |  |  |  |  | 
Min | 1.945 (2y 298d) | 1.999 (2y 270d) | 1.979 (2y 280d) | 2.007 (2y 266d) | 2.079 (2y 232d) | 2.148 (2y 200d)
Max | 6.602 (302d) | 10.953 (182d) | 51.164 (39d) | 98.827 (20D 5H) | 341.706 (5D 20H) | 1335.155 (1D 12H)
Average | 4.173 (1y 114d) | 5.619 (355d) | 9.938 (201d) | 16.443 (121d) | 22.184 (90d) | 47.122 (42d)
PAN coordinator | 8.296 (241d) | 12.737 (157d) | 58.066 (34d) | 96.835 (20D 15H) | 351.113 (5D 16H) | 1033.165 (1D 22H)

## Slide 26: Simulation results – Downstream (1/2)
Performance criteria | 11 x 11 |  | 33 x 33 |  | 100 x 100 | 
 | No SINR threshold | SINRT = 9 | No SINR threshold | SINRT = 9 | No SINR threshold | SINRT = 9
E2E successful transmission ratio (%) | 96.8476 | 99.9612 | 86.3451 | 99.4098 | 60.3034 | 96.2336
Number of hops |  |  |  |  |  | 
Max Average | 5 2.0597 | 7 2.9 | 11 5.2923 | 19 8.4816 | 28 14.716 | 54 25.6974
E2E transmission delay (s) |  |  |  |  |  | 
Min Max 99.99th percentile Average | 0.0163 0.0837 0.7968 0.0412 | 0.0163 0.139 0.0551 0.1302 | 0.0163 0.2163 0.2064 0.1002 | 0.0163 0.3514 0.341 0.1623 | 0.0163 0.5522 0.2745 0.5414 | 0.0163 0.988 0.9536 0.516

## Slide 27: Simulation results – Downstream (2/2)
Performance criteria | 11 x 11 |  | 33 x 33 |  | 100 x 100 | 
 | No SINR threshold | SINRT = 9 | No SINR threshold | SINRT = 9 | No SINR threshold | SINRT = 9
Battery consumption in 24h in mA (Expected lifetime) |  |  |  |  |  | 
Min | 1.287 (4y 93d) | 1.309 (4y 68d) | 1.339 (4y 33d) | 1.345 (4y 26d) | 1.432 (3y 301d) | 1.436 (3y 296d)
Max | 3.547 (1y 198d) | 4.08 (1y 125d) | 17.165 (116d) | 26.439 (75d) | 131.959 (15D 3H) | 316.061 (6D 7H)
Average | 2.09 (2y 226d) | 2.218 (2y 171d) | 3.213 (1y 257d) | 4.419 (1y 87d) | 5.53 (361d) | 10.679 (187d)
PAN coordinator | 4.636 (1y 66d) | 5.361 (1y 8d) | 27.897 (71d) | 35.072 (57d) | 206.919 (9D 15H) | 329.145 (6D 1H)

## Slide 28: Simulation results – Multicast (1/2)
Performance criteria | 11 x 11 |  | 33 x 33 |  | 100 x 100 | 
 | No SINR threshold | SINRT = 9 | No SINR threshold | SINRT = 9 | No SINR threshold | SINRT = 9
E2E successful transmission ratio (%) | 100 | 100 | 100 | 100 | 100 | 100
Number of hops |  |  |  |  |  | 
Max Average | 5 3.1852 | 5 3.2781 | 15 11.4861 | 15 11.7824 | 43 35.0623 | 43 36.4101
E2E transmission delay (s) |  |  |  |  |  | 
Min Max 99.99th percentile Average | 0.01305 0.0773 0.032406 0.0562 | 0.0334 0.2037 0.1373 0.0705 | 0.1673 0.33104 0.2873 0.2247 | 0.172 0.3235 0.2848 0.2299 | 0.2379 0.3551 0.3378 0.2865 | 0.2355 0.3791 0.2945 0.3721

## Slide 29: Simulation results – Multicast (2/2)
Performance criteria | 11 x 11 |  | 33 x 33 |  | 100 x 100 | 
 | No SINR threshold | SINRT = 9 | No SINR threshold | SINRT = 9 | No SINR threshold | SINRT = 9
Battery consumption in 24h in mA (Expected lifetime) |  |  |  |  |  | 
Min | 1.265 (4y 121d) | 1.27 (4y 114d) | 1.291 (4y 88d) | 1.333 (4y 40d) | 1.039 (5y 99d) | 1.046 (5y 86d)
Max | 2.551 (2y 54d) | 2.843 (1y 338d) | 7.045 (238d) | 11.078 (180d) | 21.125 (94d) | 42.568 (46D 23H)
Average | 1.909 (2y 317d) | 2.042 (2y 249d) | 2.59 (2y 42d) | 3.263 (247d) | 2.081 (2y 231d) | 3.034 (1y 294d)
PAN coordinator | 2.629 (2y 30d) | 3.002 (1y 301d) | 7.728 (258d) | 13.212 (151d) | 15.84 (126d) | 43.22 (46D 6H)

## Slide 30: Simulation results – Broadcast (1/2)
Performance criteria | 11 x 11 | 33 x 33 | 100 x 100
 | No SINR threshold/ SINRT = 9 | No SINR threshold/ SINRT = 9 | No SINR threshold/ SINRT = 9
E2E successful transmission ratio (%) | 99.956 | 99.932 | 99.925
Number of hops |  |  | 
Max Average | 9 2.6579 | 17 7.7944 | 44 22.2004
E2E transmission delay (s) |  |  | 
Min Max 99.99th percentile Average | 0.0163 0.1656 0.1641 0.0544 | 0.0163 0.4168 0.4042 0.1567 | 0.0163 0.8787 0.8483 0.4164

## Slide 31: Simulation results – Broadcast (2/2)
Performance criteria | 11 x 11 | 33 x 33 | 100 x 100
 | No SINR threshold/ SINRT = 9 | No SINR threshold/ SINRT = 9 | No SINR threshold/ SINRT = 9
Battery consumption in 24h in mA (Expected lifetime) |  |  | 
Min | 1.305 (4y 71d) | 1.326 (4y 47d) | 1.423 (3y 310d)
Max | 2.395 (2y 104d) | 6.85 (291d) | 37.824 (52.877)
Average | 1.865 (2y 342d) | 2.592 (2y 41d) | 4.018 (1y 132d)
PAN coordinator | 2.524 (2y 62d) | 7.641 (261d) | 38.501 (51d)

## Slide 32: Simulation results – P2P Unicast (1/2)
Performance criteria | 11 x 11 |  | 33 x 33 |  | 100 x 100 | 
 | No SINR threshold | SINRT = 9 | No SINR threshold | SINRT = 9 | No SINR threshold | SINRT = 9
E2E successful transmission ratio (%) | 97.6907 | 99.23 | 87.398 | 98.295 | 31.0612 | 92.0217
Number of hops |  |  |  |  |  | 
Max Average | 6 | 9 | 18 | 32 | 55 | 93
E2E transmission delay (s) |  |  |  |  |  | 
Min Max 99.99th percentile Average | 0.0705 0.0808 0.0804 0.0757 | 0.0944 0.1072 0.1069 0.1009 | 0.2285 0.2512 0.2506 0.2396 | 0.39 0.4159 0.4153 0.4035 | 0.7060 0.7131 0.7116 0.7122 | 1.1335 1.2109 1.2071 1.1736

## Slide 33: Simulation results – P2P Unicast (2/2)
Performance criteria | 11 x 11 |  | 33 x 33 |  | 100 x 100 | 
 | No SINR threshold | SINRT = 9 | No SINR threshold | SINRT = 9 | No SINR threshold | SINRT = 9
Battery consumption in 24h in mA (Expected lifetime) |  |  |  |  |  | 
Min | 0.931 (5y 322d) | 0.933 (5y 316d) | 0.933 (5y 318d) | 0.94 (5y 301d) | 1.001 (5y 171d) | 1.001 (5y 172d)
Max | 6.654 (300d) | 7.974 (250d) | 8.229 (243d) | 11.51 (173d) | 22.867 (87d) | 49.982 (40d)
Average | 2.524 (2y 62d) | 3.102 (1y 279d) | 1.817 (3y 5d) | 2.21 (2y 66d) | 2.049 (2y 276d) | 3.11 (1y 276d)
PAN coordinator | 6.712 (297d) | 6.799 (294) | 8.057 (248d) | 8.72 (229d) | 18.009 (111d) | 44.99 (44d)

## Slide 34: Simulation results – MP2P Unicast
Performance criteria | 11 x 11 |  | 33 x 33 |  | 100 x 100 | 
 | No SINR threshold | SINRT = 9 | No SINR threshold | SINRT = 9 | No SINR threshold | SINRT = 9
E2E successful transmission ratio(%) | 94.289 | 99.538 | 79.651 | 98.591 | 30.1543 | 92.0061
Number of hops |  |  |  |  |  | 
Max Average | 6 5.812 | 9 8.1998 | 18 17.3198 | 32 29.7991 | 55 53.0364 | 93 87.6034
E2E transmission delay (s) |  |  |  |  |  | 
Min Max 99.99th percentile Average | 0.0584 0.0819 0.0811 0.0733 | 0.082 0.1076 0.1073 0.0983 | 0.1912 0.2359 0.2356 0.2122 | 0.3287 0.4038 0.4035 0.3631 | 0.5842 0.7309 0.7199 0.6432 | 0.9554 1.1824 1.1762 1.0652

## Slide 35: Simulation results – MP2P Unicast
Performance criteria | 11 x 11 |  | 33 x 33 |  | 100 x 100 | 
 | No SINR threshold | SINRT = 9 | No SINR threshold | SINRT = 9 | No SINR threshold | SINRT = 9
Battery consumption in 24 hours in mA (Expected lifetime) |  |  |  |  |  | 
Min | 0.919 (5y 351d) | 0.927 (5y 322d) | 0.916 (5y 356d) | 0.92 (5y 347d) | 1.0015 (5y 171d) | 1.0013 (5y 172d)
Max | 34.608 (57d) | 27.573 (72d) | 46.367 (43d) | 77.104 (25d) | 91.817 (21d) | 180.363 (11d)
Average | 8.078 (247d) | 11.093 (180d) | 5.624 (355d) | 10.094 (198d) | 4.581 (1y 71d) | 9.235 (216d)
PAN Coordinator | 28.583 (69d) | 27.309 (73d) | 46.874 (42d) | 54.171 (36d) | 86.131 (23d) | 144.336 (13d)
Notes: There is a high probability that a device is very often used as a next hop  very high power conscumption

## Slide 36: Simulation results – P2P Multicast (1/2)
Performance criteria | 11 x 11 |  | 33 x 33 |  | 100 x 100 | 
 | No SINR threshold | SINRT = 9 | No SINR threshold | SINRT = 9 | No SINR threshold | SINRT = 9
E2E successful transmission ratio (%) | 97.257 | 97.887 | 91.697 | 98.517 | 48.877 | 96.433
Number of hops |  |  |  |  |  | 
Max Average | 11 6.776 | 15 10.647 | 28 20.647 | 32 34.7039 | 73 62.436 | 97 90.392
E2E transmission delay (s) |  |  |  |  |  | 
Min Max 99.99th percentile Average | 0.0578 0.1695 0.1559 0.0845 | 0.0699 0.1664 0.1645 0.0699 | 0.1924 0.3846 0.3793 0.2674 | 0.2869 0.4681 0.4579 0.3577 | 0.5018 1.0027 0.8088 0.989 | 0.8979 1.3645 1.3329 1.1242
Notes: 1089 devices: One packet every 30min / device  one packet in the network every 1.65s  collisions on the duty period
10000 devices: => one packet every every 0.18s

## Slide 37: Simulation results – P2P Multicast (2/2)
Performance criteria | 11 x 11 |  | 33 x 33 |  | 100 x 100 | 
 | No SINR threshold | SINRT = 9 | No SINR threshold | SINRT = 9 | No SINR threshold | SINRT = 9
Battery consumption in 24 hours in mA (Expected lifetime) |  |  |  |  |  | 
Min | 0.919 (5y 351d) | 0.931 (5y 323d) | 0.917 (5y 356d) | 0.921 (5y 347d) | 0.998 (5y 178d) | 0.999 (5y 176d)
Max | 9.623 (207d) | 9.66 (207d) | 10.055 (198d) | 11.315 (176d) | 40.206 (49d) | 41.976 (47d)
Average | 4.448 (1y 84d) | 4.821 (1y 49d) | 3.068 (1y 286d) | 3.663 (1y 181d) | 2.094 (2y 225d) | 2.2189 (2y 171d)
PAN Coordinator | 7.38 (270d) | 7.99 (250d) | 8.446 (236d) | 9.597 (208d) | 34.192 (58d) | 33.783 (59d)
Notes: Multicast spends less energy than MP2P since the forwarding is more uniform on the downstream. There isn’t a particular device that is solicited more than the others.
Besides there are less packets generated in the P2P MC compared to the MP2P.
On the other hand the average in P2P MC compared to MP2P. In MP2P, the transmission is narrowed to the beam of the devices on the way. In P2P MC, transmission is propagated as far as 3 devices away on the grid from the outer edge of the path

## Slide 38: Simulation results – P2P Broadcast (1/2)
Performance criteria | 11 x 11 |  | 33 x 33 |  | 100 x 100 | 
 | No SINR threshold | SINRT = 9 | No SINR threshold | SINRT = 9 | No SINR threshold | SINRT = 9
E2E successful transmission ratio (%) | 98.507 | 99.695 | 95.459 | 98.517 | 48.877 | 96.433
Number of hops |  |  |  |  |  | 
Max Average | 13 5.624 | 17 9.612 | 30 16.869 | 32 34.7039 | 73 62.436 | 97 90.392
E2E transmission delay (s) |  |  |  |  |  | 
Min Max 99.99th percentile Average | 0.0046 0.1853 0.1705 0.0755 | 0.0052 0.1993 0.184 0.0883 | 0.1145 0.2673 0.2562 0.1824 | 0.1954 0.4599 0.4463 0.3131 | 0.3652 0.7132 0.7103 0.5626 | 0.5402 1.2717 1.2338 0.9375
Notes: 1089 devices: One packet every 30min / device  one packet in the network every 1.65s  collisions on the duty period
10000 devices: => one packet every every 0.18s

## Slide 39: Simulation results – P2P Broadcast (2/2)
Performance criteria | 11 x 11 |  | 33 x 33 |  | 100 x 100 | 
 | No SINR threshold | SINRT = 9 | No SINR threshold | SINRT = 9 | No SINR threshold | SINRT = 9
Battery consumption in 24 hours in mA (Expected lifetime) |  |  |  |  |  | 
Min | 7.717 (259d) | 7.871 (254d) | 7.879 (253d) | 7.941 (251d) | 8.285 (241d) | 8.467 (236d)
Max | 15.135 (132d) | 16.51 (121d) | 43.289 (46d) | 47.233 (42d) | 239.03 (8d 8h) | 260.813 (7d 16h)
Average | 9.863 (202d) | 10.288 (194d) | 13.708 (145d) | 14.299 (139d) | 21.249 (94h) | 22.166 (90d)
PAN Coordinator | 9.279 (215d) | 9.518 (210d) | 28.089 (71d) | 28.813 (69d) | 155.104 (12d 21h) | 159.102 (12d)
Notes: Multicast spends less energy than MP2P since the forwarding is more uniform on the downstream. There isn’t a particular device that is solicited more than the others.
Besides there are less packets generated in the P2P MC compared to the MP2P.
On the other hand the average in P2P MC compared to MP2P. In MP2P, the transmission is narrowed to the beam of the devices on the way. In P2P MC, transmission is propagated as far as 3 devices away on the grid from the outer edge of the path

## Slide 40: Duty Cycling (DC) Support
Duty cycling starts after the initialization of the HMT
Duty cycle: 1%
  Duty period: 5s (A device wakes up every 5 seconds)
  Duty duration: 50ms (A device remains awake for 50ms and then goes to sleep)
A device must synchronize with the duty period of the next hop before transmitting the data and wait for the next duty period if a transmission cannot be completed before the end of the duty period
All the devices in the network are duty cycling in the simulation

## Slide 41: Simulation results – DC Upstream (1/2)
Performance criteria | 11 x 11 |  | 33 x 33 |  | 100 x 100 | 
 | No SINR threshold | SINRT = 9 | No SINR threshold | SINRT = 9 | No SINR threshold | SINRT = 9
E2E successful transmission ratio (%) | 98.559 | 99.965 | 21.2413 | 21.246 | 6.007 | 7.149
Number of hops |  |  |  |  |  | 
Max Average | 6 2.595 | 6 3.099 | 14 5.847 | 20 8.234 | 29 11.841 | 47 20.451
E2E transmission delay (s) |  |  |  |  |  | 
Min Max 99.99th percentile Average | 0.0163 10.0366 10.022 2.841 | 0.0163 10.039 10.022 3.722 | 0.0163 40.055 40.019 11.238 | 0.0163 65.035 55.063 17.582 | 0.0163 80.041 75.049 29.284 | 0.0163 120.043 110.037 52.903
Notes: 1089 devices: One packet every 30min / device  one packet in the network every 1.65s  collisions on the duty period
10000 devices: => one packet every every 0.18s

## Slide 42: Simulation results – DC Upstream (2/2)
Performance criteria | 11 x 11 |  | 33 x 33 |  | 100 x 100 | 
 | No SINR threshold | SINRT = 9 | No SINR threshold | SINRT = 9 | No SINR threshold | SINRT = 9
Battery consumption in 24 hours in mA (Expected lifetime) |  |  |  |  |  | 
Min | 1.085 (5y 18d) | 1.143 (4y 289d) | 0.976 (5y 224d) | 1.035 (5y 107d) | 0.487 (11y 87d) | 0.529 (10y 129d)
Max | 10.286 (194d) | 12.689 (157d) | 30.003 (66d) | 32.984 (60d) | 27.606 (72d) | 41.976 (47d)
Average | 4.206 (1y 110d) | 5.032 (1y 32d) | 7.018 (284d) | 9.681 (85d) | 5.217 (1y 18d) | 8.149 (245d)
PAN Coordinator | 9.106 (219d) | 11.146 (179d) | 19.503 (102d) | 23.359 (85d) | 20.747 (96d) | 33.783 (59d)
Notes: As the number of terminals increase they spend most of the awake time trying to access the channel in CSMA and spend less time in transmission
Most of the action happens in the intermediate hops and the packets do not reach the PAN coord

## Slide 43: Simulation results – DC Downstream (1/2)
Performance criteria | 11 x 11 |  | 33 x 33 |  | 100 x 100 | 
 | No SINR threshold | SINRT = 9 | No SINR threshold | SINRT = 9 | No SINR threshold | SINRT = 9
E2E successful transmission ratio (%) | 99.659 | 99.69 | 39.805 | 46.377 | 19.632 | 23.807
Number of hops |  |  |  |  |  | 
Max Average | 5 2.379 | 8 2.731 | 13 6.437 | 21 8.103 | 47 18.276 | 49 20.808
E2E transmission delay (s) |  |  |  |  |  | 
Min Max 99.99th percentile Average | 0.0163 10.0211 10.017 2.254 | 0.0163 10.0414 10.0406 3.1177 | 0.0163 30.0211 30.019 11.823 | 0.0163 50.017 45.049 15.949 | 0.0163 115.539 110.483 41.058 | 0.0163 120.934 110.046 52.028
Notes: There is less traffic compared to US but there is still collision with signaling packets upstream and DS packets

## Slide 44: Simulation results – DC Downstream (2/2)
Performance criteria | 11 x 11 |  | 33 x 33 |  | 100 x 100 | 
 | No SINR threshold | SINRT = 9 | No SINR threshold | SINRT = 9 | No SINR threshold | SINRT = 9
Battery consumption in 24 hours in mA (Expected lifetime) |  |  |  |  |  | 
Min | 0.227 (24y 28d) | 0.244 (22y 289d) | 0.289 (18y 357d) | 0.312 (17y 198d) | 0.295 (18y 217d) | 0.316 (17y 127d)
Max | 1.636 (3.127d) | 1.601 (3y 153d) | 8.745 (228d) | 11.028 (181d) | 13.803 (144d) | 18.771 (106d)
Average | 0.666 (8y 82d) | 0.736 (7y 162d) | 1.369 (4y 1d) | 1.775 (3y 31d) | 1.552 (3y 193d) | 1.922 (2y 310d)
PAN Coordinator | 1.969 (2y 285d) | 2.193 (2y 181d) | 11.596 (172d) | 14.248 (140d) | 20.016 (99d) | 25.215 (79d)
Notes: As the number of terminals increase they spend most of the awake time trying to access the channel in CSMA and spend less time in transmission
Most of the action happens in the intermediate hops and the packets do not reach the PAN coord

## Slide 45: Simulation results – DC Multicast (1/2)
Performance criteria | 11 x 11 |  | 33 x 33 |  | 100 x 100 | 
 | No SINR threshold | SINRT = 9 | No SINR threshold | SINRT = 9 | No SINR threshold | SINRT = 9
E2E successful transmission ratio (%) | 100 | 100 | 100 | 100 | 19.632 | 23.807
Number of hops |  |  |  |  |  | 
Max Average | 7 4.362 | 7 4.564 | 17 13.092 | 21 8.103 | 54 40.382 | 54 41.306
E2E transmission delay (s) |  |  |  |  |  | 
Min Max 99.99th percentile Average | 0.0358 15.0499 15.0366 7.8343 | 0.0374 20.0163 15.0334 8.2238 | 15.0489 35.0435 35.0434 25.6277 | 20.0163 45.0163 40.0371 28.232 | 60.03264 125.0163 115.0171 84.3288 | 65.0163 115.0172 120.0339 84.7991
Notes: There is less traffic compared to US but there is still collision with signaling packets upstream and DS packets

## Slide 46: Simulation results – DC Multicast (2/2)
Performance criteria | 11 x 11 |  | 33 x 33 |  | 100 x 100 | 
 | No SINR threshold | SINRT = 9 | No SINR threshold | SINRT = 9 | No SINR threshold | SINRT = 9
Battery consumption in 24 hours in mA (Expected lifetime) |  |  |  |  |  | 
Min | 0.24 (22y 316d) | 0.247 (22y 37d) | 0.299 (18y 106d) | 0.314 (17y 162d) | 0.335 (16y 121d) | 0.337 (16y 77d)
Max | 0.733 (7y 173d) | 0.936 (5y 311d) | 1.774 (3y 32d) | 1.918 (2y 312d) | 4.457 (1y 83d) | 5.031 (1y 32d)
Average | 0.467 (11y 267d) | 0.521 (10y 184d) | 1.421 (3y 312d) | 1.455 (3y 279d) | 1.646 (3y 120d) | 1.681 (3y 94d)
PAN Coordinator | 0.818 (6y 255d) | 0.95 (5y 279d) | 1.667 (3y 104d) | 2.091 (2y 226d) | 2.91 (3y 322d) | 3.305 (1y 240d)
Notes: Very low packet birth rate in the network. Only the MC members are sending DA to the root

## Slide 47: Simulation results – DC Broadcast (1/2)
Performance criteria | 11 x 11 |  | 33 x 33 |  | 100 x 100 | 
 | No SINR threshold | SINRT = 9 | No SINR threshold | SINRT = 9 | No SINR threshold | SINRT = 9
E2E successful transmission ratio (%) | 99.521 | 99.833 | 100 | 100 |  | 
Number of hops |  |  |  |  |  | 
Max Average | 8 3.09 | 9 3.222 | 21 8.828 | 22 9.077 |  | 
E2E transmission delay (s) |  |  |  |  |  | 
Min Max 99.99th percentile Average | 0.0163 25.0163 20.0366 4.5981 | 0.0163 25.0187 25.0163 4.8107 | 0.0163 45.0363 45.0211 16.0994 | 0.0163 50.0179 45.0339 17.0833 |  | 
Notes: There is less traffic compared to US but there is still collision with signaling packets upstream and DS packets

## Slide 48: Simulation results – DC Multicast (2/2)
Performance criteria | 11 x 11 |  | 33 x 33 |  | 100 x 100 | 
 | No SINR threshold | SINRT = 9 | No SINR threshold | SINRT = 9 | No SINR threshold | SINRT = 9
Battery consumption in 24 hours in mA (Expected lifetime) |  |  |  |  |  | 
Min | 0.268 (20y 147d) | 0.284 (19y 92d) | 0.873 (6y 100d) | 0.878 (6y 86d) |  | 
Max | 0.783 (6y 361d) | 0.851 (6y 160d) | 2.286 (2y 144d) | 2.799 (1y 349d) |  | 
Average | 0.532 (10y 105d) | 0.553 (9y 329d) | 1.753 (3y 45d) | 1.957 (2y 291d) |  | 
PAN Coordinator | 0.864 (6y 123d) | 0.798 (6y 315d) | 2.25 (2y 158d) | 2.765 (1y 358d) |  | 
Notes: Very low packet birth rate in the network. Only the MC members are sending DA to the root

## Slide 49: Simulation results – DC P2P(1/2)
Performance criteria | 11 x 11 |  | 33 x 33 |  | 100 x 100 | 
 | No SINR threshold | SINRT = 9 | No SINR threshold | SINRT = 9 | No SINR threshold | SINRT = 9
Initialization time (s) | 24.2102615 |  | 44.2342633 |  | 106.9370197 | 
E2E successful transmission ratio (%) | 91.386 | 99.833 | 65.382 | 97.554 |  | 
Number of hops |  |  |  |  |  | 
Max Average | 8 8 | 9 9 | 19 19 | 28 28 |  | 
E2E transmission delay (s) |  |  |  |  |  | 
Min Max 99.99th percentile Average | 5.0462 5.0546 5.0542 5.05044 | 5.0466 5.0549 5.0546 5.05047 | 20.0344 20.0412 20.0408 20.0378 | 30.0462 30.0549 30.0546 30.0504 |  | 
Notes: There is less traffic compared to US but there is still collision with signaling packets upstream and DS packets

## Slide 50: Simulation results – DC P2P(2/2)
Performance criteria | 11 x 11 |  | 33 x 33 |  | 100 x 100 | 
 | No SINR threshold | SINRT = 9 | No SINR threshold | SINRT = 9 | No SINR threshold | SINRT = 9
Battery consumption in 24 hours in mA (Expected lifetime) |  |  |  |  |  | 
Min | 0.126 (43y 156d) | 0.129 (42y 168d) | 0.173 (31y 219d) | 0.181 (30y 46d) |  | 
Max | 5.869 (340d) | 5.88 (340d) | 6.219 (321d) | 9.066 (220d) |  | 
Average | 2.057 (2y 242d) | 2.135 (2y 206d) | 1.028 (5y 121d) | 1.539 (3y 204d) |  | 
PAN Coordinator | 5.777 (346d) | 5.892 (339d) | 6.332 (315d) | 6.879 (290d) |  | 
Notes: Only the destination P sends DA

## Slide 51: Simulation results – DC MP2P(1/2)
Performance criteria | 11 x 11 |  | 33 x 33 |  | 100 x 100 | 
 | No SINR threshold | SINRT = 9 | No SINR threshold | SINRT = 9 | No SINR threshold | SINRT = 9
Initialization time (s) | 24.2102615 |  | 44.2342633 |  | 106.9370197 | 
E2E successful transmission ratio (%) | 93.954 | 99.356 | 50.734 | 64.403 |  | 
Number of hops |  |  |  |  |  | 
Max Average | 6 5.812 | 8 7.401 | 19 18.275 | 28 26.48 |  | 
E2E transmission delay (s) |  |  |  |  |  | 
Min Max 99.99th percentile Average | 5.0114 5.0274 5.0268 5.0228 | 5.0344 5.0549 5.0543 5.0429 | 20.0115 20.0412 20.0408 20.0287 | 30.0115 35.0393 35.0264 30.0512 |  | 
Notes: There is less traffic compared to US but there is still collision with signaling packets upstream and DS packets

## Slide 52: Simulation results – DC MP2P(2/2)
Performance criteria | 11 x 11 |  | 33 x 33 |  | 100 x 100 | 
 | No SINR threshold | SINRT = 9 | No SINR threshold | SINRT = 9 | No SINR threshold | SINRT = 9
Battery consumption in 24 hours in mA (Expected lifetime) |  |  |  |  |  | 
Min | 0.155 (35y 136d) | 0.182 (30y) | 0.173 (31y 219d) | 0.181 (30y 46d) |  | 
Max | 26.849 (74d) | 33.978 (58d) | 42.157 (47d) | 49.078 (40d) |  | 
Average | 7.312 (273d) | 10.035 (155d) | 4.752 (1y 55d) | 6.395 (312d) |  | 
PAN Coordinator | 26.589 (75d) | 29.248 (68d) | 43.206 (46d) | 37.065 (53d) |  | 
Notes: Only the terminals on the path of the MP2P use the most energy so the average energy consumption is lower with more terminals

## Slide 53: Simulation results – DC P2P Multicast (1/2)
Performance criteria | 11 x 11 |  | 33 x 33 |  | 100 x 100 | 
 | No SINR threshold | SINRT = 9 | No SINR threshold | SINRT = 9 | No SINR threshold | SINRT = 9
E2E successful transmission ratio (%) | 93.954 | 99.356 | 50.734 | 64.403 |  | 
Number of hops |  |  |  |  |  | 
Max Average | 6 5.812 | 8 7.401 | 19 18.275 | 28 26.48 |  | 
E2E transmission delay (s) |  |  |  |  |  | 
Min Max 99.99th percentile Average | 5.0114 5.0274 5.0268 5.0228 | 5.0344 5.0549 5.0543 5.0429 | 20.0115 20.0412 20.0408 20.0287 | 30.0115 35.0393 35.0264 30.0512 |  | 
Notes: There is less traffic compared to US but there is still collision with signaling packets upstream and DS packets

## Slide 54: Simulation results – DC P2P Multicast (2/2)
Performance criteria | 11 x 11 |  | 33 x 33 |  | 100 x 100 | 
 | No SINR threshold | SINRT = 9 | No SINR threshold | SINRT = 9 | No SINR threshold | SINRT = 9
Battery consumption in 24 hours in mA (Expected lifetime) |  |  |  |  |  | 
Min | 0.155 (35y 136d) | 0.182 (30y) | 0.173 (31y 219d) | 0.181 (30y 46d) |  | 
Max | 26.849 (74d) | 33.978 (58d) | 42.157 (47d) | 49.078 (40d) |  | 
Average | 7.312 (273d) | 10.035 (155d) | 4.752 (1y 55d) | 6.395 (312d) |  | 
PAN Coordinator | 26.589 (75d) | 29.248 (68d) | 43.206 (46d) | 37.065 (53d) |  | 
Notes: Only the terminals on the path of the MP2P use the most energy so the average energy consumption is lower with more terminals

## Slide 55: Simulation results – DC P2P Broadcast (1/2)
Performance criteria | 11 x 11 |  | 33 x 33 |  | 100 x 100 | 
 | No SINR threshold | SINRT = 9 | No SINR threshold | SINRT = 9 | No SINR threshold | SINRT = 9
E2E successful transmission ratio (%) | 98.507 | 99.122 | 94.199 | 98.5605 |  | 
Number of hops |  |  |  |  |  | 
Max Average | 13 5.524 | 16 6.9 | 39 18.146 | 52 23.76 |  | 
E2E transmission delay (s) |  |  |  |  |  | 
Min Max 99.99th percentile Average | 0.0466 15.0603 15.036 4.5794 | 5.0115 20.0236 20.0121 6.5682 | 10.0223 50.0134 45.0266 21.0618 | 15.0459 70.0239 65.0239 28.0437 |  | 
Notes: There is less traffic compared to US but there is still collision with signaling packets upstream and DS packets

## Slide 56: Simulation results – DC P2P Broadcast (2/2)
Performance criteria | 11 x 11 |  | 33 x 33 |  | 100 x 100 | 
 | No SINR threshold | SINRT = 9 | No SINR threshold | SINRT = 9 | No SINR threshold | SINRT = 9
Battery consumption in 24 hours in mA (Expected lifetime) |  |  |  |  |  | 
Min | 7.443 (268d) | 7.481 (267d) | 6.822 (293d) | 7.122 (280d) |  | 
Max | 12.571 (159d) | 15.455 (129d) | 15.937 (125d) | 19.199 (104d) |  | 
Average | 7.796 (256d) | 9.571 (208d) | 10.097 (198d) | 10.801 (185d) |  | 
PAN Coordinator | 7.798 (278d) | 8.069 (247d) | 9.085 (220d) | 9.631 (104d) |  | 
Notes: Only the terminals on the path of the MP2P use the most energy so the average energy consumption is lower with more terminals

## Slide 57: Data aggregation evaluation
Parameter | Value
Simulation area | 2 km x 2 km square area where CS located centered
Number of meter nodes | 1,000
Frequency band | 920 MHz
Transmission power | 20 mW
Path loss model | ITU-R P.1411-6 [15]
Shadowing model | Log-normal with standard deviation of 4.0 dB
Receiver sensitivity | -88 dBm
Modulation scheme | 100 kbps, 2 GFSK
Beacon interval | 9.83 s (BO = 10)
Active period lengths | 76.8 ms (SO = 3)
Frame payload length | 100 octets (8 ms)
Routing scheme | Tree routing
Frame arrival | Periodical per each meter node
Frame timeout | Same as arrival interval
[F. Kojima, H. Harada, “Superframe Division Multi-Hop Data Collection with Aggregation on Wi-SUN Profile for ECHONET Lite”,
WCNC’2014, Istanbul, April 2014.]

## Slide 58
Thank you
Q/A