## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Discovery Procedure]
Date Submitted: [September 17, 2014]
Source: [Huan-Bang Li, Marco Hernandez, Igor Dotlic, and Ryu Miura] Company [NICT]
Address [3-4 Hikarino-oka, Yokosuka, Kanagawa, Japan]
Voice:[+81 468475104], FAX: [:[+81 468475431], E-Mail:[lee@nict.go.jp]
Re: [Response to call for contribution of 15.8 PAC
Abstract: [Discovery Procedure for IEEE802.15.8]
Purpose: [This document is to provide a MAC mechanism]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Discovery Procedure
September 17, 2014

## Slide 3: Discovery Procedure 1
Advertisement:
  An initiator PD (I-PD) broadcasts Discovery Request message for a TBD duration during discovery period.
  Receiving PDs scan the Discovery Request message during discovery period.

## Slide 4: Illustration of Discovery Procedure 1
Discovery Request message
I-PD
J-PD_a
J-PD_b
J-PD_c
Discovery Request message
Discovery Request message

## Slide 5: Discovery Procedure 2
Publish/Subscribe :
  An initiator PD (I-PD) broadcasts Discovery Request message for a TBD duration.
  A Joiner PD (J-PD) scans the Discovery Request message and send Discovery Response message.
  The I-PD receives Discovery Response message and broadcasts a list of received J-PDs that Discovery Response message.
  J-PDs that had sent Discovery Response message but are not included in the J-PD list send Discovery Response message again.
Need further discussion

## Slide 6: Illustration of Discovery Procedure 2
I-PD
J-PD_a
J-PD_b
J-PD_c
Discovery Request message
Discovery Request message
Discovery Request message
Discovery Response message
Discovery Response message
Discovery Response message
J-PD list
J-PD list
J-PD list
Discovery Response message
Need further discussion

## Slide 7: Discovery Procedure 3
Query/Reply :
  An initiator PD (I-PD) broadcasts Discovery Request message for a TBD duration to a query PD (Q-PD).
  A Q-PD scans the Discovery Request message and send back Discovery Response message.

## Slide 8: Illustration of Discovery Procedure 3
I-PD
J-PD_a
J-PD_b
Q-PD
Discovery Request message
Discovery Request message
Discovery Request message
Discovery Response message

## Slide 9
Reference slides

## Slide 10: Motion 1: Frame
Frame: the structure is defined as the following periods in order
  Synchronization period, Discovery period, Peering period, Contention Access period, and Contention Free period.
  The duration of a frame is also the synchronization interval which is fixed with a value of TBD.
  The duration of each period is fixed and the values are TBD.

## Slide 11: Motion7: Information for Discovery
For the purpose of discovery of PDs, the discovery information represents one or more of the following IDs
  Device ID, Device Group ID, Application type ID, Application-specific ID, Application-specific user ID, Application-specific group ID.
The discovery information is not limited to IDs mentioned above.

## Slide 12: Discovery Procedure
The Discovery type is defined by a higher layer.
The MAC messages should support at least the following discovery types:
Advertisement: In Advertisement type discovery, a PD broadcasts its own discovery information and does not expect responses.
Publish/Subscribe: In Publish/Subscribe type discovery, a PD broadcasts its own discovery information and expects responses from PDs that have discovered the broadcast message(s).
Query/Reply: In Query/Reply type discovery, a PD broadcasts the discovery information of the PD or PDs being queried and expects a response or responses from the PD or PDs, accordingly.

## Slide 13: Motion9: MAC Discovery Messages
MAC shall support at least the following discovery messages:
Discovery Request message
Discovery Response message