## Slide 1: Proposed Motions for Remaining Issues
September 17, 2014

## Slide 2: Motion X0: Discovery Source ID
Background
  From offline discussion among Samsung, ETRI and InterDigital, it is identified that clarification is required on “Source address in Discovery Request Message” from Motion 22 in DCN11-14-0464-03.
  If we want to support 2-way discovery from MAC perspective, higher layer entity should be distinguished in MAC layer.
Proposed Motion
  Replace “Source address” to “Discovery Source ID”.
  Discovery Source ID is an identification to designate a specific entity in higher layer which triggers transmission of the Discovery Information in Discovery Request/Response message.
  Discovery Source ID is derived from higher layer.
  TBD: method to avoid conflict of Discovery Source ID

## Slide 3: Motion X1: Discovery Resource Selection
A discovery period comprises multiple Discovery Blocks (DBs).
A PD scans a discovery period for a suitable DB for transmission in next discovery period, if condition is met.
  The condition is based on energy sensing result from DBs which is not transmitted by the PD.

## Slide 4: Discussion for Power Management
Micro sleep
  A PD may wake up or sleep for a specific period. Details are TBD.
Short sleep
  A PD may wake up for at least Synchronization period, Discovery period and Peering period.
Long sleep
  A PD may wake up or sleep by triggering from higher layer.
Other possibilities to clarify the examples is not limited.
Other possibilities to provide other power saving mode is not limited.

## Slide 5: Motion X3: Channel Selection
Background
  According to discussion from TG8 meeting, a requirement to provide multiple channel or different channel from current one is identified. (channel means frequency channel.)
For discovery, a PD selects a channel from a channel list for discovery.
TBD: channel selection for peering
For communication, a PD may selects one or multiple channel from a channel list for communication.
Note: channel list is provisioned.

## Slide 6: Motion X4: Multi-hop Support
Background
  For the sake of progress and to avoid layer-violation,
Proposed Motion
  Any identification, context or etc. to represent multi-hop link is not specified.
  Any procedure to establish and manage multi-hop link is not specified.
  Other possibilities to support multi-hop protocol in higher layer is not limited and needs further discussion.

## Slide 7: Motion X5: MAC layer Filtering for Discovery message
MAC layer can pre-filter Discovery Request message prior to sending to higher layer.
This implies that higher layer should provide information or functions for per-filtering to MAC layer.
Note: MAC layer pre-filtering can be revisited if technical pros and cons are clearly identified.