## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Merged Proposal from NICT-OKI-ETRI for TG10]
Date Submitted: [03 November, 2014]
Source: 1[Verotiana Rabarijaona, Fumihide Kojima], 2[Hiroshi Harada], 3[Noriyuki Sato, Kiyoshi Fukui], 4[ Jaehwan Kim, Sangjae Lee, Sangsung Choi], 5[Jaebeom Kim, Jina Han, Young-Bae Ko], 6[Soo-Young Chang]
Company: 1[NICT], 2[Kyoto University], 3[OKI], 4[ETRI], 5[Ajou University], 6[SYCA]
Address: 1[3-4, Hikarino-oka, Yokosuka, 239-0847 Japan]
Voice:1 [+81-46-847-5075], FAX: [+81-46-847-5089], E-Mail:1 [rverotiana@nict.go.jp]
Re: [Call for Final Proposals.]
Abstract: [This contribution presents a merged proposal for the TG10.]
Purpose: [Merged proposal to build the baseline]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: TG10 Merger of the proposals from NICT, OKI and ETRI (Hybrid L2R)

## Slide 3: List of Functionalities to merge
1. Mesh topology discovery
Mesh Routing
Route discovery
2. Extensible mesh routing architecture (metric alternative, selection, notification, new metrics)
Routing metrics
Multiple entry and exit points
3. Unicast
a. Hop-by-hop retry
4. Broadcast
5. Low power operation
6. Mesh Security
7. Discovery and association
8. Changes to the MAC
9. Multicast routing
a. Hop-by-hop retry

## Slide 4: 1. Mesh topology discovery, mesh routing, route discovery - proposal
The HMT construction IE and the IEs for the HELLO, PANN/PANN-RP are merged
  15.4 already avails several options where the IEs can be used. The resulting IE may be included in a EB or a MP frame.
    EBs can be periodic or aperiodic
    They can have different periods depending on the IE they contain, or the IEs can be included in the same beacon. EBs with different IEs have been used in many subsequent amendments after 4e
    EBs can contain payload and header IEs
Storing and non-storing mode should be supported
  Non-storing mode requires less memory but may require a lot of energy to transmit large frames due to the intermediate hops in source routing
  Storing mode requires memory but allows low overhead frames
  The size of the memory of a device is up to the implementer but all options should be covered
  There should be a PIB set depending on the storing mode. In storing mode, a device shall be able to store at least one parent. The final size of the neighbor table is up to the vendor.

## Slide 5: 1. Mesh topology discovery, mesh routing, route discovery - proposal
Reactive or proactive
  Energy constraints require proactive routing. Flooding for route establishment uses a lot of energy. The delay in route establishment is also considerable in beacon enabled PANs
  Reactive may be used for small networks or networks without energy constraints. Reactive protocols may also be used in networks without memory constraints so that the routes can be stored to minimize the flooding for route discovery.
P2P routing
  Packet forwarded up until the first common ancestor then down to the destination: the routes can be very long in a large network
  Transversal reactive routes: may offer shorter routes but generates a lot of overhead. Necessary IEs for P2P reactive route discovery (such as PREQ-PREQ-RP) are defined.
  Most of the use cases require communication to and from a gateway. P2P reactive route discovery will be optional for use cases that may require P2P communication

## Slide 6: 1. Mesh topology discovery, mesh routing, route discovery – downward routing
Destination announcement IE, RREC and PANN-RP fulfill the same role.
  PANN-RP adds the TMTCP-aware functionality.
  The three IEs are merged as proposed later in this presentation in the Route Announcement IE

## Slide 7: L2R IE format
Bit: 0-10 | 11-14 | 15 | Octets: 0.. 2047
Length | Group ID | Type = 1 | Content
Octet: Variable | … | Variable
Nested IE | … | Nested IE
- The use of nested IEs provides flexibility to add all the necessary functionalities
- The L2R header may not be necessary as all the fields are already present in the MHR or other nested IEs

## Slide 8: Topology Construction IE
Bits: 0-7 | 8-14 | 15 | Octets: 1/2 | Octets: 0/1 | 0/2/8 | 0/1 | 0/1 | 0/1 | 0/9 | Variable | … | Variable
Length | Sub-ID | Type = 0 | Descriptor | Entity ID | Tree Root address | Depth | Sequence number | TC IE interval | MCO fields | Path quality metric 1 | … | Path quality metric N
Bits: 0-2 | 3-5 | 7 | 8-11 | 12-15 | Octet: 0/Variable | 0/Variable
Path quality metric ID | Priority | Reserved | Length of the Value (octets) | Length of the Threshold (octet) | Threshold | Value
Bit:0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8-10
Descriptors present | High Reliability | Data Aggregation | Multi-channel Operation (MCO) | Brother routing | DS route required | Reactive P2P discovery | Storing mode | Number of metrics
11 | 12-13 | 14 | 15 |  |  |  |  | 
Tree Root address mode | Security modes | Multicast subscription in RA | Reserved |  |  |  |  | 
Octet: 0/8 | 0/1
Associated PAN coord (if MCO) | Allocated channel number (if MCO)

## Slide 9: Topology Construction IE – description 1
All the fields after the Type are not present if the IE is in request frame (EBR). In this case, the IE is used to discover existing L2R network
If a device belongs to different routing trees, it includes the corresponding number of Topology Construction IE in the EB
Descriptor: indicates the functionalities available in a L2R routing instance. If the first bit is set to 0, the rest of the descriptor field is ignored, and the descriptor size is 1 octet.
  High reliability: if set to 1, the AR field in the MHR must be set to 1 and all the packets must be acknowledged. If set to 0, acknowledgment is optional.
  Data aggregation: if set to 1, data aggregation is allowed in the L2R network, otherwise, data aggregation is prohibited. If data aggregation is allowed in a L2R network, the buffering time is indicated in the PIB
  Multi-channel operation: indicates if multiple channels and multiple PANs are used in the L2R network.
  Brother routing: if set to 1, routing through a brother is allowed in the network. This implies that the network can use a loop avoidance mechanism.
  DS route required: if set to 1, all the devices are required to send a Route Annoucement IE to build downstream routes

## Slide 10: Topology Construction IE – description 2
Descriptor (cont’d):
  Reactive P2P discovery: if set to 1, reactive P2P discovery is allowed
  Storing mode: if set to 1, the network is in storing mode. If set to 0, the network is on non-storing mode and source routing must be used
  Number of metrics: indicates the number of link quality metrics at the end of the nested IE
  Address modes present: indicates if the address mode fields of the addresses in the IE are present. If this field is set to 0, only 16-bit addresses are used and the address mode fields are not present.
  Security modes:
    00: none
    01 : PAN credentials
    10 : KMP
    11 : Reserved
  Multicast subscription in RA: if set to 1, Route Announcement (RA) may contain Multicast subscription field and multicast routing is accordingly used. If set to 0, multicast packets are flooded and filtered by the upper layer

## Slide 11: Topology Construction IE – description 3
Entity ID: identifies an entity (ex: data collection entity, control and monitoring entity…) reachable through the L2R network. An entity may be reachable through several tree roots (gateway) and a tree root may be connected to several entities.
Tree root address mode: present only if the “Address modes present” flag is set to 1
Tree root address: address of the root of the tree offering routing towards an entity available.
Depth: Distance in hops of the transmitting device to the root of the tree, establishing parent-child and brotherhood relationship between the devices. A node that has lost all paths to the root sends a TC IE with a depth of 0xffff.
Sequence number: Set by the root of the tree and propagated. Used to know the latest tree information. Several consecutive TC IE with the same SN indicates that there might be a path breakage upstream of the device transmitting the TC IE or that the tree root is not available anymore
TC IE interval: interval between each Topology construction IE.
Multi-Channel Operation fields (TMCTP): present only if MCO is enabled in the descriptor
  Associated PAN coordinator: address of the PAN coordinator to which the transmitting device is associated. Present only if the MCO is enabled.
  Allocated channel number: indicates the channel on which the coordinator of the transmitting device is operating. Present only if MCO is enabled

## Slide 12: Topology Construction IE – description 4
Path quality metric: Describes the metric in use in the L2R network to evaluate a path between a device and the root. This field also is used to inform the network of any update/change in the metrics in use. Several metrics may be used in one L2R network.
  Path quality metric ID: identifies the metric in use in the network. The metrics used in the proposals can be assigned IDs as default metrics (hop count, SINR, Inactive Overhead Aware Link Metric). Remaining IDs may be used by the implementers. Set by the root of the tree and propagated by the other devices
  Priority: indicates the priority of the current metric over other metrics that may be present. Set by the root of the tree and propagated by the other devices
  Length of Value: in octets. Set by the root of the tree and propagated by the other devices
  Length of Threshold: in octets. If “Brother routing” is set to 0, this field shall be set to 0. Set by the root of the tree and propagated by the other devices
  Value: value of the metric of the transmitting device, only present if it needs to be shared with neighbors.
  Threshold: present only if “brother routing” is set to 1. Indicates the threshold of the metric that a link with a parent must satisfy. If the threshold is not satisfied the better of the best parent and best brother is selected as a next hop

## Slide 13: Neighbor Link Metric IE
Bits: 0-10 | 11-14 | 15 | Bits: 0 | 1-7 | Octets: Variable | … | Variable
Length | Sub-ID | Type= 1 | Address mode present | Num. of neighbors | Neighbor metric container 1 | … | Neighbor metric container N
Bits: 0-3 | 4 | 5-7 | Octets: 2/8 | Variable | … | Variable
Num. of metrics | Addr. mode | Reserved | Neighbor address | Link metric 1 | … | Link metric M
Bits: 0-3 | 4-7 | Octets: Variable
Length | Link quality metric ID | Value

## Slide 14: Neighbor Link Metric IE – description 1
This IE is used to inform the link metrics between the transmitter of the IE and the neighbors present in the IE. The IE is sent by broadcast on one hop. (Ex. Incoming link cost)
  Address mode present: indicates if the address mode fields of the neighbor addresses in the IE are present. If this field is set to 0, only 16-bit addresses are used and the address mode fields are not present.
  Number of neighbors: The number of neighbors to which the issuer node sends the metric(s).
  Neighbor metric container field: contains the metrics measured by the issuer node. Each container can carry one or more metrics.
  Number of metrics: indicates the number of link metrics present in the container.
  Address mode: Address mode of the neighbor address
  Neighbor address: Neighbor’s address

## Slide 15: Neighbor Link Metric IE – description 2
  Link metric : describes the metric used to evaluate a link between two neighboring devices. This field also is used to inform the network of any update/change in the metrics in use. Several metrics may be used in one L2R network. The metrics in use are decided by the root of the tree, and they are propagated to the other devices
    Length: represents the length of this field.
    Link quality metric ID: identifies the metric. The metrics used in the proposals can be assigned IDs as default metrics (hop count, SINR, Inactive Overhead Aware Link Metric). Remaining IDs may be used by the implementers
    Value: value of the link metric between the transmitting device and the neighbor

## Slide 16: Route Announcement IE
Bits: 0-10 | 11-14 | 15 | 1 | Octets: 0/1 | 0/2/8 | 0/2/8 | 0/9 | Octets: 0/1 | 1 | 0 - Variable
Length | Sub-ID | Type = 1 | Descriptor | Entity ID | Tree Root address | Source address | Multi-channel operation fields | Multicast subscription | Number of intermediate addresses | Intermediate addresses list
Octets: 0/8 | 0/1
Associated PAN coordinator extended address | Allocated channel number
Bits: 0-5 | 6-7 | Octets: 0/2 | … | 0/2
Number M of multicast group2 | Reserved | Multicast address 1 | … | Multicast address M
Bit | Flag
0 | Multi-Channel Operation
1 | Multicast subscription
2 | Tree root address mode
3 | Source address mode
4 | Intermediate Address mode present
5-7 | Reserved
Octets: 0/1 | 0/2/8 | … | 0/1 | 0/2/8
b0: Intermediate hop address mode 1 b1-7: reserved | Intermediate hop address 1 | … | b0: Intermediate hop address mode N b1-7: reserved | Intermediate hop address N

## Slide 17: Route Announcement IE – description 1
Used to build downstream routes and/or to announce a subscription to a multicast group. In the latter case, the multicast addresses announced are treated as unicast addresses for routing
Descriptor: bitmap informing of information present in the IE
  Multi-channel operation: indicates if the routing tree spans several PANs  the MCO fields are required
  Multicast subscription flag: indicates the presence or absence of the “multicast subscription” field.
  Tree root address mode
  Source address mode
  Intermediate Address mode present: indicates the presence of the address modes of the intermediate hops in the IE. If set to 0, only short addresses are used
Entity ID: identifies an entity (ex: data collection entity, control and monitoring entity…) reachable through the L2R network.
Tree root address: address of the root of the tree offering routing towards an entity available.
Source address: address of the original source of the RA IE

## Slide 18: Route Announcement IE – description 2
Multi-channel operation fields: fields regarding the MCO. These fields are present only if the bit for “Multi-channel operation” in the Device Status is set to 1
  Associated PAN coordinator extended address: address of the PAN coordinator which the transmitting device is associated to.
  Allocated channel number: indicates the channel on which the coordinator of the transmitting device is operating.
Multicast subscription:
  Number of multicast group: number of multicast groups to which the source of the route announcement IE belongs.
  Multicast address: address of the multicast group to which the source of the destination announcement IE belongs. L2R will have a block of 2 byte addresses reserved for multicast groups (ex: 0xff00 ~ 0xfffd). Subscription and mapping to the multicast groups are up to the implementer and out of the scope of L2R.
    Only using short addresses for multicast routing

## Slide 19: Route Announcement IE – description 3
Number of intermediate addresses: Number of addresses in the intermediate address list.
Intermediate addresses list: list of addresses between the source of the route announcement IE and the root of the tree. Each intermediate hop device appends it own address before forwarding the IE and increment the “Number of Intermediate addresses”. This list is present only if the network is in non-storing mode. If the address mode is not present short addresses are used.

## Slide 20: Short Route Announcement IE
Used to by a device to inform a neighbor of a path to a destination.
Assumes small scale networks (within 10 hops) such as HANs with only one PAN, tree root ID co-located with the PAN coordinator, same addressing mode within the PAN
Bits: 0-7 | 8-14 | 15 | Octet: 1 | 2/8 | 1 | 0 - Variable
Length | Sub-ID | Type = 0 | Sequence number | Route Destination Address | Number of intermediate addresses | Intermediate addresses list
Sequence number: used to identify the latest SRA IE
Route Destination Address: address of the final destination device of the current route announcement.
Number of intermediate addresses: Number of addresses in the intermediate address list.
Intermediate addresses list: list of addresses between the source of the route announcement and the destination. Each intermediate hop device appends it own address before forwarding the IE and incre.

## Slide 21: Reactive P2P Request IE (P2P-RQ)
Bits: 0-7 | 8-14 | 15 | Octet: 1 | 2/8 | 2/8 | 1 | 1 | 4 | 0/1 | 1 | 0 - Variable
Length | Sub-ID | Type = 0 | Descriptor | Route Destination address | Route Source Address | HOP Count | TTL | Sequence number | Allocated channel number | Number of intermediate addresses | Intermediate addresses list
Bit 0 | 1 | 2 | 3 | 4 | 5-7
Request Direct Response | Multi-channel operation | Route Destination address mode | Route Source address mode | Address mode present | Reserved
Octets: 0/1 | 0/2/8 | … | 0/1 | 0/2/8
b0: Intermediate hop address mode 1 b1-7: reserved | Intermediate hop address 1 | … | b0: Intermediate hop address mode N b1-7: reserved | Intermediate hop address N

## Slide 22: Reactive P2P-RQ IE – Description (1)
Descriptor
  Direct response: if set to 1, any intermediate device that has a route information to the destination responds directly with a Reactive P2P-RP to the originator node.
  Multi-channel operation: indicates if multiple channels and multiple PANs are used in the L2R network.
  Destination address mode
  Source address mode
Route Destination address : indicates the destination address that the source device wants to find. Extended addressing must be used if MCO is enabled
Route Source address : indicates the address of the original transmitter of the Reactive P2P discovery message. Extended addressing must be used if MCO is enabled

## Slide 23: Reactive P2P-RQ IE – Description (2)
  HOP Count: the number of hops from the source node
TTL: Remaining number of transmissions allowed. Decreased at each hop. If 0, the packet shall not be forwarded
Sequence number: indicates the sequence number of reactive P2P message that is utilized to avoid loop.
Allocated channel number: indicates the channel on which the coordinator of the transmitting device is operating. Present only if MCO is enabled
Number of intermediate addresses: Number of addresses in the intermediate address list.
Intermediate addresses list: list of addresses between the source and the destination of the route being requested. Each intermediate hop device appends it own address before forwarding the IE. This list is present only if the network is in non-storing mode. If the address mode is not present short addresses are used.

## Slide 24: Reactive P2P-RP IE
Bits: 0-7 | 8-14 | 15 | 1 | Octets: 2/8 | 2/8 | 0/1 | 1 | 0 - Variable
Length | Sub-ID | Type = 0 | Descriptor | Route Source Address | Route Destination address | Allocated Channel number | Number of intermediate addresses | Intermediate addresses list
Bit: 0 | 1 | 2 | 3 | 4-7
Multi-channel operation | Route Destination address mode | Route Source address mode | Intermediate Address mode present | Reserved
Octets: 0/1 | 0/2/8 | … | 0/1 | 0/2/8
b0: Intermediate hop address mode 1 b1-7: reserved | Intermediate hop address 1 | … | b0: Intermediate hop address mode N b1-7: reserved | Intermediate hop address N

## Slide 25: Reactive P2P-RP IE – Description (1)
Descriptor
  Multi-channel Operation: if set to 1, the routing is be done across several PANs using different channels
  Route Destination address mode
  Route Source address mode
  Intermediate Address mode present: indicates the presence of the address modes of the intermediate hops in the IE. If set to 0, only short addresses are used
Route Destination address : indicates the destination address that the source device wants to find. Extended addressing must be used if MCO is enabled
Route Source address : indicates the address of the original transmitter of the Reactive P2P request. Extended addressing must be used if MCO is enabled
Allocated channel number: present only MCO is enabled
Number of intermediate addresses: Number of addresses in the intermediate address list.
Intermediate addresses list: list of addresses between the source and the destination of the route, copied from the P2P-RQ IE. This list is present only if the network is in non-storing mode. If the address mode is not present short addresses are used.

## Slide 26: L2R Routing IE
The L2R Routing IE is added to a data frame to enable its routing. A device looks at the destination address therein and finds the appropriate next hop based on its neighbor/routing table when source routing is not used
Bits: 0-10 | 11-14 | 15 | Octets:1 | 0/1 | 0/1 | 2/8 | Octets: 0/Variable | 1
Length | Sub-ID | Type = 1 | Descriptor | Entity ID | Bit 0: Tree root address mode Bits 1-7: reserved | Tree Root address | Addressing fields (original source and final destination) | L2R sequence number
 |  |  |  |  | 1 | 1 | 0/1 | 0 - Variable
 |  |  |  |  | TTL | E2E Number of retry | Number of intermediate addresses | Intermediate addresses list
Bits: 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
Data aggregation | Source routing | Multi-channel operation | L2R Retransmission | Delay critical | Guaranteed transmission | Intermediate Address mode present | Reserved

## Slide 27: L2R Routing IE – description 1
Descriptor
  Data aggregation: indicates if the current packet can be aggregated.
  Source routing: if set to 1, an intermediate address list is present.
  Multi-channel operation: if set to 1, the routing is done across several PANs using different channels
  L2R retransmission: indicates if retransmission through an alternative neighbor is allowed for the current packet
  Delay critical: if set to 1, the packet should not be queued but forwarded immediately or discarded.
  Guaranteed transmission: If set to 0 and if the queue is full, the current packet may be discarded. If set to 1, the current packet must be buffered in the queue. The first packet that does not require guaranteed transmission in the queue is discarded and the incoming packet is queued.
    * If Delay critical is set to 1 then Guaranteed transmission is ignored.
  Intermediate Address mode present: indicates the presence of the address modes in the IE. If set to 0, only short addresses are used

## Slide 28: L2R Routing IE – description 2
Entity ID: : identifies an entity (ex: data collection entity, control and monitoring entity…) reachable through the L2R network.
Tree root address mode: present only if the “Address modes present” flag is set to 1
Tree root address: address of the root of the tree offering routing towards an entity available.
Addressing fields:
  PAN ID the original source and final destination: present only if inter-PAN communication is enabled
  Address modes of the original source and final destination addresses: present only if the “Address modes present” flag is set to 1
  Address of the original source and the final destination.
L2R sequence number: sequence number of the data frame being routed
TTL: Time to live to avoid infinite loop
E2E Number of retry: remaining number of times the packet is allowed to be retransmitted on the path to the destination.

## Slide 29: L2R Routing IE – description 3
Number of intermediate addresses: present only if “source routing” is set to 1. Indicates the number of intermediate addresses between the source and the final destination. The number is decreased by 1 at each hop.
Intermediate address list: present only if “source routing” in the Topology construction IE is set to 1. Each intermediate hop removes its address before forwarding the packet. Each address is preceded with an “Address mode” field if the “Address mode present” flag is set to 1, otherwise only short addresses are used.

## Slide 30: Short L2R Routing IE
We propose to use a short routing IE (in order to accommodate very small scale networks such as Home Energy Management Systems (HEMS) networks with only one PAN
Bits: 0-7 | 8-14 | 15 | Octets: Variable | 1 | Octets: 0/1 | 0 - Variable
Length | Sub-ID | Type = 0 | Addressing fields (original source and final destination) | L2R sequence number | Number of intermediate addresses | Intermediate addresses list
Addressing fields:
  PAN ID the original source and final destination: present only if inter-PAN communication is enabled
  Address modes of the original source and final destination addresses: present only if the “Address modes present” flag is set to 1
  Address of the original source and the final destination.
L2R sequence number: sequence number of the data frame being routed

## Slide 31: Short L2R Routing IE - description
Number of intermediate addresses: present only if “source routing” is set to 1. Indicates the number of intermediate addresses between the source and the final destination. The number is decreased by 1 at each hop.
Intermediate address list: present only if “source routing” in the Topology construction IE is set to 1. Each intermediate hop removes its address before forwarding the packet. Each address is preceded with an “Address mode” field if the “Address mode present” flag is set to 1, otherwise only short addresses are used.

## Slide 32: Data Aggregation IE
Used in data frames.
Bit: 0-7 | 8-14 | 15 | Bit: 0 | 1-7 | Variable
Length | Sub-ID | Type = 0 | Address mode present | Reserved | IE content
Bits: 0-3 | 6-7 | Octet: 0/1 | 2/8 | Octets: 1 | … | Octet: 0/1 | 2/8 | 1
Number N of aggregated packets | Reserved | b0: Source 1 address mode b1-7: reserved | Source address 1 | Length of the aggregated packet 1 | … | b0: Source N address mode b1-7: reserved | Source address N | Length of the aggregated packet N

## Slide 33: Data Aggregation IE - description
  Address modes present: indicates the presence of the address modes in the IE. If set to 0, only short addresses are used
  Number N of aggregated packets
  Source i address mode: i = 1… N
  Source address i: Address of the source of the packet i
  Length of the aggregated packet i: length in octets

## Slide 34: Address Assignment RQ IE
Bits: 0-7 | 8-14 | 15 | Octet: 8
Length | Sub-ID | Type = 0 | Joining device address
Sent by a coordinator to the PAN coordinator after receiving an Association request from a device wishing to join the PAN. Used in a MP frame jointly with a L2R Routing IE.
- Joining device address: Address of the device requesting to join the PAN

## Slide 35: Address Assignment RP IE
Bits: 0-7 | 8-14 | 15 | Octet: 8 | 2
Length | Sub-ID | Type = 0 | Joining device address | Allocated address
Joining device address: Address of the device requesting to join the PAN
Allocated address

## Slide 36: KMP Relay IE
Bits: 0-7 | 8-14 | 15 | Octet: 1 | 2/8
Length | Sub-ID | Type = 0 | b0: Joining device address mode b1-7: reserved | Joining device address
Used after association, relayed from the joining device to the PAN coordinator
Joining device address mode
Joining device address: Address of the device requesting to join the PAN

## Slide 37: 3. Unicast - Hop-by-hop retry
Unicast routing using the L2R Routing IE.
Hop-by-hop retry
  Retransmission to next best parent when possible
  Retransmission to best brother or next best parent, only if “Brother routing” in the Topology construction IE is enabled

## Slide 38: 4. Broadcast
Flooding with record of the source address and sequence number. Discarding of seen packets
Use of random jitter

## Slide 39: 5. Low power operation
Low power operation is informed by the MAC (CSL, RIT, Beacon enabled mode…)
Forwarding of packets must be synchronized with the awake time of the next hop

## Slide 40: 6. Mesh security
3 modes of operations – pre-shared, KMP, no security
  The mode in use in the network should be informed by the Topology construction IE.
KMP Scheme should be considered with conjunction with discovery and association procedure.

## Slide 41: 7. Discovery and association
Association to the PAN with 802.15.4 MAC
Association to the L2R network with EBR/ EB
Detection of short address duplication
Discovery of the L2R network with EBR/ EB

## Slide 42: 8. Changes to the MAC
Topology construction IE
L2R routing IE (Short/Long)
Route announcement IE (Short/Long)
Reactive P2P-RQ/RP IE
Data aggregation IE
Address assignment RQ/RP IE
KMP Relay IE

## Slide 43: 9. Multicast routing
Reserving a block of short addresses for multicast (ex: 0xFF00 ~ 0xFFFD).
Mapping between the short addresses and the multicast addresses is up to the implementer. Subscription/leave is an upper layer function treated as data frames by L2.
We suggest only using short addresses for multicast routing.
Multicast address assignment and de-assignment is conducted through primitives from the next upper layer
Two types of multicast
  Flooding + higher layer filter
    recommended for small scale networks or non energy constrained networks
  Going up by unicast, going doing by multicast
    reduced number of transmissions
    recommended for large scale networks and energy constrained networks, requires the multicast subscription field