## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Summary of L2R Proposals
Date Submitted: Nov. 2014
Source: Clint Powell, Powell Wireless Commsulting, LLC
Contact: Clint Powell, Powell Wireless Commsulting, LLC
Voice: +1 480-586-8457, E-Mail: cpowell@ieee.org
Re: TG10 (L2R) Proposals
Abstract: Summary of Proposals Presented at July 2014 Mtg. and Status Update
Purpose: For Nov. 2014 802.15/802.1 Joint Session Update
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.
Notes: Jul 12, 2010
Page 1

## Slide 2
802.15 TG10 (L2R)
  Draft a recommended practice for Layer 2 Routing of Dynamically Changing 802.15.4 Mesh Networks.
Notes: Jul 12, 2010
Page 2
----- Meeting Notes (17/01/2011 11:38) -----
Replace 1st paragraph with context for TVWS

## Slide 3
Heard 4 Proposals
    15-13-0753-19-0010-technical-guidance-document
  Proposal #1 (Rabarijaona, et al): doc. # 15-14-0408-00
  Proposal #2 (Sato, N., Fukui, K.): doc. # 15-14-0393-02
  Proposal #3 (Joo, S.-S., et al.): doc. # 15-14-0401-01
  Proposal #4 (Lee, S., et al.): doc. # 15-14-0409-02
Summary of L2R Proposals Heard at July 2014 Mtg.
Notes: Jul 12, 2010
Page 3

## Slide 4
Proposal #1 - doc. # 15-14-0408-00
Rabarijaona, et al.
Hierarchical Mesh Tree Routing
Main Topics Covered
  Uses concept of Parent, Brother, Child nodes
  Hierarchical Mesh Tree (HMT) Formation, Maintenance Update
    Neighbors are parent, brother, child depending on depth
    Neighbor table is filled after device association w/PAN
    Neighbor table is maintained through EB broadcasts
    Metrics - link quality (BER, success, latency, SINR...) - chosen by the root of the tree
  HMT Routing
    Link Quality Threshold (LQT), w.r.t. chosen metric, is used to determine route
    Makes use of Multipurpose (MP) Frame with a Destination Announcement IE
    If the device does not have enough memory source routing will need to be utilized for packets going upstream
    Covered Routing For
      Multi-Point to Point (MP2P)
      Point to Multi-Point (P2MP)
      Point to Point (P2P)
      Multicast
      Broadcast
  High Reliability
    HR Option is invoked when Acknowledgement Request (AR) bit is set to 1
    If ACK is not received packet is forwarded through another neighbor
    In particular, HR option can be used when no LQT is set
Notes: Jul 12, 2010
Page 4

## Slide 5
Proposal #1 - doc. # 15-14-0408-00 (cont’d.)
Rabarijaona, et al.
Hierarchical Mesh Tree Routing
Main Topics Covered (cont’d.)
  Data Aggregation
    Node aggregates the packets collected from its neighbors with its own pending packet (if present) before forwarding them
    Need to use timer for length of time packet is buffered
Requires the use of 4 New Information Elements (IE's):
  HMT Construction IE
    Used in a Enhanced Beacon or Command Frames
  L2R Routing IE
    Used in Data Frames
  Data Aggregation IE
    Used in Data Frames
  Destination Announcement IE
    Used in a MP Frame sent to the root of the tree
Simulation Results
  SINR used for metric, but flexible to use other metrics
  Simulations assumed Enhanced Beacons (EB) were transmitted every 2 min
Notes: Jul 12, 2010
Page 5

## Slide 6
Proposal #2 - doc. # 15-14-0393-02
Sato, N., Fukui, K.
L2R Final Proposal
Main Topics Covered
  Mapping to the functional requirements of TGD
    Described how/where the TGD functional requirements are covered in the proposal
  Boot strap / key management / security
    Bootstrap example given
  Proposal of L2R commands / messages
    2 step Route Establishment (Re)
      Estab. of upward path
      Inform relation od parent/child to PAN coord.
    Upward Re
      All nodes broadcast HELLO frame to neighbors, carrying link costs between (outgoing) its neighbor nodes and itself
      Receiving nodes decide incoming link cost
      Mutual out/in link cost is then decided by each device. Path cost to the root is calculated by adding link cost and announced to the neighbors. Choosing the lowest path cost, the parent is decided
    Downward Re
      Each node starts to send RREC (route record) frame to its parent node periodically after upward routing is established. RREC contains relationship of parent and child
      PAN coordinator can get all of parent-child relationship info from the network by RREC. PAN coordinator sends a frame using source routing for downward transmission
Notes: Jul 12, 2010
Page 6

## Slide 7
Proposal #2 - doc. # 15-14-0393-02 (cont’d.)
Sato, N., Fukui, K.
L2R Final Proposal
L2R PIBs Needed
  To Support RF Tx Power Control
    Add "Number of neighbor" PIB
    Add "Transmit Power" metric
  To Support Frequency Agility
    Add PAN busy on channel
    Add indication of new channel and when to all nodes
  Broadcast/Multicast
    Rate control and jitter adjustment needed due to flooding of networks
  Multicast
    App. layer filtering by group id for flooding
Outline of multiple subnets operation
  Instance ID and individual path cost is needed for each instance
Routing protocol operation details
  New Payload Group ID "L2R IE" needed for L2R
  Format same as Nested IE for MLME IE
  Need to define Nested IE for each frame type (commands or data frame)
  L2R IE Header (HDR) field described
    Frame Control field and Sub-ID's for L2R Payload IE given
Notes: Jul 12, 2010
Page 7

## Slide 8
Proposal #2 - doc. # 15-14-0393-02 (cont’d.)
Sato, N., Fukui, K.
L2R Final Proposal
Routing protocol operation details (cont’d.)
  The following frames were described:
    Data (upward, downward) Frames
    End-2-End ACK Frame
    Hello command Frame
    Hello Request command Frame
    Route Record command Frame
    MGT-request command Frame
    MGT-response command Frame
    KMP Relay command Frame
    FA Notification command Frame
    FA Channel update command Frame
Simulation Results
  Hop Count used for metric, but flexible to use other metrics
  Hello period of 64 sec
  Delay of forwarding of 10 mSec
Notes: Jul 12, 2010
Page 8

## Slide 9
Proposal #3 - doc. # 15-14-0401-01
Joo, S.-S., et al.
Layer 2 Routing Final Proposal to Call for Contributions
Main Topics Covered
  MAC Link Network (MLN)
    Sub layer peer control via
      L2R IE -header
      L2R payload IE - payload
    Joining
      Send assoc .req. as a cluster root or not
    Maintaining Layer 2 Routing
      maintain cluster matrix as PAN coordinator, cluster root router, router
    Relies on using DSME
    Primitives added
      MLC-LINK-SETUP.request/indication/response/confirm
      MLC-LINK-RELEASE.request/indication/response/confirm
      MLC-MANAGEMENT.request/confirm
    L2R frames
    Uses payload of MAC Data frame for L2R frames
  Tiered Cluster-Tree (TCT) concept introduced
    Device location done via Cskip addressing (deprecated by ZigBee)
    Uses a TCT routing information base
  TCT Routing Metrics defined
    Routing- link type, link quality, load balance
    Route cost calc. - link cost, virtual link cost, route cost
Notes: Jul 12, 2010
Page 9

## Slide 10
Proposal #3 - doc. # 15-14-0401-01 (cont’d.)
Joo, S.-S., et al.
Layer 2 Routing Final Proposal to Call for Contributions
Main Topics Covered (cont’d.)
  TCT Route Maintenance includes
    Maintain virtual link and router
    Updating routing information
    Periodical update
    Event driven update
Proposal not limited to just using DSME MAC (from 15.4e), but standard MAC as well
Simulation Results
  IP link distance from TCP used for metric, but could use hop count
  ZigBee IP Network used
Notes: Jul 12, 2010
Page 10

## Slide 11
Proposal #4 - doc. # 15-14-0409-02
Lee, S., et al.
Proposal of the Hybrid L2 Routing for IEEE 802.15.10
Main Topics Covered
  Proactive Routing - relies on following new control messages
    PAN coordinator announcement (PANN)
    PAN coordinator announcement reply (PANN-RP)
    Frame formats shown for
      ANN and PANN-RP
    Message Sequence Charts Given for
      Msg. Seq. btwn. PAN Coord. and Child Coord.
      Msg. Seq. btwn. Parent Coord. and Child Coord.
    Proactive Route Discovery in TMCTP Illustrated
  Reactive Routing - relies on following new control messages
    P2P route request (PREQ)
    P2P route reply (PREQ-RP)
    Frame formats shown for
      PREQ and PREQ-RP
    Message Sequence Charts Given for
      Msg. Seq. Using PREQ and Direct Reply
      Msg. Seq. Using PREQ Broadcasting
    Reactive Route Discovery in TMCTP Illustrated
Uses concept of TV White Space Multi-channel Cluster Tree PAN (TMCTP)
Notes: Jul 12, 2010
Page 11

## Slide 12
Proposal #4 - doc. # 15-14-0409-02 (cont’d.)
Lee, S., et al.
Proposal of the Hybrid L2 Routing for IEEE 802.15.10
Simulation Results
  Inactive Overhead Aware Link Metric used for metric (where link cost is calculated using channel access overhead, inactive duration overhead and link error rate of the link), but flexible to use other metrics
  Simulated Results Given for:
    Special 108 node Network Using TMCTP
    However, can be used or non TMCTP networks
  For simulations:
    IEEE 802.15.4m TMCTP
      Slotted CSMA/CA (CAP only)
      Beacon based synchronization and association response and request
    Frequency and modulation: 2.4GHz O-QPSK
    Data rate: 250 kbps
    Packet Size: 100 bytes
    Data Traffic Interval: 15 sec
Notes: Jul 12, 2010
Page 12

## Slide 13
Full/Final Simulation Results and Perf. Metrics Presented
  15-13-0753-19-0010-technical-guidance-document
  15-14-0489-02-0010-performance-metrics-for-proposal-evaluation
  Proposal #1 (Rabarijaona, et al): doc. # 15-14-0536-01
  Proposal #2 (Sato, N., Fukui, K.): doc. # 15-14-0532-00
  Proposal #3 (Joo, S.-S., et al.): doc. # 15-14-0546-00
  Proposal #4 (Lee, S., et al.): doc. # 15-14-0604-01
Summary of Sept. 2014 Mtg.
Notes: Jul 12, 2010
Page 13

## Slide 14
Draft TOC Developed & Reviewed
  15-14-0516-01-0010-example-draft-toc
Proposals to Baseline Process Selected
  15-14-0517-00-0010-discussion-points-to-incorporate-the-proposals
  15-14-0518-00-0010-proposals-to-baseline-process
Functionality Comparison of Proposals Generated
  15-14-0520-02-0010-list-of-functionalities
Summary of Sept. 2014 Mtg. (cont’d.)
Notes: Jul 12, 2010
Page 14

## Slide 15
3 of the 4 Proposals working on merging since Sept. Mtg.
  15-14-0622-00-0010-merged-proposal-to-tg10
  Finalizing merger early this week
4th proposal to be merged with other 3 this week
Next Steps
  Adopt a baseline proposal by EOW
  Revise TOC
  Determine text drafting responsibilities by EOW
  Prepare baseline draft before Jan. Mtg.
  Pre-review of baseline draft before Jan. Mtg.
  Finalize baseline draft at Jan. Mtg.
  Start 1st Letter Ballot after Jan. Mtg.
Nov. 2014 Mtg.
Notes: Jul 12, 2010
Page 15