## Slide 1: Proposed Motions for Assigned Tasks
November 3, 2014
Shannon (Samsung)

## Slide 2: Assigned Tasks
[Chair] Each champion's "Detailed" presentation/discussion for assigned tasks. This time, we need to get down to more details including TBD items to the extent that we could generate decent spec draft.
  1) Discovery source ID: Shannon
  2) Discovery resource selection: Shannon
  3) Power management: BJ
  4) Channel selection: H.B. Li
  5) MAC layer filtering for discovery message: Qing
  6) Champion for TBDs resolution in Draft Specification v0.3 for "communication period": Shannon
  7) Champion for TBDs resolution in Draft Specification v0.3 for "Discovery and peering": Qing.
  8) Discovery signal at PHY level: Marco.

## Slide 3: Discovery Source ID
Unfortunately, there was not much discussion on this item.
  [SHP] Since there can be multiple PAC applications (higher layer entities), we need an ID to distinguish these higher layer entities when MAC receives Discovery Response message and indicate to the 'appropriate' higher layer entity. By the same motivation, MAC address can not give any information on higher layer, therfore it is not good as source address. In addition, MAC address has a privacy issue when someone want to track your PAC activity.

## Slide 4: Motion X0: Discovery Source ID
Background
  From offline discussion at Athens among Samsung, ETRI and InterDigital, it is identified that clarification is required on “Source address in Discovery Request Message” from Motion 22 in DCN11-14-0464-03.
  If we want to support 2-way discovery from MAC perspective, higher layer entity should be distinguished in MAC layer.
Proposed Motion
  The contents of “Source address” is “Discovery Source ID”.
  Discovery Source ID is an identification to designate a specific entity in higher layer which triggers transmission of the Discovery Information in Discovery Request message.
  TBD: whether Discovery Source ID is derived from higher layer.
  TBD: method to avoid conflict of Discovery Source ID

## Slide 5: MAC-layer Filtering for Discovery Message
Unfortunately, there was not much discussion on this item.
  [SHP] I think that we don't need pre-filtering for Discovery Request message at MAC layer, because higher layer can do that. MAC layer can not store many # of discovery information for possible pre-filtering. Even though pre-filtering is assumed to be supported, it should consider memory issue and the size of required information.

## Slide 6: Motion X1: MAC-layer Filtering for Discovery Message
If MAC-layer filtering is to be supported, MAC should be designed to consider the followings:
  How to reduce required memory to store many number of Discovery information designated from higher layer
  How beneficial is the filtering to overall discovery procedure to find ‘known’ Discovery information
  Under considerations on typical use-cases such as commercial advertisement and recommendation marketing, ‘unknown’ Discovery information will be major. MAC-layer filtering is only valid to PDs having ‘known’ Discovery information.

## Slide 7: Discovery Resource Selection
From email discussion on this item, we got a procedural sketch to select discovery resource as following:
  Basically random resource selection is used to transmit a discovery signal.
  In addition, the random resource selection should consider congested scenario. It can be achieved by selecting available resources which means resources not collided or occupied.
  Therefore a PD select a discovery resource from available resources which are determined by scanning on discovery resources.
  If there is no available resource, the PD decreases its discovery signal transmission rate per a discovery period to make uncongested resources.

## Slide 8: Motion X2: Discovery Resource Selection
A discovery period comprises multiple Discovery Blocks (DBs).
A PD selects a DB from available DBs in a discovery period, if the PD wants to send Discovery information.
  The available DBs are determined by scanning DBs in a Discovery period.
Congestion control should be considered when there is no available DBs
  TBD: how to avoid from congested situation

## Slide 9: Motion X3: Power Management
???

## Slide 10: Motion X4: Communication Period
Scheduling request period and Scheduling response period are located like one approach from the followings:
  Option 1) Scheduling request/response period are located between Peering period and CAP.
  Option 2) Scheduling request/response period are located between CAP and CFP.
Motion
  Who supports option 1) for the location of Scheduling request/response period?
  If the motion fails, it means option 2) is adopted.