## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Proposed text for frequency channel selection]
Date Submitted: [November 5, 2014]
Source: [Huan-Bang Li1, Marco Hernandez1, Igor Dotlic1, Ryu Miura1, and Qing Li2]
Company [1=NICT, 2=InterDigital]
Address [3-4 Hikarino-oka, Yokosuka, Kanagawa, Japan]
Voice:[+81 468475104], FAX: [:[+81 468475431], E-Mail:[lee@nict.go.jp]
Re: [Proposed text for drafting 15.8 PAC]
Abstract: [proposed text of channel selection procedure for IEEE802.15.8]
Purpose: [This document is to provide a MAC mechanism]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.
<November 2014>

## Slide 2: Proposed Text For Frequency Channel Selection
November 5, 2014

## Slide 3: Proposed Text (1)
    The frequency channel selection shall be performed by higher layers in cooperation with MAC and PHY. Frequency channel selection methodologies might include the following.
    Pre-assigned frequency channel selection at the time of system installation
    Contention based frequency channel selection with CCA. CCA might use energy detection (ED), carrier sensing, or other techniques used for channel measurements and detections.

## Slide 4: Proposed Text (2)
    To minimizing discovery latency, the channel to start discovery procedure should be pre-specified when contention based channel selection is performed. Discovery and emergency message are given the highest priority to use this channel (naming of the channel is TBD: i.e. TBD channel).
    To minimizing discovery latency, it is also desired to specify the order of candidate channel list for discovery if the TBD channel is not available, e.g. reaching its accommodation capacity or failing the required QoS, etc.

## Slide 5: Proposed Text (3)
    When the contention based frequency channel selection is applied in peering procedure, the information of selected frequency channel must be shared among PDs involved in peering.

## Slide 6: Proposed Text (4)
    When contention based frequency channel selection is applied in communication procedure, the information of selected frequency channel must be shared among all joined PDs.
    Channel hopping must be enabled for coexistence purpose. The manner of channel hopping is TBD.
    Communication procedure should have lower priority for using the TBD channel which is primarily for Discovery and emergency messages.

## Slide 7: Motion
Motion: To approve “the proposed text of frequency channel selection for TG8” (DCN: 14-0662-01-0008) and include it in the Standard Draft d05.
      Moved: Huan-Bang Li
      Second:
      Yes:
      No:
      Abstain: