## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [TG8 Security Consideration]
Date Submitted: [November 5, 2014]
Source: Myung Jong Lee [CUNY]
Address Dept of EE, CUNY, 140th St, New York, NY 10031]
Voice:[+1-212-650-7260], FAX: [+1-201-650-8249],
E-Mail:[lee@ccny.cuny.edu]
Re: [.]
Abstract: []
Purpose: [Summary of TG8 PAC security issues by Robert Moskowitz, TG9 Chair]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Security Consideration for TG8
MPDU large enough for KMP 250 minimum. 2048 makes you very IP friendly Consider 802.15.4k sub-mac fragmentation to use small PPDU but large MPDU
Traffic selector
EthType would be nice. Work out subset of which are appropriate
Or 802.15.4e Information Element as used in 802.15.9
Multi-hop 802.1/802.3 MAC-in-MAC as used in Provider Bridging 802.11s 3-address mesh structure 802.15.10 2 address mac forwarding .

## Slide 3: Security Consideration for TG8
On to MACsecurity for TG8 ECDH is your lightest asymetric setup, 'Only' wide multiple needed. First device Identity. 'raw keys' as used in HIP and CoAP for identity Side channel registration as in QRcode reading or Opertunistic admittance (I don't know who you are, but you are you)
n^2 keying for each link keying.
8 bit processors slow on EC operations. Expect 10s but optimization gets it down to 5s and dedicated circuits faster. No issue on 32bit systems.
Group keys still require one EC to join, but also require group key management. Do two devices exhaust their use of the counters, requring rekeying? Member expell and rekey. Frame counter for AES-CCM or GCM. 32bit recommended. CAN be managed with key hierarchy with shorter counters; see 802.1AE.