## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Comment resolutions on the review comments for the letter ballot.
Date Submitted: 21 January, 2014
Source: Chandrashekhar Thejaswi PS, Kiran Bynam and Jinesh Nair
E-Mail: c.thejaswi@samsung.com
Abstract: Comment resolutions.
Purpose: Response to the letter ballot comments.
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
ID | Reviewer | Pg. No | Clause | Ln. No. | Comment | Suggestion | Resolution
1074 | Frederik Beer | 7 | 8.1.2.14 | 16 | The Band 863-876 has only 3 channels, but could serve a lot more. | Adjust number of channels. | Revised
Modifications:
In Table 2 (Pg. 7 ), in the cell corresponding to 5th row (band “863-876 MHz”), and 3rd col.(col. “TotalNumChan”)
replace ‘3’ by ‘5’.
ID | Reviewer | Pg. No | Clause | Ln. No. | Comment | Suggestion | Resolution
1075 | Frederik Beer | 7 | 8.1.2.14 | 16 | Check the 951 Mhz band. I am not sure if it actually goes from 951-958. And the First centerfreq is 951 which is the lower boundary. But then again I am no expert in Japan bands. | Get someone who knows this band. | Revised
Modifications:
In Table 2 (Pg. 7 ), replace the 7th row (band 951-958 MHz) with the following row:
950-956 | 2 | 3 | 951

## Slide 3
ID | Reviewer | Pg. No | Clause | Ln. No. | Comment | Suggestion | Resolution
1281 | James Gilb | 11 | 30 | 2 | No text is allowed to follow a clause title, it must be in a subclause. | Either delete the text as it is unnecessary, move it to another location or add a sub-clause title 30.1 General. | Revised
Modifications:
In Pg. 11, Ln. 2: Immediately after title of the clause 30, insert a new sub-clause 30.1. under the title “General” . In this sub-clause, place the introduction part.
950-956 | 2 | 3 | 951

## Slide 4: Comments on MCS/MFI/CFI
No. | Reviewer | Pg. No | Clause | Ln. no. | Comment | Suggestion | Resolution
1290 | Benjamin A. Rolfe | 12 | 30.1.2.2.3 | 24 | Is a "Modulation Format" exactly the same thing as a "Modulation and Coding Scheme"? Yes it is, and so we should not introduce a new term; use the nomenclature of the standard being amended | Use "Modulation and Coding Scheme" instead of MFI. | Revised
1291 | Benjamin A. Rolfe | 12 | 30.1.2.2.3 | 24 | "The MFI field specifies the type of modulation employed" is not a technically correct or complete description of the field. What you probably mean is that the MFI field indicates the Modulation and Coding Scheme used to encode the PHY Payload (a fact I guessed since the text does not specify to what part of the PPDU the MFI applies to, or even if it applies to the PPDU at all). | Change field name to "Modulation and Coding Scheme" to be consistent with the standard; Change to read "The Modulation and Coding field shall be set to the MCS used to encode the PHY Payload" and specify what MCS is used to encode the PHR. | Revised
1079 | Frederik Beer | 15 | 30.4.2 | 15 | I find the distinction between MCS and Modulation format a little irritating. | Discuss if this can be merged somehow or find more distinctive names. | Revised

## Slide 5: Modifications:
MFI/CFI fields have been merged into a single field MCS. References to MFI/CFI are replaced with MCS.
In Pg. 12, replace Figure 8 with the following figure:
Pg. 12-13, delete sub-clauses 30.1.2.2.3 and 30.1.2.2.4 and create a sub-clause
under the title “MCS field”. Add the following text
“ The MCS field specifies the modulation and the coding scheme applied on the PSDU. There are four modulation formats and two FECs provided. Valid values of the MCS field and the corresponding mapping of the modulation and coding schemes are given in Table 5.”

## Slide 6
In Pg. 13, replace Table 8 with the following table:
Change the caption for table to “Table 5—Mapping of the MCS field”
Delete the sub-clause 30.4.2 and the Table 7.
MCS field | Modulation format | FEC
(0, 0, 0) | 1/1-TASK | BCH
(1, 0, 0) | 2/4-TASK | BCH with interleaving
(0, 1, 0) | 3/8-TASK | BCH with interleaving
(1, 1, 0) | 5/32-TASK | BCH with interleaving
(0, 0, 1) | 1/1-TASK | SiPC
(1, 0, 1) | 2/4-TASK | SiPC
 | Modulation format | FEC
(0, 0, 0) | 1/1-TASK | BCH
(1, 0, 0) | 2/4-TASK | BCH with interleaving
(0, 1, 0) | 3/8-TASK | BCH with interleaving
(1, 1, 0) | 5/32-TASK | BCH with interleaving
(0, 0, 1) | 1/1-TASK | SiPC
(1, 0, 1) | 2/4-TASK | SiPC

## Slide 7
In Pg. 15, sub-clause 30.4.1, replace the entire text with the following text
“MCS specifies the modulation and coding schemes to be applied on the PSDU. In any given frequency band of operation, six modes of MCS (0-5) are defined based on the data rates. When BCH coding applied on the PSDU (i.e., MCS = 0 – 3 ), preamble format P2 and the SFD/PHR spreading format C2 are 5 applied; and when SiPC coding is applied on the PSDU (i.e., MCS = 4, 5), preamble format P1 and the SFD/PHR spreading format C1 are applied. The MCS, preamble formats, spreading formats and corresponding data rates for different frequency bands are provided in Table 7, Table 8 and Table 9. Also, for each modulation format, the parameters such as constellation size (Q), modulation order (M), spreading sequence length (L) are specified. ”

## Slide 8
ID | Reviewer | Pg. No | Clause | Ln. no. | Comment | Suggestion | Resolution
1285 | James Gilb | 14 | 30.2 | 22 | It is almost as if you don't want people to understand this, so it is expressed in the most obtuse manner possible. That or this is an academic research project that no one has thought of implementing as an actual product. | Just have a table that has the bit, 1 or 0, and the corresponding spreading code. All the c's and fancy math notation distract from the description. Plus the figure is essentially useless. | Revised
Modifications:
In Pg. 14, delete Figure 11, and it’s the sentence referring to it in Ln. 22.
Replace Table 6 with the following table
Spreading format | Spreading factor | SFD/PHR bit | Bit –to-sequence mapping
C1 | 4 | 0 | [1 0 0 1]
 |  | 1 | [0 -1 -1 0]
C2 | 8 | 0 | [1 0 -1 0 0 -1 0 1]
 |  | 1 | [0 -1 0 1 1 0 -1 0]

## Slide 9
ID | Reviewer | Pg. No | Clause | Ln. no. | Comment | Suggestion | Resolution
1060 | Kiran Bynam | 23 | 30.5.2.1 | 29 | There is no need for this subtitle, since it is already mentioned in 30.5.2. Also, ensure notation are consistent. Especially, w.r.t. the set C. | merge 30.5.2.1 with its parent subclause,and also omit duplicated sentences. Also maintatin consistency in the notation. | Revised
Modifications:
In Pg. 23, delete sub-clause 30.5.2.1, and the sub-clause 30.5.2.2. Replace the text in 30.5.2 with the following text:
“Ternary sequence spreading is performed by a process of mapping each data symbol to a unique sequence of chips. The mapping is determined by the modulation format specified by the MCS field. The parameters for different modulation formats are given in 30.5. For a modulation format with the constellation size, Q, and the spreading sequence length, L, this stage maps data symbols from to a set of L-length ternary sequences. The following sub-clauses outline the data-symbol-to-chip mapping for different modulation formats.
Chip transmission order: For an L-length chip-sequence,, shall be transmitted first, and shall be transmitted last.”
Change the sub-clauses 30.5.2.1.1 -30.5.2.1.4, to “H4” heading.

## Slide 10
ID | Reviewer | Pg. No | Clause | Ln. no. | Comment | Suggestion | Decision
1288 | James Gilb | 28 | 30.8 | 11 | There is no “baseband signal” in the standard. A compliant implementation is not required to create that baseband signal, only the RF signal is specified. The inclusion of this detail, as with the ASK with negative amplitude (no such thing exists at RF, all amplitude is positive, but it may have a relative phase difference) in the previous subclause cast a shadow on this entire effort. The goal is to create an RF waveform, not a baseband waveform. | Delete the baseband signal representation as it is meaningless. | Revised
Modifications:
In Pg. 28, delete the entire text in the sub-clause 30.8 with the following text:
“ The modulated PPDU signal is represented as
where
are the chips of PPDU
is the chip duration
is the number of chips in the PPDU
is the angular frequency of the carrier
is the random phase. ”

## Slide 11
ID | Reviewer | Pg. No | Clause | Ln. no. | Comment | Suggestion | Decision
1104 | Chandrashekhar Thejaswi PS | 29 | 30.9 | 18 | Appropriately mention the transmit PSD limits in 433 and 470 MHz bands. The bandwidths of the channels in each of these bands are mentioned as 400KHz. | incoporate the change | revised
Modifications:
In Pg. 29, sub-clause 30.9.1,
Replace the Table 18 with the following table:
Replace the sentence in Ln. 22-23 (Pg. 29) with the following sentence:
“For the relative limit, the reference level shall be the highest average spectral power measured within kHz of the carrier frequency.”
Frequency range | Relative limit | Absolute limit
MHz | -20 dB | -20 dBm
Frequency range | Relative limit | Absolute limit
 | -20 dB | -20 dBm

## Slide 12: Comments on FEC/multiple FECs
No. | Reviewer | Pg. No | Clause | Ln. no. | Comment | Suggestion | Decision
1015, 1239, 1301 | Timothy Harrington, James Gilb, M. Lynch | 16 | 30.4.3 | 2 | There is no need to define a new FEC as there are already many defined in 802.15.4. The new FEC does not enable lower power than the existing FECs | Replace the BCH and SiPC with a single FEC from the base standard. | Revised
1298 | Benjamin A. Rolfe | 13 | 30.1.2.2.4 | 3 | Support for 2 FEC schemes adds complexity without clear benefit. Pick a coding method and stick with it. | see comment | Revised
Modifications:
Please see our presentation on FEC

## Slide 13
No. | Reviewer | Pg. No | Clause | Ln. no. | Comment | Suggestion | Decision
1018 | Guido Dolmans | 23 | 30.5.1.2.3 | start 6 - end 11 | Our comment on FEC was rejected in the previous comment form, but we are still in favor of a (9,8)_q single-parity-check (SiPC) code. The SiPC code has simpler encoding complexity (a simple summation over binary bit vectors in GF field). Therefore, it is preferred to be applied in the scenario where the transmitter of the sensor node has really low power and complexity constraints. | add SiPC code | Revised
1019 | Guido Dolmans | 17 | 30.5 | start 2 - end 6 | The proposed SiPC code has comparable code gain and decoding complexity compared to the chosen BCH code. The ‘bit-to-data-symbol’ SiPC block can be reused from the encoding of BCH code (please see figure 12, functional diagram in the draft proposal) such that not too much complexity is added when these two FEC codes are both implemented. | add SipC code | Revised
Modifications:
The comments of this reviewer are essentially the justifications
for the use of SiPC codes.

## Slide 14: Comment resolution: Comments on FEC/multiple FECs
A presentation is prepared to defend the inclusion of two FECS.

## Slide 15: Comments on 5C requirement of distinct identity
No. | Reviewer | Pg. No | Clause | Ln. no. | Comment | Suggestion | Decision
1013, 1237, 1299, | Timothy Harrington, James Gilb, M. Lynch | 11 | 30 | 1 | The draft does not meet the 5C requirement of distinct identity. There are already low power PHYs defined in 802.15.4, the O-QPSK PHY, LRP UWB and BPSK PHY all enable power usuage at or below the proposed TASK PHY. The TASK PHY does not take advantage of ASK modulation (it requires phase coherency in the transmitter) nor is it a constant envelope modulation (e.g., FSK) and so the resulting designs will end up even higher power than the currently defined PHYs. | Delete Clause 9 and references to the ULP TASK PHY. | Rejected

## Slide 16: Resolution
Meets the requirements of PAR, which are unique:
  Support of multiple data rates in the specified bands up to 1Mbps
  Power consumption <15 mW (as per PAR)
Support in the design of ultra low power receivers, like SRR based receivers etc.
Support for both coherent and non-coherent receivers, due to the employment of
spreading based on ternary sequences.
ULP capability of TASK:
  Supports ULP receivers.
  Advanced transmitter designs are available which can ensure ultralow
  power consumption.

## Slide 17: Comments on the co-existence document
No. | Reviewer | Pg. No | Clause | Ln. no. | Comment | Suggestion | Decision
1016 | Steve JILLINGS | - | - | - | 15-14-0565-00-004q Coexistence Assurance Document: No supporting documentation to support coexistence of the TASK PHY with existing 802. PHYs operating in colocated frequency bands | Produce supporting documentation | Revised
1187 | Mike McInnis | 46 | Annex C Bibliography | 2,3, 4 | If the 15-14-0565-00-004q-coexistence-assurance-for-ieee-802-15-4q.docx document is listed in this paragraph as a reference document, the reference document states in paragraph 2 the following 'The Ultra Low Power (ULP) GFSK and ULP TASK Physical Layers defined in amendment 802.15.4q are substantially similar to the Physical Layers defined in amendments 802.15.4k and 802.15.4p. The bands used are a subset of the union of the bands defined in those amendments. The coexistence assurance documents defined for 15.4k and 15.4p provide adequate analysis for 15.4q environment.' if the TG4q ULP TASK and ULP GFSK PHYs are substantially similar to the PHYs defined in amendments 802.15.4k and 802.15.4p then how do the ULP TASK and ULP GFSK differ enough from all previous 802.15.4 PHYs to justify becoming new 802.15.4 PHYs? | Make the appropriate changes to the coexistence document to resolve this issue or proceed no further with the 802.15.4q draft standard. | Revised

## Slide 18: Resolution: Revised
Coexistence document will be prepared for ULP-TASK PHY.