## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [An Initial Proposal of Reference Architecture for TG4s]
Date Submitted: [12 January 2015]
Source: [Shoichi Kitazawa, Masayuki Ariyoshi] Company [ATR]
Address [Hikaridai, Seika, Kyoto JAPAN]
Voice:[+81-774-95-1565], FAX: [], E-Mail:[kitazawa@atr.jp, ariyoshi@atr.jp]
Re: []
Abstract: [This document proposes a reference architecture for TG4s.]
Purpose: [For discussion.]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: An Initial Proposal of Reference Architecture for TG4s
Authors:

## Slide 3: Spectrum Resource Measurement
Spectrum Resource Usage (SRU) information is collected using existing PIBs
MLME and PLME exchanges the SRU information through existing SAPs
MLME may send the SRU information to Next Higher Layer by IE
PHY
MAC
Next Higher Layer
MCPS SAP
MLME SAP
PD SAP
PLME SAP
RF SAP
MLME
MAC PIB
MAC Command
part sublayer
PLME
PHY PIB
MCPS:MAC Common Part Sublayer
MLME:MAC Layer Management Entity
PD: PHY Data
PLME: Physical Layer Management Entity
PIB: PAN information base

## Slide 4: A Possible Procedure for Spectrum Resource Measurement and Management
The Network Manager (NM) requests the measurement of the SRU information to Pico Net Controllers (PNC).
Each PNC collects the SRU information from attached Devices and report them to the NM.
Based on the collected SRU information, the NM may perform network management (including a management for efficient spectrum resource usage).
PNC1
Network Manager
Device
PNC1
Device
PNCn
Device
Types of PIBs and IEs used for SRMM to be defined

## Slide 5
802.15.4
Coordinator
802.15.4
Coordinator
802.15.4
Coordinator
Radio resource contention will be occur
between different piconet
Detecting spectrum resource usage and notifies to the management entity.
TG4s aims at building a standard to specify MAC framework for exchanging information on SRU.
The Network Manager
controls PHY/MAC parameter based on spectrum resource usage.
Network manager
General use case

## Slide 6: Example of SRU related PHY PIBs
Attribute | Type | Range | Description
phyCurrentChannel | Integer | As defined in 10.1.2 | The RF channel to use for all following transmissions and receptions, 10.1.2.
phyCCAMode | Integer | 1–6 | The CCA mode, as defined in 10.2.7.
phyCurrentPage | Integer | Any valid channel page | This is the current PHY channel page. This is used in conjunction with phyCurrentChannel to uniquely identify the channel currently being used.
phyCCADuration | Integer | 0-1000 | The duration for CCA, specified in symbols for PHYs operating in the 920 MHz band.