## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Metrics used in some Wireless Sensor Network standards]
Date Submitted: [12 March, 2015]
Source: [Mitsuru Iwaoka] Company [Yokogawa Electric Corp.]
Address [2-9-32 Nakacho, Musashino-shi, Tokyo, 180-8750, Japan]
Voice:[+81-422-52-5519], FAX: [+81-422-52-6975], E-Mail:[mitsuru.iwaoka.1961@ieee.org]
Re: [15-14-06570-00 “Call for Contributions”]
Abstract: [This submission describes a set of Metrics that are used in some Wireless Sensor Network standards (ISA100.11a and WirelessHARTTM) as a candidate for measurement items of 802.15.4s.]
Purpose: [To support the creation of Technical Guidance Document in IEEE802.15.4s.]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Metrics used in some Wireless Sensor Network standards
Mitsuru Iwaoka
Shusaku Shimada
R1: Correct measurement table

## Slide 3: Preface
Some Wireless Sensor Network (WSN) standards (ISA100.11a and WirelessHARTTM) provide a set of metrics for:
  Network health monitoring
  Link health monitoring
  Device health monitoring
Some of these metrics are also useful for other 802.15.4 based networks.
802.15.4s SRU should support a subset of these metrics.

## Slide 4: Summary of Metrics
Metrics | Network | Link | Ch. | Device
Number of joins to the network |  |  |  | 
Latency |  |  |  | 
Number of packets transmitted |  |  |  | 
Number of packets received |  |  |  | 
Number of failed transmission (No Ack) |  |  |  | 
Percentage of time of failed transmissions (No Ack) |  |  |  | 
Number of deferred transmission (CCA) |  |  |  | 
Percentage of time of deferred transmissions (CCA) |  |  |  | 
Number of failed reception (CRC error) |  |  |  | 
Received signal level (RSSI) |  |  |  | 
Received signal quality indicator (RSQI) |  |  |  | 
Average / Maximum Buffer Utilization |  |  |  | 
Security |  |  |  | 

## Slide 5: Metric: Throughput
Throughput is not directly measured
Number of successfully transmitted packets are measured periodically.
  Throughput is estimated by
    Num. of successfully Tx packets / interval

## Slide 6: Metric: Latency
Two types of latency metric are used:
  The percentage of scheduled packets that arrive later than expected.
    These packets may be delayed due to delivery over secondary paths or due to congestion in intermediate devices.
  Latency is computed from the packet timestamp and the time of packet reception
    Each packet receives a timestamp when it is put in the transmit buffer
    Standard deviation of latency (jitter) is also computed
Time synchronization is necessary (e.g. TSCH)

## Slide 7: Metric: Security
Link level MIC error counter
Network level MIC error counter
Network level failed join counter

## Slide 8: Metric: RSSI/RSQI
RSSI is reported as a signed 8-bit integer, reflecting an estimate of received signal strength in dBm.
  RSSI reports may be biased by +64 dBm to give an effective range of -192 dBm to +63 dBm.
RSQI is reported as a qualitative assessment of signal quality, with higher number indicating a better signal.
  1..63 indicates a poor signal
  64..127 a fair signal
  128..191 a good signal
  192..255 an excellent signal.
  0 indicates that the chipset does not support any signal quality diagnostics other than RSSI.

## Slide 9: Network / Link / Device
A gateway accumulate measurement of each link to calculate network level metrics.
Each device provides link level and channel level measurements of metrics.
Propose to support Link and channel level metrics in 802.15.4s.