## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Multi-hop transmission in CAP/CFP periods
Date Submitted: Jan. 2015
Source: [Woongsoo Na, Sungrae Cho]
Company: [Chung-Ang University, Korea]
Address:
E-Mail: [wsna@uclab.re.kr, srcho@uclab.re.kr)
Re: P802.15.8 Draft D0.6
Abstract: Multi-hop transmission in CAP/CFP periods.
Purpose: Approval.
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Multi-hop transmission in CAP/CFP Periods
Jan. 2015
Woongsoo Na (Chung-Ang University)

## Slide 3: Contents
Description of Multi-hop transmission in CAP period (Unicast)
Decripition of Multi-hop transmission in CAP period (Multicast)
Description of Multi-hop transmission in CFP period (Unicast)
Decripition of Multi-hop transmission in CFP period (Multicast)

## Slide 4: Unicast Multi-hop Data Transmission in CAP (Unicast)
A PD can transmit data frame in CAP.
A source PD waits random time period and transmits data frame If channel is idle.
If a relay PD receives multi-hop data frame from neighbor, it also waits random time and transmits data frame in CAP period.

## Slide 5: Unicast Multi-hop Data Transmission in CAP (Multicast (or groupcast))
A PD can transmit multicast data frames in CAP.
A source PD waits random time period and transmits multicast data frame if channel is idle.
If a relay PD receives multi-hop data frame from neighbor, it checks the source of received frame is same multicast group or not.
If the source is same multicast data frame, it also waits random time and transmits data frame in CAP period.
Otherwise, it does not transmit anything.

## Slide 6: Unicast Multi-hop Data Transmission in CFP (Unicast)
A PD can transmit data frame in CFP.
A source PD determines a relay PD and transmits candidate RSs to its neighbors including the relay PD.
The receiver replies scheduling resource to TXPD based on resource information and determines another relay PD.
Again, the receiver transmits candidate RSs to another relay PD.
It continues until destination PD is scheduled.

## Slide 7: Unicast Multi-hop Data Transmission in CFP (Multicast (or groupcast))
A PD can transmit data frame in CFP.
A source PD determines a relay PD and transmits candidate RSs to its neighbors including the relay PD.
The receiver replies scheduling resource to TXPD based on resource information and determines another relay PD.
Again, the receiver transmits candidate RSs to another relay PD.
It continues until all multicast group members are scheduled.