## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Reliable data transmission
Date Submitted: Jan. 2015
Source: [Woongsoo Na, Sungrae Cho]
Company: [Chung-Ang University, Korea]
Address:
E-Mail: [wsna@uclab.re.kr, srcho@uclab.re.kr)
Re: P802.15.8 Draft D0.6
Abstract: Reliable data transmission.
Purpose: Approval.
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Reliable data transmission
Jan. 2015

## Slide 3: Reliable data transmission
MAC multicast in P2P environments may not need each receiver to perform retransmission-based reliability for each multicast MAC frame.
Based on ACK Type, different levels of multicast data transmission reliability could be achieved.

## Slide 4: ACK-Type (Full ACK, Partial ACK)
      Full ACK
        All destination PDs in the multicast group should send acknowledgement, referred to as Full ACK.
        To resolve the ACK implosion problem, Block-ACK, pre-ACK, Selectively ACK schemes can be considered.
Partial ACK
        Only a portion of destination PDs need to send back an ACK, referred to as Partial ACK.

## Slide 5: ACK-Type (Any ACK, Location-based ACK)
Any ACK
  ACK is only required from any one of destination PDs in the multicast group. The source PD may multicast new packets only after receiving ACKs from any destination PD in the multicast group or the maximum number of retransmissions for a packet is violated.
Location-based ACK
  Only destination PDs that are around a location need to send back an ACK, referred to as Location-based ACK

## Slide 6: ACK-Type (Context-based ACK, Information-based ACK)
      Context-based ACK
        Only destination PDs that have certain preconfigured context information need to send back an ACK, referred to as Context-aware ACK. Context information such as mobility can be leveraged to decide if an ACK is needed or not.
      Information-based ACK
  The source PD should indicate if an ACK is required 1) for each packet, 2) just for some packets, or 3) just when intended information such as a command or an event is fully decoded