## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Proposed Spectrum Resource Measurement Report Structure]
Date Submitted: [15 January 2015]
Source: [Mineo Takai] Company [Space-Time Engineering]
Address [Rolling Hills Estates, CA 90274, USA]
Voice:[+1-310-541-1360], FAX: [], E-Mail:[mineo@ieee.org]
Re: []
Abstract: [This document proposes a spectrum resource measurement report structure.]
Purpose: [For discussion.]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Proposed Spectrum Resource Measurement Report Structure
Authors:

## Slide 3: SRM requests by Spectrum Resource Management Entity
Spectrum Resource Management Entity (SRME) may send Spectrum Resource Measurement (SRM) requests to its registered networks in order to better understand current spectrum resource usage for its effective spectrum management.
802.15.4
Coordinator
802.15.4
Coordinator
Spectrum Resource Management Entity (SRME)
SRM Request
SRM Report

## Slide 4: Two different types of SRM requests
Periodic (including one-time): An SRM report is to be sent at the time specified in the SRM request, and then periodically when the reporting interval is specified in the request.
Conditional: An SRM report is to be sent when conditions specified in the SRM request are met.
Both types of SRM request should include metric(s) to be measured, and optionally the measurement interval.

## Slide 5: Proposed SRM report structure
SRM report header should include at least the following:
  Reporting device ID
  Measurement time
  Number of measurements included in the report
SRM report payload can include multiple pairs of measurement metric type and value as long as those measurements were performed by the same device at the same time.
All the measurement metric types and the details (precision, unit etc.) of their associated value(s) are to be defined in TG4s.
Header
Type
Value
Type
Value
Type
Value
…