## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Fully Distributed Synchronization Scheme for PAC with Additional Simulations
Date Submitted: March 2015
Source: [Byung-Jae Kwak, Moon-Sik Lee]1,
[Junhyuk Kim, Kyounghye Kim, Nah-Oak Song, June-Koo Kevin Rhee] 2
Company: [ETRI, Korea] 1, [KAIST, Korea]2
Address:
E-Mail: [bjkwak@etri.re.kr, moonsiklee@etri.re.kr] 1,
[kim.jh@kaist.ac.kr, khye.kim@kaist.ac.kr, nsong@kaist.ac.kr, rhee.jk@kaist.edu]2
Re: P802.15.8 Draft D0.8
Abstract: Presents additional simulation result of the proposed fully distributed synchronization scheme for PAC to address comments from Jan. 2015 meeting..
Purpose: Approval.
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Fully Distributed Synchronization Scheme for PAC with Additional Simulations
March. 2015

## Slide 3: Introduction
P802.15.8/D0.8 still has an incomplete description of fully distributed synchronization scheme (e.g., phase update rule)
Proposal 15-15-0053-02-000 was not accepted during Jan 2015 meeting
  “No evidence that 180o rule is optimum.”
  More comparison needed: e.g., 90o rule, 270o rule, etc.
  See minutes for more info.: 15-15-0099-00-0008

## Slide 4: A Brief Recap of Phase Update Rules
Convex curve
  Used in the original firefly sync. scheme
  Two parameters
    b: convexity (the larger, the stronger)
    : coupling

## Slide 5: A Brief Recap of Phase Update Rules
  180o rule
    Simple
    No parameters to optimize
    Rationale behind 180o rule
      Mimic the convex curve
      with exaggerated behavioral change
      to make it work for PAC (random access transmission of sync signals)

## Slide 6: A Brief Recap of Phase Update Rules
  360o rule
    Only natural to ask:
    “Why not 360o rule?”
    Also
      Simple
      No parameters to optimize
    See simulation results

## Slide 7: A Brief Recap of Phase Update Rules
  90o rule & 270o rule
    How do you know 180o is the best?
    More variations of the same concept
90o rule
270o rule

## Slide 8: A Brief Recap of Phase Update Rules
  Do we have to test all possible degrees?
    No!
    See the discussion in the following slides

## Slide 9: Simulation Results: Initial Sync. (1/3)
Comparison of 5 rules for updating oscillator phase
  Convex curve [Mirollo 1990]
  90o rule
  180o rule
  270o rule
  360o rule
[Mirollo 1990] R. E. Mirollo, S. H. Strogatz, “Synchronization of pulse-coupled biological oscillators,”
SIAM J. Appl. Math., vol. 50, no. 6, pp. 1645-1662, Dec. 1990.

## Slide 10: Simulation Results: Initial Sync. (2/3)
Convex curve simulation results (Source: 15-15-0053-0x-0008)
  1000 PDs in 500m x 500m area (random clustered drop)
  Average of 30 independent runs
  Discussion
    Small coupling (=0.05~0.1) gives better performance in multi-hop networks (end-to-end: about 10 hops)
    But, in small networks, large coupling gives better performance [Tyrrell 2009]
    Need to be optimized for a particular scenario
 | =0.01 | =0.03 | =0.05 | =0.1 | =0.3 | =0.5 | =0.7
b=1 | 162.6 | 133.7 | 95.4 | 88.3 | 130.7 | 430.4 | 517.8
b=1.2 | 182.9 | 97.7 | 88.2 | - | - | - | -
b=4 | - | - | - | 192.6 | 535.7 | 1085.2 | 1380.5
b=7 | - | - | - | 184.2 | 1030.2 | 1629.1 | 1337.2
Table: Mean #frame to synchrony
[Tyrrell 2009] Alexander Tyrrel, “Firefly Synchronization in Wireless Networks,” Ph.D. Thesis,
Department of Engineering Science, University of Klagenfurt, Austria, July 2009.

## Slide 11: Simulation Results: Initial Sync. (3/3)
90o rule, 180o rule, 270o rule, & 360o rule
  1000 PDs in 500m x 500m area (random clustered drop)
  Average of 100 independent runs
# frames to synchrony | 90o rule | 180o rule | 270 o rule | 360o rule
Mean | 153.65 | 51.68 | 2816.59 | 6428.91
Std. deviation | 400.04 | 28.76 | 3672.88 | 6712.29
Converged? | Yes | Yes | 99 out of 100 | 96 out of 100
Min | 33 | 20 | 22 | 455
Max | 3917 | 178 | 26073 | 29106

## Slide 12: Simulation Results: Network Merge (1/5)
Definitions
  A PAC network is a set of PDs, any two PDs of which can exchange data or control messages with each other either directly or through a multi-hop relay route.
  Two networks “meet” when one or more PDs in one network can communicate with one or more PDs in another network directly or through a multi-hop relay route.
    Two networks can meet each other when the networks move, or any obstacle separating the two networks is removed.
    In general, when two networks meet, the reference timing of the two networks are different and they will interferer with each other.
  When two PAC networks meet, the two networks are merged or synchronized by making the PDs in the two networks have the same reference timing.

## Slide 13: Simulation Results: Network Merge (2/5)
Network merge scheme
  Detection: PDs in Net 1 & Net 2 detect Net 2 & Net 1
  Indication: PDs indicate the “detection” in the synchronization signal (to wake up PDs in sleep mode)
  Move (consistent with 180o rule):
    If T1 < T2, PDs in Net 2 move to Net 1: 180o rule
    If 3*T1 < T2, PDs in Net 2 move to Net 1: 90o rule
    If T1 < T2*3, PDs in Net 2 move to Net 1: 270o rule
  Complete
    After all PDs move

## Slide 14: Simulation Results: Network Merge (3/5)
The scenario
  2 PAC networks: blue: 100 PDs in 50m radius; red: 1000 PDs in 250m radius
  Average of 100 independent runs: (10 drops) x (10 runs / drop)
Random relative phase between two networks
Clustered random drop
Edge distance: 30m
Tx range: 56m

## Slide 15: Simulation Results: Network Merge (4/5)
90o rule, 180o rule, 270o rule, & 360o rule
  1000 PDs in 500m x 500m area (random clustered drop)
  Average of 100 independent runs
# frames to synchrony | 90o rule | 180o rule | 270o rule | 360o rule
Mean | 11.441) | 12.222) | 368.07 | 859.17
[Min, Max] | [1, 26] | [2, 26] | [2, 9445] | [19, 10983]
Std. deviation | 7.50 | 7.99 | 1354 | 1932
1) Only 47 out of 100 merged successfully. (20: Net 1  Net 2, 27: Net 1  Net 2)
2) 49: Net 1  Net 2, 51: Net 1  Net 2
Note: If convex curve was used, mean = 248.867 and Std. deviation = 10.373

## Slide 16: Simulation Results: Network Merge (5/5)
What’s up with 90o rule & 360o rule?
  90o rule
    Did not work half of time (53 out of 100)
    If the phase difference between the two networks is 90o ~ 270o, they ignore each other.
    The similar situation is true for other angles smaller than 180o
  270o rule: suffer from Ping-Pong effect as 360o rule does

## Slide 17: Review of the Proposed Text

## Slide 18: Motion
“Move to accept the text proposal included in 15-15-0191-02-0008 to be accepted into P802.15.8 Draft Std. D0.8.”
Mover: BJ
Second:
Result: Yes/No/Abstain =