## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Leaving procedure of group for PAC]
Date Submitted: [March 10th, 2015]
Source: [Woongsoo Na and Sungrae Cho]
Company: [Chung-Ang University, Korea]
E-Mail: [wsna@uclab.re.kr srcho@cau.ac.kr]
Re: [This is the original document]
Abstract: [Leaving procedure of group for PAC]
Purpose: [To introduce proposed leaving procedure for PAC]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
Leaving Procedure of Group for PAC

## Slide 3: Leaving Group (1/5)
There are several reasons for a PD to leave from the network: (1) by its intention, (2) by mobility, (3) by limited resources.
If a PD wants to leave from a group, it multicasts (within K-hop) a MGNF with notification type set to 2. A recipient of MGNF may send rekeying messages to valid group members for forward secrecy.
  Upon receiving the MGNF, a forwarding PD deletes the entry of the originator of the MGNF, and forward the MGNF.
  Upon receiving the MGNF, a non-forwarding PD deletes the entry of the originator of the MGNF, but does not forward the MGNF.

## Slide 4: Leaving Group (2/5)
If PD C wants to leave from a group, it multicasts a MGNF with notification type set to 2.
<PD C’s Group Table >
Destination Address | ……
D | ……
A
B
C
D
: Multicast Group Notification Frame
<PD A’s Group Table>
Destination Address | ……
D | ……
<PD D’s Group Table>
<PD B’s Group Table>
Destination Address | ……
A | ……
C | ……
Destination Address | ……
A | ……
C | ……
D | ……

## Slide 5: Leaving Group (3/5)
  B receives the MGNF from C and deletes the entry of the originator of the MGNF, and forward the MGNF.
<PD C’s Group Table>
Destination Address | ……
D | ……
A
B
C
D
<PD A’s Group Table>
Destination Address | ……
D | ……
<PD D’s Group Table>
<PD B’s Group Table>
Destination Address | ……
A | ……
C | ……
Destination Address | ……
A | ……
C | ……
D | ……
: Multicast Group Notification Frame

## Slide 6: Leaving Group (4/5)
PD D receives the MGNF and it deletes the entry of the originator of the MGNF.
<PD C’s Group Table>
Destination Address | ……
D | ……
A
B
C
D
<PD A’s Group Table>
Destination Address | ……
D | ……
<PD D’s Group Table>
<PD B’s Group Table>
Destination Address | ……
A | ……
C | ……
Destination Address | ……
A | ……
D | ……
: Multicast Group Notification Frame

## Slide 7: Leaving Group (5/5)
Finally, PD C leaves the group.
A
B
C
D
<PD A’s Group Table>
Destination Address | ……
D | ……
<PD D’s Group Table>
<PD B’s Group Table>
Destination Address | ……
A | ……
Destination Address | ……
A | ……
D | ……
: Multicast Group Notification Frame

## Slide 8: Flow Chart - Leave Scenario
PD 1
PD 2
PD 3
Group Leave Request (Send MGNF (Type = 0))
Group Join Reply (Send ARCF)
Forward MGNF (Type = 0)
PD 1 Leave The Group
Reply ACK
Link Break