## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [How to support mobility for the group in PAC]
Date Submitted: [March 10th, 2015]
Source: [Woongsoo Na and Sungrae Cho]
Company: [Chung-Ang University, Korea]
E-Mail: [wsna@uclab.re.kr srcho@cau.ac.kr]
Re: [This is the original document]
Abstract: [How to support mobility for the group in PAC]
Purpose: [To introduce proposed mobility supporting features for PAC]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
Mobility Supporting for Group in PAC

## Slide 3: Mobility Support for Group (1/4)
Previously, B was 2-hop away from A.
If B moves within the one-hop coverage of A, both of A and B are aware of each other within the one-hop by MGNF’s TTL and update their routing table.
Then, A or B sends a MGNF (notification type = 6) to C.
When C receives that MGNF, C is aware that A and B become closer.
  If C is a group member, it does not do anything.
  If C is a forwarding PD, it deletes group entries whose destination field is A and B.
B
A
A
C
B
Multicast Group Notification Frame
Move

## Slide 4: Mobility Support for Group (2/4)
Since expiration timer is proportional to the number of hops from the impaired PD, the closest multicast group member detects link breakage.
A PD starts local repair if it detects link breakage between multicast group members (due to expiration timer).
Then, the PD multicasts MGNF (notification type = 7) .
If PDs receiving the MGNF create routing entry of originator of the MGNF during Tw .
Then the PD performing local repair broadcasts an ACF within K-hop coverage.
Link
Break
PD
Disappear
Link
Break
Local
Repair
Start
Local
Repair
Start
Advertisement Command Frame

## Slide 5: Mobility Support for Group (3/4)
If a PD receiving the ACF then It compares the receiving frame’s Device Group ID & Application type ID & Application-specific ID & Application-specific group ID with its own.
  If they all are same, it finds entry the originator of the ACF in its routing table. And it found the entry then check the expiration timer.
  If the expiration timer is less than Tm then replies an ARCF to the PD sending the ACF. (Tm is threshold time to decide reply)
  In other case, the PD receiving the ACF does not reply.
  If any of them is not same, it decrements the TTL of the ACF and forwards the ACF.
Local repair &
merging groups.

## Slide 6: Mobility Support for Group (4/4)
Find/join procedure by using ACFs and ARCFs can help merging disjoint groups.
  If a PD in a group receives a ACF from different disjoint group with the same Device Group ID & Application type ID & Application-specific ID & Application-specific group ID, it can initiate merging process.
  The PD then replies to the ACF originator with ARCF.
  Then, these two disjoint groups are merged by Device ID Creation Scheme.
Local repair by using ACFs and ARCFs also can help merging disjoint groups.
  Each group member performs local repair periodically during TL (long duty cycle) in order to merge disjoint groups.

## Slide 7: Flow Chart - Local Repair
PD 1
PD 2
PD 3
PD 2 Disappear
Send ACF
Link is Broken
Reply ARCF
PD 1 detects the link broken (due to MGNF (Type = 1))
New Link is established
Send MGNF (notification type = 7) .