## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Overview Text for IEEE 802.15 TG8 PAC
Date Submitted: March 2015
Source: Byung-Jae Kwak, Gyung-Chul Sihn, Moon-Sik Lee
Company: ETRI, Korea
Address:
E-Mail: bjkwak@etri.re.kr, neuro@etri.re.kr, moonsiklee@etri.re.kr
Re: P802.15.8 Draft D0.8
Abstract: Overview text for IEEE 802.15.8 PAC Draft Std.
Purpose: Approval.
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Introduction
Base document: P802.15.8/D0.8
Existing text: black
New text: red

## Slide 3
---- Beginning of text ----
1. Overview
1.1 General
Peer aware communications (PAC) networks are wireless personal area networks (WPAN) used for direct communication among PDs. Unlike conventional wireless networks, PAC uses fully distributed coordination and connections effected via PAC involve no infrastructure. This feature allows efficient direct communication among PDs to support wide range of peer to peer communication scenarios.
1.1 1.2 Scope
This standard defines physical layer (PHY) and medium access control (MAC) sublayer specifications for Wireless Personal Area Networks (WPAN) Peer Aware Communications (PAC) optimized for peer to peer and infrastructure-less communications with fully distributed coordination. PAC features include:
- Discovery for peer information without association
- Discovery signaling rate typically greater than 100 kbps
- Discovery of the number of PDs in the network
- Scalable data transmission rates, typically up to 10 Mbps
- Group communications with simultaneous membership in multiple groups
- Relative positioning
- Operational in selected globally available unlicensed/licensed bands below 11 GHz
- Multi-hop relay
- Security
(continued on next page)

## Slide 4
(continued from previous page)
1.2 1.3 Purpose
The standard provides for scalable, low power, and highly reliable wireless communications for emerging services such as social networking, advertising, gaming, streaming, and emergency services.
Multiple PHYs are defined to support a variety of frequency bands and requirements
2. Normative references
---- End of text ----

## Slide 5: Motion
“Motion to accept the overview text in 15-15-0236-01-0008 to be added to P802.15.8 Draft Std. D0.8.”
Mover:
Second:
Result: Yes/No/Abstain =