## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Introduction to 802.11 Association Procedure
Date Submitted: March 2015.
Source: Jae Seung Lee, Byung-Jae Kwak, Moon-Sik Lee
Company: ETRI
Address: 218 Gajeong-ro, Yuseong-gu, Daejeon, 305-700, Korea
Voice: +82-42-860-1326
FAX:
E-Mail: [jasonlee@etri.re.kr, bjkwak@etri.re.kr, moonsiklee@etri.re.kr]
Re: P802.15.8 Draft D0.8
Abstract: Introduction material about 802.11 Association Procedure.
Purpose: Informational.
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Introduction to 802.11 Association Procedure
March 2015

## Slide 3: Introduction
Efficient association procedure should be defined for PAC
This document introduces association procedures of 802.11 to help design PAC association procedures

## Slide 4: 802.11 Initial Link Setup Overview
Initial link setup includes all operations required to enable packets exchange:
  Network & BSS discovery
  Authentication & association
  Higher layer setup (such as IP address configuration)
 | BSS Discovery* | Network Discovery | Authentication & Association* | Higher Layer Setup* (DHCP / IP)

## Slide 5: BSS Discovery (1/2)
A station becomes aware of the existence of a BSS
through scanning
  passively seeking Beacon transmissions or
  actively probing for the existence of an AP through a Probe
  Request /Response exchange
Passive Scanning
  The AP in an infrastructure BSS periodically broadcasts Beacon frames
  The Beacon frame carries regulatory information, capability information and information for managing the BSS

## Slide 6: BSS Discovery (2/2)
Active Scanning
  A STA actively probes for the existence of an AP through
  a Probe Request /Response exchange
  An AP that receives a broadcast Probe Request sends
  a Probe Response to the station making the request

## Slide 7: Network Discovery
802.11u has been developed to provide network selection and Generic Advertising Service (GAS)
802.11u defines protocols for network selection, including the 802.21 protocol, multiple SSID query for faster scanning, and network type identification
Discovery of suitable networks is possible through the advertisement of access network type, roaming consortium and venue information, via management frames
Source: IEEE 802.11 11-11-1499r0

## Slide 8: Association
Before a STA is allowed to send data via an AP it must become associated with the AP
Association provides a mapping between the STA and AP that allows messages within the DS to reach the AP with which the STA is associated and ultimately to the station itself
Association is initiated by the STA with the STA sending an Association Request to the AP
If the STA is admitted, the AP responds with an Association Response
The STA and AP exchange capability information (support for optional features) and the AP informs the STA of specific operating parameters within the BSS

## Slide 9: Authentication
Open System authentication admits any STA to the DS
RSNA supports authentication based on IEEE Std 802.1X-2004 after Open System authentication
IEEE 802.1X authentication utilizes the EAP to authenticate STAs and the Authentication Server with one another

## Slide 10: Higher Layer Setup
Higher Layer Setup is required to establish IP layer connectivity
DHCP is used for IP configuration
Outside the scope of IEEE 802.11

## Slide 11: Initial Link Setup Procedure
Beacon with 802.11u Interworking IE
Probe Request
Probe Response
GAS Initial Request
GAS Initial Response
GAS Comeback Request
GAS Comeback Response
802.1X (EAPOL-Start)
802.1X (EAP-Identity Request)
802.1X (EAP-Identity Response)
802.1X (EAP-Auth. Exchange)
RADIUS (EAP-Auth. Exchange)
RADIUS (Access-Accept)
802.1X (EAP-Success)
- Network Discovery (Defined by 11u)
ANQP provides Network Information
STA selects network using the information
Association Request/
Response
AAA Server
AP
Authentication (null)
Authentication Response
Association Request (SSID)
Association Response (AID)
4-Way Handshake (PTK, GTK)
STA
BSS Discovery
(Passive Scanning or Active Scanning)
Open Authentication
802.1x EAP Authentication
4-way handshake
(Pairwise and Group Key establishment)

## Slide 12: 802.11ai (FILS) Overview
TGai focuses on reducing the time spent in any phase of the initial link set-up
FILS focuses on an environment where mobile users are
constantly entering and leaving the coverage area
of an existing extended service set (ESS)
  Every time the mobile device enters an ESS, the mobile
  device has to do an initial link set-up.
  This requires efficient mechanisms that:
    (a) scale with a high number of users simultaneously entering an ESS
    (b) minimize the time spent within the initial link set-up phase
    (c) securely provide initial authentication

## Slide 13: 11ai Scanning Enhancement
More control to scanning procedures:
  Terminating the on-going scanning
  More reporting options of the scanning result
  Immediate reporting
  Reporting after a channel is scanned
  Legacy: reporting after scanning is completed
Announcing one or more neighbor BSS or channel
information in Beacon, Probe Response and
Fast Discovery (FD) frame
  Reduce chances of scanning channels with no AP
  BSSID of neighbor AP enables more precise active scanning
  More information on neighbor BSSs may be provided
Source: IEEE 802.11-13/1325r5

## Slide 14: 11ai Active Scanning Enhancement (1/2)
More control to scanning procedures:
One Probe Response may contain information of
multiple APs
  The total number of Probe Request and Probe Responses is
  reduced
STA 1
Probe
Request
Ch 1
Ch 6
Request for
information of other BSSs
AP1
AP2
AP3
STA 1
Probe Response + Neighbor List
Contains information of itself (AP 2), as well as AP 1 and AP 3 of Channel 1 and
Channel 6
Cn 1
Ch 6
AP1
AP2
AP3
Source: IEEE 802.11-13/1325r5

## Slide 15: 11ai Active Scanning Enhancement (2/2)
Probe Request contains criteria to responding Probe
Response from the AP
  Response is transmitted by the AP only if the criteria is met to reduce unnecessary Probe Responses
  Criteria include:
    STA’s preference on AP’s capability (E.g, STA prefers only HT or VHT Aps)
    Reception power
    AP’s channel access delay, STA’s QoS requirement, etc
STA 1
Probe Request
Specify criteria on responding Probe
Response
to APs
AP1
AP2
AP3
STA 1
Probe
Response
Probe
response
is transmitted
if all the criteria are met
AP1
AP2
AP3
Source: IEEE 802.11-13/1325r5

## Slide 16: 11ai Passive Scanning Enhancement
FILS Discovery (FD) frame: short beacon frame for fast discovery of APs
  FD frame is transmitted between Beacon frames for a fast AP/Network discovery
  FD frame may be transmitted as a non-HT duplicate PPDU, enabling a larger channel than 20MHz
Payload of FD Frame
Primary
channel of the transmitter
Preamble
Payload of FD Frame
Payload of FD Frame
Payload of FD Frame
Preamble
Preamble
Preamble
T2
time
Example #1
T1
time
T3
time
Example #2
Example #3
Beacon
FD frame
Source: IEEE 802.11-13/1325r5

## Slide 17: Concurrent Higher Layer Setup
Significant reduction in setup signaling
  Authentication, 4-way handshake, Association, Higher layer setup
  (including IP address assignment) completed in 2 roundtrip
  signaling messages
Fast authentication & FILS IP address assignment speeds up the
authentication & IP Address assignment procedure

## Slide 18: Reduced Overhead by piggy back
Piggy-backing info along FILS authentication protocol:
  Higher-layer setup, including IP address assignment
  Authorization functionality, subscription credentials, etc.
STA
AP
Association Request
Beacon/Probe Resp.
Authentication Request
Authentication Response
Association Request
Key
Establishment
Key
Confirmation
TTP
Services
+ piggy-backed info response
+ piggy-backed info request
Authentication help
Configuration help
IP address assignment
Authorization
Subscription
credentials
Source: IEEE 802.11-13/1325r5

## Slide 19: Brief Overview of WiFi P2P (1/4)
Wi-Fi Direct is a P2P technology defined by the Wi-Fi Alliance
  aimed at enhancing direct device to device communications in Wi-Fi
  builds upon the IEEE 802.11 infrastructure mode
    inherits QoS, power saving, and security mechanism from 802.11 infrastructure mode
  Devices negotiate who will take over the AP-like functionalities
  legacy Wi-Fi devices may seamlessly connect to Wi-Fi Direct devices

## Slide 20: Brief Overview of WiFi P2P (2/4)
P2P Group is similar to an infrastructure BSS with a P2P Group Owner assuming the role of the AP and a P2P Client assuming
the role of the STA
  A legacy device may also join as a STA
A P2P Device supports both Group Owner and Client roles
Topology [6]:
1:1 | 1:n | Concurrent Operation
 | . | 

## Slide 21: Brief Overview of WiFi P2P (3/4)
When two P2P devices discover each other, they negotiate their roles to establish a P2P Group
  P2P Client, P2P GO (Group Owner)
Once the P2P Group is established, other P2P Clients can join the group as in a traditional Wi-Fi network
  Legacy clients can also communicate with the P2P GO
  Legacy 802.11 STAs see the P2P GO as a traditional AP

## Slide 22: Brief Overview of WiFi P2P (4/4)
P2P GO
  announces itself through beacons
  runs a DHCP server to provide P2P Clients with IP addresses
Only the P2P GO is allowed to cross-connect the devices in its P2P Group to an external network
  e.g., a 3G network, infrastructure WLAN
Wi-Fi Direct does not allow transferring the role of P2P GO within a P2P Group
  If the P2P GO leaves the P2P Group, then the group is torn down, and has to be reestablished

## Slide 23: Example of Wi-Fi Direct topologies
Source: [7]

## Slide 24: Initial Link Setup Procedure for WiFi P2P
P2P Standard Group formation [7]
WPS Provisioning

## Slide 25: Standard Group Formation
Discovery Phase
  P2P devices discover each other
  First, 802.11 Scanning is used to discover existing P2P Groups
  Next, performing probe request/probe response for device discovery
  GAS query can be used
GO Negotiation Phase
  negotiate which device will act as P2P GO, and on the channel where the group will operate on
  P2P devices send a GO Intent value
  the device declaring the highest value becomes the P2P GO

## Slide 26: Autonomous Group Formation
P2P Autonomous Group formation [7]
A P2P Device becomes the P2P GO, by starting to transmit beacons
Other devices discover the group using scanning
Discovery phase is simplified
No GO Negotiation phase

## Slide 27: Persistent Group Formation (1/2)
P2P Persistent Group formation [7]
P2P devices can declare a group as persistent
The devices forming the group store network credentials
The assigned P2P GO and Client roles for subsequent re-instantiations of the P2P group

## Slide 28: Persistent Group Formation (2/2)
After the Discovery phase, if a P2P Device recognizes to have formed a persistent group with the corresponding peer in the past, any of the two P2P devices can use the Invitation Procedure to quickly re-instantiate the group.
GO Negotiation phase is replaced by the invitation exchange
the WPS Provisioning phase is significantly reduced because the stored network credentials can be reused

## Slide 29: Security
Wi-Fi Direct devices uses WPS (Wi-Fi Protected Setup)
  Based on WPA-2
  supports a secure connection with minimal user intervention
WPS allows to add a new device to the network for secure connection by
  a PIN in the P2P Client, or
  pushing a button in the two P2P Devices
  NFC, USB flash drive, etc.
Phase 1: GO generates and issues the security keys
Phase 2: P2P Client disassociates and reconnects using its new authentication credentials
  If two devices already have the required network credentials (Persistent group formation), there is no need to trigger the first phase

## Slide 30: Delay in WiFi P2P Initial Link Setup
Source: [7]
Discovery Delay
Formation Delay
  Time required for GO Negotiation, WPS Provisioning, and Address configuration

## Slide 31: Other 802.11 D2D Technologies
802.11 ad hoc mode operation (IBSS):
  Never became widely deployed in the market
  lack of efficient power saving support or extended QoS capabilities
  No support for group communication
  Being replaced by Wi-Fi Direct
802.11z (Tunneled Direct Link Setup (TDLS))
  enables direct device to device communication
  requires stations to be associated with the same AP

## Slide 32: References
[1] IEEE P802.11-REVmc/D4.0, January 2015
[2] IEEE P802.11ai /D4.0, February 2015
[3] Improving WLAN System Performance, 11-13-1325r5, Nov 11, 2013
[4] TGai Experimental Test Report of FILS, 11-13-0323r2, 2013.
[5] GAS Query Optimization in 11ai, 11-11-1499r0, Oct 24, 2011.
[6] P2P Technical Specification Proposal Overview, WFA, May 15 2009.
[7] Device-to-Device Communication with WIFI-Direct: Overview and Experimentation, Daniel Camps-mur, et.al., IEEE Wireless Communications June 2013

## Slide 33: Q & A