## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [MAC security for IEEE 802.15.8 PAC]
Date Submitted: [March 10th, 2015]
Source: [Woongsoo Na and Sungrae Cho]
Company: [Chung-Ang University, Korea]
E-Mail: [wsna@uclab.re.kr srcho@cau.ac.kr]
Re: [This is the original document]
Abstract: [MAC security for IEEE 802.15.8 PAC]
Purpose: [To introduce proposed MAC security for PAC]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: MAC security for IEEE 802.15.8 PAC
Woongsoo Na,
Sungrae Cho
Chung-Ang University

## Slide 3
Security Mechanism for PAC

## Slide 4: Authentication
Process of verifying ‘who’ is at the other end of the link
Performed for devices (PAC_ADDR)
Achieved by authentication procedure based on the stored authentication key (AUTH_KEY) or by peering (entering a PIN)
Slide 4

## Slide 5: Authorization
Process of deciding if device X is allowed to have access to service Y
Trusted devices (authenticated) are allowed to services
Untrusted or unknown devices may require authorization based on interaction before access to services is granted
Authorization always includes authentication
Technically, key would be derived or given (established) to the authorized user
Slide 5

## Slide 6: Authorization
Device trust levels
Trusted device | The device has been previously authenticated, An AUTH_KEY is stored The device is marked as “trusted” in the device DB
Untrusted device | The device has been previously authenticated An AUTH_KEY is stored But the device is not marked as “trusted” in the device DB
Unknown device | No security information is available for this device This is also an untrusted device
Slide 6

## Slide 7: Security Modes
Security mode 1 (non-secure)
  When a PAC device is in security mode 1, it shall never initiate any security procedure
Slide 7

## Slide 8: Security Modes
Security mode 2 (service level enforced security)
  When a PAC device is in security mode 2, it shall not initiate any security procedure before a channel establishment request has been received or a channel establishment procedure has been initiated by itself
  Whether a security procedure is initiated or not depends on the security requirements of the requested channel or service
  Security mode 1 can be considered as a special case of security mode 2 where no service has registered any security requirements
Slide 8

## Slide 9: Security Modes
Security mode 2 (cont.)
  A PAC device in security mode 2 should classify the security requirements of its services using the following attributes
Authentication required | - Before connecting to the application, the remote device must be authenticated
Authorization required | - Access is only granted automatically to trusted PAC devices, or untrusted devices after an authorization procedure - Always requires authentication to verify that the device is the right one
Encryption required | - The link must be changed to encrypted mode, before access to the service is possible

## Slide 10: Security Modes
Security mode 3 (link level enforced security)
  When a PAC device is in security mode 3, it shall initiate security procedures before the channel is established

## Slide 11: Security Parameters
PAC_ADDR: PAC device address (unique for each device)
AUTH_KEY: used for authentication purposes
ENC_KEY: encryption key (for secure unicast)
GENC_KEY: group encryption key
RAND: frequently changing random or pseudo-random number made by the PAC device itself
Entity | Size
PAC_ADDR | xxx bits
AUTH_KEY | 160 bits
ENC_KEY | 128 bits
GENC_KEY | 128 bits
RAND | 128 bits
Entity | Size
PAC_ADDR | xxx bits
AUTH_KEY | 
ENC_KEY | 
GENC_KEY | 
RAND | 

## Slide 12: Flow Chart for Authentication
Authentication start
Already authenticated
Peering allowed
Peering
Authentication OK
Authentication fail
Link key (AUTH_KEY) available
no
no
no
fail
yes
yes
ok
yes

## Slide 13: Flow Chart for Authorization
Authorization start
Trusted
Create trust
Authorization OK
Authorization fail
Link key (AUTH_KEY) available
no
no
no
fail
yes
yes
yes
Creation of trust allowed?
yes
Authentication succeed?
Slide 13

## Slide 14: Infrastructureless Architecture
No coordinator or AAA (authentication, authorization, accountability) server
Using PIN (symmetric), or certificate (asymmetric) issued by the trusted third party
  Cf) Bluetooth pairing
Slide 14

## Slide 15: Key Derivation
PRF
PRF
PRF
PRF
PIN
PIN
AUTH_KEYAB
AUTH_KEYAB
ENC_KEY
ENC_KEY
Authentication
Encryption
Device A
Device B
During
peering
Slide 15

## Slide 16: Infrastructure Architecture
AAA (authentication, authorization, accountability) server
(Dynamic) Coordinator
  Intermittent connection to the AAA server
Using master key (symmetric) issued by the AAA server, or certificate issued by the AAA server
  Cf) IEEE 802.1x, Kerberos protocol
2G/3G/LTE
AAA server
Server for some services (e.g., advertising)
Authentication &
communication
flow
Communication
flow
coordinator
Slide 16

## Slide 17
PD A
Coordinator B
AS
(Re)association
Association
EAP authentication
EAP Start(Msg Header)
ENC_KEY
Group key delivery
Group key delivery delay
EAP Transfer(EAP Payload)
EAP Transfer(EAP Success)
Access Accept(PMK)
MSK
PMK
AUTH_KEY
SA-ENC-Challenge
SA-ENC-Request
SA-ENC-Response
3-way handshake
MSK, PMK
Key Request
Key Reply(ENC_KEY)
ENC_KEY delivery
AUTH_KEY
ENC_KEY
PMK

## Slide 18: EAP Authentication
Extensible Authentication Protocol (EAP)
  De facto authentication protocol for infrastructure architecture (interact with AAA server)
    IEEE 802.16, 802.11, …
  Fulfill the criteria: mutual authentication, protection against the man-in-the-middle attack
  EAP-PSK, EAP-AKA, EAP-PEAP, …
  Yields the512-bit master secret key (MSK)
    Then the other key encryption keys (KEK) and HMAC/CMAC keys are derived from the MSK
Slide 18

## Slide 19: Authentication Key Generation
PD A and AS derive MSK, and then PMK
PD A and coordinator B derive AUTH_KEY from PMK
Then, PD A and coordinator B derive
  A shared KEK
  HMAC/CMAC key from the AUTH_KEY

## Slide 20: SA-ENC 3-Way Handshake
Provides the following security guarantees:
  Full mutual authentication
  PD A is alive and that A possesses the AUTH_KEY
  Coordinator B is alive
  The coordinator B is guaranteed that SA-ENC-Update is sent by the PD A and is fresh
Slide 20

## Slide 21: ENC_KEY Distribution
After a successful authorization, the PD A dynamically requests parameters for SA(security association) including ENC_KEY
  KEY_Request
  KEY_Reply
Slide 21

## Slide 22: Group Key Distribution
In a network environment where the secure multicast and broadcast service (MBS) is supported, additional group key (GENC_KEY) generation and delivery process is performed optionally after ENC_KEY distribution procedure
Update on every membership change
  Backward security
  Forward security
Slide 22