## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: LB101 Comment Resolutions.
Date Submitted: 12 March, 2015
Source: Chandrashekhar Thejaswi PS, Kiran Bynam and Jinesh Nair
E-Mail: c.thejaswi@samsung.com
Abstract: Comment resolutions.
Purpose: Response to the letter ballot comments.
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
CID | Pg.No | Clause | Ln. No. | Comment | Suggested Change | Mandatory
3059 | 4 | 6.17 | 2 | I know that the FSK PHY put this table in the MAC, but it was a mistake that is fixed in the current draft of the revision. Don't make the same mistake, move this to the PHY subclause. | Move 6.17 to somewhere in Clause 30, perhaps in 30.1 | YES

## Slide 3
Resolution: Revised
Proposed change:
In Pg.4, Delete Line 1, and delete clause 6.17 and Table 4a.
In Pg.12, sub-clause 30.1, after line 3-4, add the following text:
“ For ULP-TASK PHY, the symbol duration parameters for MAC and PHY timing parameters, for different bands of operation shall be as given in Table 336.”
Insert Table 4a (as Table 336), with its caption after the above text.

## Slide 4
CID | Pg.No | Clause | Ln. No. | Comment | Suggested Change | Mandatory
3082 | 7 | 8.3.1 | 5 | Change the Data Rate description to match what are currently used in latest draft, i.e. just refer to table which have MCSP data rate parameter for each data rate used. | i.e. change the text to say “For ULP-TASK PHY valid values are defined in Table XXX. For ULP-GFSK PHY valid values are defined in Table YYY.”. Add Table XXX in section 30.3 where it columns “DataRate as used in MCSP-DATA primitive”, and “Corresponding MCS identifier”, or something similar, or just add “DataRate as used in MCSP-DATA primitive” as one column to tables 339-341, and change the text to say “are defined in Tables 339-341”. Also Add Table YYY in section 31.2, or again add “DataRate as used in MCSP-DATA primitive” to the table 352. Actually how does the upper layer indicate it wants to use RateSwitch feature when sending packet? | Yes

## Slide 5
Resolution (1): Revised
Proposed change for ULP-TASK PHY:
In Pg. 7, sub-clause 8.3.1. In the “Description” column,
Modify the sentence
“For ULP-TASK PHY, values 0-7 are valid: each value corresponds to the MCS as described in 30.3.” to
“For ULP-TASK PHY, values 0-7 are valid: each value corresponds to the MCS as described in 30.3 (given in Table 339- Table 341)”
In Pg. 15, Ln. 13, sub-clause 30.3.1.
After the sentence
“The MCS identifier and the corresponding data rates for different ….”
Add the following sentence after the sentence:
“The values presented in “Data rate” columns of each of these tables correspond to the “DataRate” as used in MCPS-DATA primitive as described in 8.3.1.”

## Slide 6
Resolution (2): Revised
Proposed change for RS-GFSK PHY:
In Pg. 7, sub-clause 8.3.1. In the “Description” column,
Modify the sentence:
“For ULP-GFSK PHY, values 0-7 are valid; each value corresponds to the MCS as described in 31.2.”
to:
“For RS-GFSK PHY, values 0-7 are valid: each value corresponds to the MCS Identifier as described in 31.2 (given in Table 352)”
In Pg. 32, Ln. 3, sub-clause 3.2, after the sentence:
“Table 352 shows the primary modulation and channel parameters for the ULP-GFSK PHY MCSs.”
Add the following sentence after the sentence:
“The values presented in “RS-GFSK MCS Identifier” column correspond to the “DataRate” as used in MCPS-DATA primitive as described in 8.3.1.”

## Slide 7
CID | Pg.No | Clause | Ln. No. | Comment | Suggested Change | Mandatory
3084 | 9 | 10.1.2.12 | 3 | In table 165 add “Band designation” as first column in so the bands in table 164 can be matched with this table. | Add “Band designation” to first column and fill it values from Table 164. | Yes
Resolution: Revised
In Pg.8, sub-clause 10.1.1: Replace Table 164 with the following modified table:
Frequency band identifier fb | Frequency (MHz) | Designation
0 | 169.400-169.475 | 169 MHz band
1 | 433.050-434.790 | 433 MHz band
2 | 450-470 | 450 MHz band
3 | 470-510 | 470 MHz band
4 | 779-787 | 780 MHz band
5 | 863-876 | 863 MHz band
6 | 896-901 | 896 MHz band
7 | 901-902 | 901 MHz band
8 | 902-928 | 915 MHz band
9 | 915-921 | 918 MHz band
10 | 917-923.5 | 917 MHz band
11 | 928-960 | 928 MHz band
12 | 950-956 | 950 MHz band
13 | 1427-1518 | 1427 MHz band
14 | 2400-2483.5 | 2450 MHz band

## Slide 8
In Pg.9, sub-clause 10.1.2.13: Replace Table 165 with the following modified table:
Frequency band identifier | ChanSpacing (MHz) | TotalNumChan | ChanCenterFreq0 (MHz)
1 | 0.4 | 4 | 433.3
3 | 0.8 | 50 | 470.4
4 | 2 | 4 | 780
5 | 2 | 6 | 864
8 | 2 | 10 | 906
12 | 2 | 3 | 951
14 | 5 | 16 | 2405

## Slide 9
CID | Pg.No | Clause | Ln. No. | Comment | Suggested Change | Mandatory
3004 | 29 | 30.8.10 |  | proposed section and "LQI" are not going well with each other | replace this section with the procedure dealing with "SNR meaurement" | Yes
3036 | 29 | 30.8.10 | 22 | "The minimum and maximum LQI values (0x00 and 0xff) should be associated with the lowest and highest quality compliant signals detectable by the receiver, and LQI values in between should be uniformly distributed between these two limits" is missing a vital word: respectively. | "The minimum and maximum LQI values (0x00 and 0xff) should be associated with the lowest and highest quality compliant signals detectable by the receiver, respectively, and LQI values in between should be uniformly distributed between these two limits." | Yes
Resolution: Revised
In Pg. 29, Replace the sub-clause 30.8.10 with the following title and the text:
“
30.8.10 SNR measurement
The minimum and maximum SNR values (0x00 and 0xff) should be associated with the lowest and highest quality compliant signals detectable by the receiver, respectively, and SNR values in between should be uniformly distributed between these two limits. ”

## Slide 10
CID | Pg.No | Clause | Ln. No. | Comment | Suggested Change | Mandatory
3125 | 38 | A | 8 | This bibliography entry is not referenced in the draft. | Find a place to reference it in the draft. | yes
Resolution: Revised
In Pg. ix, Ln. 16, in “Introduction” clause, add the reference as below:
“The features and benefits of ULP TASK are described in [B42].”
In sub-clause 5.7.1, add the following sentence as an itemized para:
“For the ULP-TASK PHY and ULP-GFSK PHY: “TG4q Coexistence Assurance Document” [B15].”

## Slide 11
CID | Pg.No | Clause | Ln. No. | Comment | Suggested Change | Mandatory
3010 |  | 30 | Table 337, 339, 340, 341 | replace "BCH+ SIPC" with "BCH with interleaving + SiPC" | Please change | yes

## Slide 12
Resolution: Revised
Proposed Changes:
In Pg. 13, Table 337, replace the “FEC” column with the following column
In the footnote of Table 337, (Pg. 13, Ln. 17) replace the foot note by
“NOTE—`BCH + SiPC’ indicates the concatenated code generated by BCH code as the outer
code and the SiPC as the inner code.
‘BCH with interleaving + SiPC’ indicates concatenated code generated by BCH with
interleaving as the outer code and the SiPC as 18 the inner code.”
FEC
BCH
BCH with interleaving
BCH with interleaving
BCH with interleaving
BCH + SiPC
BCH with interleaving + SiPC
BCH with interleaving + SiPC
BCH with interleaving + SiPC

## Slide 13
In sub-clause 30.3, Tables 339,340 and 341,
Replace the “Coding format” column of all the tables with the following column
Coding format
BCH
BCH with interleaving
BCH with interleaving
BCH with interleaving
BCH + SiPC
BCH with interleaving + SiPC
BCH with interleaving + SiPC
BCH with interleaving + SiPC