## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [ Device discovery text]
Date Submitted: [ April 28th, 2015 ]
Source: [Marco Hernandez, Huan-Bang Li, Igor Dotlić, Ryu Miura ]
Company: [NICT]
Address: [3-4 Hikarino-oka, Yokosuka, 239-0847, Japan]
Voice:[+81 46-847-5439] Fax: [+81 46-847-5431] E-Mail:[]
Re: [In response to call for technical contributions TG8]
Abstract: [ ]
Purpose: [Material for discussion in 802.15.8 TG]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Device discovery
5.1.2.5 Device discovery
  The PAN coordinator or a coordinator A PD indicates its presence on a PAN to other devices PDs by transmitting beacon frames its discovery information during the discovery period. This allows other devices to perform device PD discovery.
  A coordinator that is not the PAN coordinator shall begin transmitting beacon frames only when it has successfully associated with a PAN. The transmission of beacon frames by the device is initiated through the use of the MLME-START.request primitive with the PANCoordinator parameter set to FALSE.†
    †No required for PAC.

## Slide 3: Device discovery
  On receipt of this primitive, the MLME shall begin transmitting beacons based on the StartTime parameter, as described in 5.1.2.4, using the identifier of the PAN with which the device has associated, macPANId, and its extended address, macExtendedAddress, if macShortAddress is equal to 0xfffe, or its short address, macShortAddress, otherwise. A beacon frame shall be transmitted at a rate of one beacon frame every aBaseSuperframeDuration × 2n, where n is the value of macBeaconOrder.†
    †No required for PAC.

## Slide 4: Device/Peer discovery
PD discovery information contains:
  Device ID (MAC address?) (low level ID) consisting of x bits.
  Peer ID (from higher layers) (high level ID) consisting of x bits.
  Group ID (from higher layers) consisting of x bits.
  Application ID (from higher layers) consisting of x bits.
Still undecided if device ID, as a low level ID, is required in the specification.
  If discovery information is generated and processed from higher layers, device ID (low level ID) may not be needed.
  Maybe device ID (low level ID) is useful for authentication between a Peer ID and a particular PD.