## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Input to the TRD of TG3d
Date Submitted: 12 May 2015
Source: Thomas Kürner Company TU Braunschweig
Address Schleinitzstr. 22, D-38092 Braunschweig, Germany
Voice:+495313912416, FAX: +495313915192, E-Mail: t.kuerner@tu-bs.de
Re: doc. 14/0309r5
Abstract: This document summarizes some input/thoughts for various sections of the TRD.
The document defines required input and proposes a restructering of some sections.
Purpose: Input to the Technical Requirements Document (TRD) of IEEE 802.15 TG3d (100G)
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Input to the TRD of TG3d
Thomas Kürner
TU Braunschweig

## Slide 3: Scope
This document summarizes some input/thoughts for various sections of the TRD.
The document proposes a restructering of some sections of doc. 14/0309r5 and proposes new text for some of the sections

## Slide 4: Proposal for Restructering the Document in Section 7ff (1/2)
7. Topology and Link Switching
8. Target Data Rates
9. Transmission Distances
10. Operational Frequency Bands
11. Regulatory Requirements (merge of former sections 11 and 12)
12. Channel Models
13. Link Budget and SNR Analysis (includes also the former section on antenna gain and required alignment accuracy).

## Slide 5: Proposal for Restructering the Document in Section 7ff (2/2)
14. MAC Mechanism (this will include also former section 18 beem steered or control channel assisted device discovery)
15. I/O Interfaces and Memory Buffer Considerations
16. Fast Connection Setup Scheme
17. Security Mechanism

## Slide 6: Section 7: Topology and Link Switching
Proposal for new text:
  In all use cases the topology will be point-to-point (P2P) and limited to two active devices. It may be necessary to switch between several links, see Figure 1.
Figure 1: Switched Point-to-Point Links; Link 1 TRX1 to TRX2 switched to link 2 TRX1 to TRX 3
TRX1
TRX2
TRX3
Link 1
Link 2

## Slide 7: Section 8 Target Data Rates
Proposal for new text:
  The PHY should support the data rates as defined in Table 1
  Table 1: Data Rates for different use cases
Use case | Minimum Data Rate in Gb/s | Maximum Data Rate in Gb/s | Required BER
Intra-Device Communication | 24 | 100 | 10-12
Close Proximity Communication | tbd | 100 | tbd
Wireless Fronthauling | tbd | 10 | 10-12
Wireless Backhauling | tbd | 100 | 10-12
Data Center | 1 | 100 | 10-12

## Slide 8: Section 9 Transmission Distances
Proposal for new text:
  The data rates specified in section 8 shall be achieved for transmissions over the distances specified in table 2
Use case | Transmission Distance
Intra-Device Communication | 10 cm or less
Close Proximity Communication | 50 mm or less
Wireless Fronthauling | a few hundred meters
Wireless Backhauling | a few hundred meters up to a few kilometers
Wireless Data Center | 10-100 m

## Slide 9: 10. Operational Frequency Bands
Proposal for new text:
The operational frequency bands are from 252 to 325 GHz. The frequency bands 252 to 275 GHz have already an allocation for MOBILE and FIXED services in the radio regulations. The band 275 – 325 GHz is not allocated to any servcie in the radio regulations, but may be used for active services, if the conditions in footnote 5.565 of the radio regulations are met.
<tbd: include options for channelization>

## Slide 10: 11. Regulatory Requirements and Coexistence
Proposal for a new sub-structure
11.1 Requirements from the Radio Regulations
<this will include text from current sections 12, 11.1 and 11.2>
11.2. Coexistence among different use cases
<introductory text from current section 11>

## Slide 11: Section 13: Link Budget and SNR Analysis
Propose new text:
Proposals have to include link budget calculations, which show, that the requirements defined in sections 8 and 9 can be met. This shall include also requirements on the antenna gain and the required alignment accuracy, which is use case dependent. An example link budget is given in table 3.
<include table from current section 16 as table 3>

## Slide 12: 14. MAC Mechanism
All current text should be deleted.
Proposal for a new sub structure:
19.1. Beam steered or control channel assisted device discovery
19.2. Link Establishment Beaconing Protocol
19.3. PHY/MAC header fields and premable defintions
19.4. Requirements MAC for an established link

## Slide 13: 15. I/O Interface and Memory Buffer Considerations
Proposal for new text:
The choice of features regarding these items are up to the implementer. However, proposals should include a statement on the expected numbers.

## Slide 14: 16. Fast Connection Setup Scheme
Proposal for new text:
This is relevant for the close proximity use case only. However the consideration of this feature is not part of the amendment developed in this TG. The fast connection setup will be developped in the parallel running TG 3e.

## Slide 15: 17. Security Mechanism
Proposal of new text:
Proposals should indicate how security can be integrated. Diffentiation may be made between
  the links for the wireless backhaul/fronthaul, data center and intra-device communication use cases, where links will be establised on a longer time period
  the links for the close proximity communication, where the links survive only a short time period.