## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Proposal of a TG3d Channel Model for Wireless Backhaul/Fronthaul
Date Submitted: 11 July 2015
Source: Thomas Kürner Company TU Braunschweig
Address Schleinitzstr. 22, D-38092 Braunschweig, Germany
Voice:+495313912416, FAX: +495313915192, E-Mail: t.kuerner@tu-bs.de
Re: doc. 14/0310r6
Abstract: This document proposes a channel for the wireless backhaul/fronthaul use cases in TG3d
Purpose: Input to the Channel modeling Document of IEEE 802.15 TG3d (100G)
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Proposal of a TG3d Channel Model for Wireless Backhaul/Fronthaul
Thomas Kürner
TU Braunschweig

## Slide 3: Operational Characteristics for Backhaul/Fronthaul Applications at 300 GHz
The mitigation of the high path loss at 300 GHz requires high gain antennas in the order of 40 dB at both sides of the link for a transmission distance of several hundred meters.
This requires a LOS connection
In addition such high gain antennas are spatial filters, that supress multi path propagation at large
A path loss model to evaluate the link budget is sufficient as a first approximation

## Slide 4: Relevant Propagation Characteristics (1/2)
The relevant propagation mechanism in such an environment, which are contributing to increase the free space loss are described in [1]:
  Atmospheric gas attenuation
  Rain attenuation
  Cloud and fog attenuation

## Slide 5: Relevant Propagation Characteristics (2/2)
For terrestrial links it can be assumed that the link is operated below the height of clouds. The situation that a link penerates clouds may happen for example in some alpine regions with one transceiver at a high mountain, but it is unlikely, that ultra-high capacity links are required there. Therefore the attenuation by clouds may be less relevant.
However, the influence of fog may be interest also for dense urban area

## Slide 6: Calculation of the total Path Loss
The overall path loss at a distance d and a carrier frequency f can be modelled as:
where
(1)

## Slide 7: Specific Attenuation by Atmospheric Gases according to ITU-R P.676-10 [2]
Two methods are decribed in ITU-R P.676-10:
  A more detailed line –by-line calculation of gaseous attenuation
  A simplified method, based on curve-fitting of the line-by-line calculation agrees with the more accurate calculations to within an average of about 10% at frequencies removed from the centres of major absorption lines. The absolute difference between the results from these algorithms and the line-by-line calculation is generally less than 0.1 dB/km and reaches a maximum of 0.7 dB/km near 60 GHz.
In the following the specific attenuation due to dry air and water vapour, is estimated using the simplified algorithms, valid for the frequency range 120 to 350 GHz

## Slide 8: Specific Attenuation go for Dry Air
go is calculated using the following equations:
where: f : frequency (GHz)
rp = ptot/1013, where ptot represents total air pressure
rt  288/(273  t)
p : pressure (hPa)
t : temperature (C)
(2)
(3)
(4)

## Slide 9: Specific Attenuation gW for Water Vapour (1/2)
gw is calculated using the following equations:
(5)

## Slide 10: Specific Attenuation gW for Water Vapour (2/2)
where  is the water-vapour density (g/m3).
(6)
(7)
(8)

## Slide 11: Example
Exemplary result for the specific attenuation from 1 to 350 GHz at sea-level for dry air (p=1013 hPa, t=15°C) and water vapour with a density of r=7.5 g/m3 (from [2])

## Slide 12: Specific Attenuation gR by Rain according to ITU-R P. 838-3 [3] (1/2)
gR is calculated according to the folowing equation:
Values for k and a for the frequencies 200, 300 and 400 GHz are given in the following table
where:
R: rain rate in mm/h
k : either kH or kV for horizontal and vertical polarization, respectively
 : either H or V. for horizontal and vertical polarization, respectively
(9)
Frequency (GHz) | kh | H | kV | V
200 | 1.6378 | 0.6382 | 1.6443 | 0.6343
300 | 1.6286 | 0.6296 | 1.6286 | 0.6262
400 | 1.5860 | 0.6262 | 1.5820 | 0.6256

## Slide 13: Specific Attenuation gR by Rain according to ITU-R P. 838-3 [3] (2/2)
For linear and circular polarization, and for all path geometries, the coefficients in equation (9) can be calculated from the values given the previous table using the following equations:
where q is the path elevation angle and t is the polarization tilt angle relative to the horizontal (t = 45° for circular polarization).
(10)
(11)

## Slide 14: Typical Rain Rates [1,4]
Type of Precipitation | Range of R (mm/h) | Intensity
Drizzle | R < 0,1 | Light
Drizzle | 0,1 < R < 0,5 | Moderate
Drizzle | R > 0,5 | Heavy
Rain | R < 2,5 | Light
Rain | 2,5 < R < 10 | Moderate
Rain | 10 < R < 50 | Heavy
Rain | R > 50 | Extreme

## Slide 15: Exemplary Results for Specific Rain Attenuation gR at the Carrier Frequencies 200, 300 and 400 GHz
f/GHz | Horizontal Polarisation |  |  | Vertical Polarisation |  | 
 | R= / mm/h |  |  | R / mm/h |  | 
 | 0,1 | 5 | 50 | 0,1 | 5 | 50
200 | 0,38 | 4,57 | 19,89 | 0,38 | 4,56 | 19,66
300 | 0,38 | 4,49 | 19,12 | 0,39 | 4,46 | 18,87
400 | 0,38 | 4,35 | 18,37 | 0,37 | 4,33 | 18,28

## Slide 16: Specific Attenuation due to Fog and Clouds according to ITU-R P.840-6
The specific attenuation within a cloud or fog can be written as:
where:
c : specific attenuation (dB/km) within the cloud
Kl : specific attenuation coefficient ((dB/km)/(g/m3))
M : liquid water density in the cloud or fog (g/m3).
(12)

## Slide 17: Calculation of the Specific Attenuation Kl
(dB/km)/(g/m3) (12)
where f is the frequency (GHz), and:
(13)
(14)
(15)

## Slide 18: Calculation of the Specific Attenuation Kl cont.
where:
0 = 77.66 + 103.3 ( – 1) (16)
1 = 0.0671 (17)
2 = 3.52 (18)
 = 300 / T (19)
with T the temperature (K).
and the principal and secondary relaxation frequencies are:
fp = 20.20 – 146 ( – 1) + 316 ( – 1)2 GHz (20)
fs = 39.8fp GHz (21)

## Slide 19: Average values for water content in fog and clouds [5,6]
Cloud type | Average water content in g/cm3
large cumulus | 2.5
fair weather cumulus | 0.5
Stratocumulus | 0.2
Stratus | 0.2-0.3
Altostratus | 0.2
Fog type | Average water content in g/cm3
medium fog (visibility of the order of 300 m) | 0.05
thick fog (visibility of the order of 50 m) | 0.5

## Slide 20: References
[1] G. A. Siles, J. M. Riera, P. Garcia-del-Pino, Atmospheric Attenuation in Wireless Communication Systems at Millimeter and THz Frequencies, IEEE Antennas and Propagation Magazine, Vol. 57, No. 1, February 2015, pp. 48-59
[2] Rec. ITU-R P.676-10, Attenuation by atmospheric gases, 2013
[3] Rec. ITU-R P.838-3, Specific attenuation for rain for use in prediction methods, 2005
[4] Guide to Meteorological Instruments and Methods of Observation, World Meteorological Organization (WMO), Geneva, Switzerland, 2008.
[5] Rec. ITU-R P.840-6, Attenuation due to clouds and fog, 2013
[6] H. J. aufm Kampe, Visibility and Liquid Water Content in the free Atmosphere, Journal of Meteorology, Vol. 7, p. 54-57, February 1950