## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Proposed Resolution for Comment CID 53 from Letter Ballot #104
Date Submitted: May 10, 2015
Source: Soo-Young Chang (SYCA), Jaebeom Kim (Ajou Univ.), and Jaehwan Kim and Sangsung Choi (ETRI)
Company: SYCA, Ajou Univ. and ETRI
Address:
Voice: +1 530 574 2741, E-Mail: sychang@ecs.csus.edu and kimj@etri.re.kr
Re:
Abstract: Proposed comment resolution for a comment on the draft of TG10 L2R routing for Letter Ballot #104
Purpose: To suggest a comment resolution for Letter Ballot #104
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Comment CID 53
Commentor
  Don Sturek
Comment
  There are several omissions related to L2R over multiple PANs: 1) Discovering devices (or finding destination addresses) for devices that are not in the current PAN or in an adjoining PAN - For example a messages comes from the internet to the Tree Root for PAN ID 1 destined for a device that is not the PAN coordinator in PAN ID 4 - How is this packet routed from PAN ID 1 to PAN ID 3 to PAN ID 4? I did not see any structures exchanged between these PAN that would describe how the path is determined 2) Use of short addresses - There is no coordination of short address assignment so I assume the PAN ID must accompany any short address including those from other PANs - What structure contained this cross PAN routing 3) Support for PANs on different channels - In Figure 3, say PAN ID 1, 2, 3 and 4 are all on different channels. The routers that connect these PANs cannot be routers in BOTH PANs they are a member unless they have 2 radios - Is a different radio for each of these PAN memberships assumed? If not, how can a device that is a member of both PAN ID 1 and 3, for example, be a router in both with a single radio?

## Slide 3: Comment CID 53 (cont’d)
Proposed Change
  Either the information is missing or needs a better explanation in this section.

## Slide 4: Proposed Resolution (Accept in Principle)
Proposed Change
  Change p9 Lines 37-38 to
An L2R mesh tree may also span more than one PAN organized in different neighboring clusters such as in a TMCTP network ([15.4], 6.2.8). An L2R mesh tree deployed over more than one PAN is illustrated in Figure 3. In this scenario, all L2R devices must use extended address mode to avoid address confliction between PANs. The L2R provides multi-channel PAN route construction between PANs not only to PAN coordinators but also to PAN devices by using MCO field. In the TMCTP, a (child) PAN coordinator periodically switches its operation channel to communicate with its parent PAN coordinator and its PAN devices.
To provide stable route construction between multi-channel PANs, each device in the L2R notifies both its own channel and the channel of its parent PAN coordinator. The single radio interface-multichannel data communication procedure is defined in IEEE 802.15.4m TMCTP ([15.4], 6.2.8).