## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Proposed Resolution for Comment CID 249 from Letter Ballot #104
Date Submitted: May 10, 2015
Source: Soo-Young Chang (SYCA), Jaebeom Kim (Ajou Univ.), and Jaehwan Kim and Sangsung Choi (ETRI)
Company: SYCA, Ajou Univ. and ETRI
Address:
Voice: +1 530 574 2741, E-Mail: sychang@ecs.csus.edu and kimj@etri.re.kr
Re:
Abstract: Proposed comment resolution for a comment on the draft of TG10 L2R routing for Letter Ballot #104
Purpose: To suggest a comment resolution for Letter Ballot #104
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Comment CID 249
Commentor
  Tero Kivinen
Comment
  The device should also check that its address is not already in the intermediate address list, and if so, it should ignore the request, i.e. not reply it again.
Proposed Change
  The current described method will immediately ping pong between each devices by both devices appending themselves to the intermediate list until the TTL gets to zero.

## Slide 3: Proposed Resolution (Accept in Principle)
Proposed Change
  Change p32. lines 8-12:
When a device receives a P2P-RQ IE and is not the desired destination, it decrements the value in the TTL field, increments the value in the Number of Intermediate Addresses field, appends its own address to the Intermediate Address List field, and rebroadcasts the P2P-RQ IE.
to
When a device receives a P2P-RQ IE and is not the desired destination, it checks whether it is the duplicated one or not by using the message sequence number. If the SN of the received P2P-RQ is the same as the previous one, then it checks the hop count (or link metric) between messages. If the hop count (or link metric) value is bigger than the previous one, the received P2P-RQ is discarded. Otherwise, it decrements the value in the TTL field, increments the value in the Number of Intermediate Addresses field, appends its own address to the Intermediate Address List field, and rebroadcasts the P2P-RQ IE.