## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Additional Comments from Charles Perkins for Letter Ballot #104
Date Submitted: May 12, 2015
Source: Charlie Perkins
Company: Futurewei
E-Mail: charliep@computer.org
Abstract: Additional Comments to TG10 L2R routing for Letter Ballot #104
Purpose: To have the comments adopted for further consideration
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Additional Technical Comments
43 | 10 | 4.3 | 52 | is allowed by the mesh root | Allow device to decide for itself
64 | 17 | 5.1.2.2 | 33 | "unless the encryption key ... known to all the devices" | How can the devices tell? Is a bit needed in the beacon?
66 | 17 | 5.1.2.2 | 42 | appropriate error code | Error code must be specified. Is there a table of errors?
78 | 23 | 5.2.1 | 34 | "Number of metrics in use in the L2R mesh tree" | How does this work? (xref needed)
79 | 23 | 5.2.1 | 34 | "Number of metrics in use in the L2R mesh tree" | Is zero allowed? If not, valid range is 0x01 - 0x07
84 | 25 | 5.2.2 | 31 | 13 is wrong link cost | Should be 15
96 | 26 | 5.2.2.1 | 25 | How are the metric parameters known by all devices in PAN? | Explain or modify
97 | 26 | 5.2.2.1 | 33 | Why use maximum frame size instead of average? | Explain or modify
113 | 38 | 5.4.1.4 | 47 | Are all devices required to support DAgg / payload bunding? | Tough decision :-)
114 | 39 | 5.4.1.4 | 15 | "E2E Retry Limit are set by the device forwarding the aggregated..." | This makes the individual payloads NOT E2E.
116 | 39 | 5.4.1.4 | 22 | Can aggregated frames be delayed for more aggregation? | Tough decision :-)
136 | 47 | 5.5.1.3 | 25 | Reactive should not be disallowed | Replace "proactive routing" by "Start L2R routing"
157 | 52 | 6.2.1 | 46 | There is no SN field in the IE | Insert if needed
164 | 53 | 6.2.1.1 | 40 | Could allow RA IE to have multicast regardless of this bit | Consider deleting the field
166 | 53 | 6.2.1.1 | 47 | "Security Level field is present in the TC IE." | Why not put the field here?
175 | 54 | 6.2.1.2 | 22 | identifier space needs more description and specification | Provide text about ID space. Is it a registry?
186 | 56 | 6.2.2.6 | 37 | "Hours" unit is not needed. | Make into a reserved bit?
212 | 62 | 6.2.6.2 | 49 | "Entity ID field identifies an entity" | This might require a registry of EntityIDs
219 | 64 | 6.2.6.11 | 4 | Suggest bit vector format for Intermediate Hop Descriptor | 7 bits for Addresses, 1 bit for "continuation"
228 | 68 | 6.2.10.1 | 54 | "or discarded" -- but is pre-emption a possibility? | Consider pre-emption
259 | 87 | 7.2.1 | 27 | Is a timeout associated with L2R-DATAL2R-DATA.confirm? | If not, clarify handling of "request" state
269 | 90 | 7.2.1.2 | 40 | Are error codes needed for Delay Critical or GuaranteedTx? | Add error codes as appropriate

## Slide 3: More discussion about comments (1)
43 / 10 / 4.3 / 52 / is allowed by the mesh root / Allow device to decide for itself
  Not clear why mesh root needs to control brother routing
64 / 17 / 5.1.2.2 / 33 / "unless the encryption key ... known to all the devices" / How can the devices tell?
  How does the FFD know whether all devices have the encryption key?
66 / 17 / 5.1.2.2 / 42 / appropriate error code / Error code must be specified. Is there a table of errors?
  What is the code for a failed Join? Where is the table for it?
78 / 23 / 5.2.1 / 34 / "Number of metrics in use in the L2R mesh tree" / How does this work? (xref needed)
  xref to the description of the operation
79 / 23 / 5.2.1 / 34 / "Number of metrics in use in the L2R mesh tree" / Is zero allowed? If not, valid range is 0x01 - 0x07
  Various fields used for counting should not allow zero as a valid count
84 / 25 / 5.2.2 / 31 / 13 is wrong link cost / Should be 15
  Verify the correct cost for using the link.

## Slide 4: More discussion about comments (2)
96 / 26 / 5.2.2.1 / 25 / How are the metric parameters known by all devices in PAN? / Explain or modify
  For the Inactive Time Aware metric to work, these parameters must be known to all devices
97 / 26 / 5.2.2.1 / 33 / Why use maximum frame size instead of average? / Explain or modify
  Average frame size would provide a measurement more meaningful for the particular network
113 / 38 / 5.4.1.4 / 47 / Are all devices required to support DAgg / payload bunding? / Tough decision :-)
  Is probably O.K. if some devices do not support, but any destination must support
114 / 39 / 5.4.1.4 / 15 / "E2E Retry Limit are set by the device forwarding the aggregated..." / This makes the individual payloads NOT E2E.
  The endpoints do not control the number of retries for a frame in an aggregation
116 / 39 / 5.4.1.4 / 22 / Can aggregated frames be delayed for more aggregation? / Tough decision :-)
  Pro: more aggregation. Con: more delay not controlled by the endpoints

## Slide 5: More discussion about comments (3)
136 / 47 / 5.5.1.3 / 25 / Reactive should not be disallowed / Replace "proactive routing" by "Start L2R routing“
  Agreed to fix
157 / 52 / 6.2.1 / 46 / There is no SN field in the IE / Insert if needed
  All other control frames have the SN
164 / 53 / 6.2.1.1 / 40 / Could allow RA IE to have multicast regardless of this bit / Consider deleting the field
  Does the implementation of multicast require configuration control
166 / 53 / 6.2.1.1 / 47 / "Security Level field is present in the TC IE." / Why not put the field here?
  Just in case it makes more sense to collect together related information in the same place
175 / 54 / 6.2.1.2 / 22 / identifier space needs more description and specification / Provide text about ID space. Is it a registry?
  Not clear how a device would know which mesh to join just based on a number from 0 to 255.
186 / 56 / 6.2.2.6 / 37 / "Hours" unit is not needed. / Make into a reserved bit?
  O.K. for TC IE according to morning discussion

## Slide 6: More discussion about comments (4)
212 / 62 / 6.2.6.2 / 49 / "Entity ID field identifies an entity" / This might require a registry of EntityIDs
  Same idea already in comment 175
219 / 64 / 6.2.6.11 / 4 / Suggest bit vector format for Intermediate Hop Descriptor / 7 bits for Addresses, 1 bit for "continuation“
  Save space for listing Intermediate Hop Addresses, as discussed
228 / 68 / 6.2.10.1 / 54 / "or discarded" -- but is pre-emption a possibility? / Consider pre-emption
  Delay critical frames may be important for transmission and deserve special treatment
259 / 87 / 7.2.1 / 27 / Is a timeout associated with L2R-DATAL2R-DATA.confirm? / If not, clarify handling of "request" state
  In case the acknowledgement never arrives, need to clean up state
269 / 90 / 7.2.1.2 / 40 / Are error codes needed for Delay Critical or GuaranteedTx? / Add error codes as appropriate
  Agreed to fix in conjunction with another comment resolution in AM1 session