## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: 3e proposal
Date Submitted: 9 July 2015
Source: Ken Hiraga, Doohwan Lee, Kazumitsu Sakamoto, Toshimitsu Tsubaki and Masashi Shimizu
Company: NTT Corporation
Address: Hirarinooka 1-1, Yokosuka Japan
Voice:+81-46-859-3474, FAX: +81-46-855-1497, E-Mail: hiraga.ken@lab.ntt.co.jp
Re: [Proposed aspects of PHY for HRCP]
Abstract: This document describes an outline of the key features for achieving high transmission rates.
Purpose: Overview of PHY aspects of full proposal for 3e.
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Contents
  MIMO MCS for 100 Gbit/s
  HRCP Channel model
    Channel response measurements
    SISO model
    MIMO extension

## Slide 3: 1. MIMO for high rate
We propose the use of MIMO (Multiple Input and Multiple Output) in line-of-sight (LOS) propagation environment for high rate MCS
For 100 Gbit/s transmission, channel aggregation will be employed
Final presentation will be made at the September meeting.

## Slide 4: MIMO MCS
MCS# | Modulation | Code Rate (same as 15.3c) | PHY transmission rate, Gbit/s |  |  |  |  |  |  |  |  | 
 |  |  | x1 mode |  | x2 mode |  | x4 mode |  | x8 mode |  | x16 mode | 
 |  |  | without pilot word | with pilot word* | without pilot word | with pilot word* | without pilot word | with pilot word* | without pilot word | with pilot word* | without pilot word | with pilot word*
1 | QPSK | 14/15 | 3.3 | 2.9 | 6.6 | 5.7 | 13.1 | 11.5 | 26.3 | 23.0 | 52.6 | 46.0
2 | 16QAM | 14/15 | 6.6 | 5.7 | 13.1 | 11.5 | 26.3 | 23.0 | 52.6 | 46.0 | 105.1 | 92.0
3 | 64QAM | 14/15 | 9.9 | 8.6 | 19.7 | 17.2 | 39.4 | 34.5 | 78.8 | 69.0 | 157.7 | 138.0
x1 mode: SISO + single channel
x2 mode: SISO + dual channels aggregation
x4 mode: [4x4 MIMO in 1 channel]
x8 mode: [4x4 MIMO in 2 channels] or [8x8 MIMO in 1 channel]
x16 mode: [8x8 MIMO in 2 channels] or [16x16 MIMO in 1 channel]
* Pilot word length/sub-block length = 1/8
Use of MIMO
Notes: PHY criteria 5: 100 Gbit/s+

## Slide 5: Channel aggregation
Channel # | Start frequency | Center frequency | Stop frequency
1 | 57.240 | 58.320 | 59.400
2 | 59.400 | 60.480 | 61.560
3 | 61.560 | 62.640 | 63.720
4 | 63.720 | 64.800 | 65.880
Frequency channels
Channel aggregation
1 & 3
2 & 4
1 & 4
Notes: The start and stop frequencies are nominal values. The frequency spectrum of the transmitted signal needs to conform to the transmit spectral mask as well as any regulatory requirement.

## Slide 6: PHY frame structure design
To be presented in detail at the September meeting
ANT4
ANT3
ANT2
ANT1
MIMO-CES #4
MIMO-CES #3
MIMO-CES #2
MIMO-CES #1
M streams data
MIMO channel estimation
MIMO PHY frame structure example when M=4
MIMO-STF
MIMO-STF
MIMO-STF
MIMO-STF
Payload #4
Header #4
Payload #3
Header #3
Payload #2
Header #2
Payload #1
Header #1
Notes: TJC打ち合わせで決定：
FFTサイズは 64シンボル， GIはそのうち8 シンボル
※11adのSTFは，Ga128*16 + -Ga128*1= 1152シンボル

## Slide 7: 2. HRCP channel model HRCP channel measurement scenario
Kiosk side
Microstrip antenna
In order to extract the values of channel model,
channel impulse response was measured using a network analyzer.
Portable device
side
(with chassis)
Distance
40 mm
Distance
40 mm
10 mm
10 mm
Measurement area*
Portable device
Kiosk
Network Analyzer
Port 2
Port 1
x
y
z
System configuration
* The antenna in the portable device side is moved around within the square area and a number of impulse responses was measured. The responses are averaged along this area to get the power delay profile.

## Slide 8: Channel measurement and parameter extraction procedure
Frequency domain measurement
10 mm
10 mm
Network Analyzer
Port 2
Port 1
Similar measurement to that described in the CMD.
Time domain
channel responses
at thousands of points in the measurement area
Averaging
Frequency domain
channel responses (S21) at thousands of points in the measurement area
IFFT
Power delay profile (PDP):
averaged through the measurement area in x-y plane
Channel
Measurement area

## Slide 9: PDP and channel model
Chart: τ [nsec]
Sample# (oversample=4) | Time [nsec] | Level[dB] | Phase
0 | 0 | 0.00 | 0°
1 | 0.145 | -6.88 | random
2 | 0.29 | -13.24 | random
3 | 0.435 | -25.37 | random
4 | 0.58 | -31.30 | random
5 | 0.725 | -40.77 | random
6 | 0.87 | -43.38 | random
7 | 1.015 | -49.56 | random
8 | 1.16 | -49.59 | random
9 | 1.305 | -49.06 | random
10 | 1.45 | -41.16 | random
11 | 1.595 | -52.24 | random
12 | 1.74 | -50.72 | random
Channel model
PDP obtained from the measurement
Notes: some cluster is included
(fixed value)

## Slide 10: MIMO extension of channel model
A set of SISO responses
Rx#1
Rx#2
Tx#1
Tx#2
MIMO channel response is in a matrix
MIMO transmission channel
In this figure, the number of branches is M = 2.
Rx#1
Rx#2
Tx#1
Tx#2
D
d
MIMO propagation channel
h22
h11
h21
h12
hji
Each is a SISO impulse response model. The propagation distance is reflected in each model as the propagation loss and phase rotation in the first tap.
Notes: Time diff. h21 and h11 = 5/4/c = 4 [psec]

## Slide 11: MIMO extension: how to make hji
τ [samples]
|hji| [dB]
0
1
2
…
First tap = LOS component:
rji is the geometrical distance between Tx#i and Rx#j
Phase: rji*(2π/λ)
Amplitude: (λ/4πrji)2
Each has LOS component as the first arrival wave (at the first tap).
Rx#i
Tx#i
Rx#j
Tx#j
r
Delayed taps:
Phase: random
Amplitude:(λ/4πr)2
hji
MIMO transmission in HRCP:
Propagation environment in which the LOS component is dominant

## Slide 12: MIMO extension: Optimum element spacing
Chart: Transmission distance, D / λ0
M = 16
M = 8
M = 4
M = 2
M = 9
As mentioned in the CMD,
Element spacing is an important factor in the MIMO channel
Hence the element spacing will be optimized in the simulation

## Slide 13
MIMO extension:
Array size
d
D
Tx array
Rx array
Microstrip antenna
Basically the propagation channel is LOS MIMO.
when the number of elements M = 16 and the transmission distance D = 20 mm, optimum element spacing will be d = 5.5 mm hence array is 20mm x 20 mm. (Reference: 3e CMD)
PHY Criteria 6

## Slide 14: Thank you