## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Proposal for SRMM MAC PIB in Technical Guidance Document]
Date Submitted: [11 July, 2015]
Source: [Hidetoshi Yokota and Ruben Salazar] Company [Landis&Gyr]
Address: [1-2-9 Nishi Shimbashi Minato-ku, Tokyo 105-0003, Japan,
30000 Mill Creek Av., Alpharetta, GA 30022, USA ]
Voice: [+81 3-5532-7455, +1 678 258 3165], E-Mail:[hidetoshi.yokota@landisgyr.com, ruben.salazar@landisgyr.com]
Re: [“TG4s Technical Guidance Document”, IEEE 802.15-14-0555-05-004s]
Abstract: [This contribution proposes SRMM MAC PIB that should be considered in the Technical Guidance Document for measuring spectrum resources in WPAN.]
Purpose: [Discussion and approval]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and July be made publicly available by P802.15.

## Slide 2
Proposal for SRMM MAC PIB in Technical Guidance Document
Authors:

## Slide 3: Outline of the proposal
Proposed General MAC PIB for SRMM
  Follows 8.4.2.x in [1]
Discussion
  Definition of specific MAC PIB attributes
  Reuse of existing attributes
Reference [1] IEEE802.15.4-REVc-D00

## Slide 4: Proposal for SRMM MAC PIB (Section 5)
5.2.1 General MAC PIB for SRMM
Attribute | Type | Range | Description | Default
macChannelLoadEnabled | Boolean | TRUE, FALSE | If TRUE, the device is using functionality specific to Channel Load | -
macLinkStatisticsEnabled | Boolean | TRUE, FALSE | If TRUE, the device is using functionality specific to Link Statistics | -
macInterferenceMeasurementEnabled | Boolean | TRUE, FALSE | If TRUE, the device is using functionality specific to Interference Measurement | -
macNodeStatisticsEnabled | Boolean | TRUE, FALSE | If TRUE, the device is using functionality specific to Node Statistics | -

## Slide 5: Proposal for SRMM MAC PIB (Cont’d)
Attribute | Type | Range | Description | Default
macChannelOccupancyStatisticsEnabled | Boolean | TRUE, FALSE | If TRUE, the device is using functionality specific to Channel Occupancy Statistics | -
macWakeupStatisticsEnabled | Boolean | TRUE, FALSE | If TRUE, the device is using functionality specific to Wakeup Statistics | -
macTimeSynchErrorEnabled | Boolean | TRUE, FALSE | If TRUE, the device is using functionality specific to Time Synch Error | -
macSecurityEnabled | Boolean | TRUE, FALSE | If TRUE, the device is using functionality specific to SRMM Security | -

## Slide 6: Proposal for SRMM MAC PIB (Cont’d)
Attribute | Type | Range | Description | Default
macLatencyEnabled | Boolean | TRUE, FALSE | If TRUE, the device is using functionality specific to Network Latency | -
macReportEnabled | Boolean | TRUE, FALSE | If TRUE, the device is using functionality specific to Management Report | -

## Slide 7: Discussion
SRMM specific MAC PIB attributes can be defined based on the table for Functional Requirements
  Examples of Channel Load attributes
Attribute | Type | Range | Description | Default
macED | Integer | 0x0000-0xffff | An estimate of the received signal power within the bandwidth of the channel. | -
macCCA | Integer | 0x0000-0xffff | The duration for which the measuring device determined the channel to be busy | -
macActiveScan | Integer | 0x0000-0xffff | Active scan time period | -
… | … | … | … | -

## Slide 8: Discussion (cont’d)
It is necessary to study more and well define:
  “Interference measurement”
  “Channel Occupancy”
  “Latency”
MAC performance metrics specific MAC PIB attributes are also defined in Table 144 of Ref [1]
  macRetryCount
  macTxSuccessCount
  macRxSuccessCount
  …  It is necessary to determine whether to use these parameters or define separate attributes