## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: High Efficiency RTS/CTS Handshaking Minimizing Exposed Node Problems
Date Submitted: July ,2015
Source: [Nah-Oak Song, Junhyuk Kim]1, [Byung-Jae Kwak]2 Company [KAIST]1, [ETRI]2
Address []1,
[218 Gajeong-ro, Yuseong-gu, Daejeon, Korea]2
E-Mail:[nsong@kaist.ac.kr, kim.jh@kaist.ac.kr]1, [bjkwak@etri.re.kr]2
Re: P802.15.8 Draft D0.12.0
Abstract: Proposes a new RTS/CTS handshaking mechanism that improves efficiency by minimizing exposed node problem.
Purpose: Discussion
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: High Efficiency RTS/CTS Handshaking Minimizing Exposed Node Problems
July 2015
IEEE 802.15 Plenary

## Slide 3: Terminology
NAV
“The network allocation vector (NAV) is a virtual carrier-sensing mechanism. […] The MAC layer frame headers contain a duration field that specifies the transmission time required for the frame, in which time the medium will be busy. The stations listening on the wireless medium read the duration field and set their NAV, which is an indicator for a station on how long it must defer from accessing the medium.”
  (Source: Wikipedia)

## Slide 4: Communication Range (1)
R_control : comm. range of control packet such as RTS, CTS, ACK
R_data : comm. range of data packet ( ≤ R_control )
R_carrier : carrier sensing range (assume R_carrier = R_control)

## Slide 5: Communication Range (2)
Case 1: the sender and the receiver are closely located
  High transmission rate can be chosen, reducing the communication range

## Slide 6: Communication Range (3)
Case 2: the sender and the receiver are not closely located
  Low transmission rate is chosen, making the communication range long

## Slide 7: Original RTS/CTS Handshaking
NAV Setting Mechanism

## Slide 8: Proposed RTS/CTS Handshaking (1)
Original RTS/CTS handshaking
  Removes hidden nodes
  Instead, creates more exposed nodes
  Thus, results in inefficient use of valuable resource
Proposed RTS/CTS handshaking
  Minimizes exposed nodes created by the original RTS/CTS handshaking
  By smart NAV setting mechanism

## Slide 9: Proposed RTS/CTS Handshaking (2)
When RTS is sent:
  PDs in the comm. range of RTS (PDRTS) set NAV for the duration of CTS

## Slide 10: Proposed RTS/CTS Handshaking (3)
When CTS is sent:
  PDs in the comm. range of CTS (PDCTS) set NAV for the duration of DATA

## Slide 11: Proposed RTS/CTS Handshaking (4)
When Data packet is sent:
  PDs receiving data packet (PDData) sets NAV for duration of ACK

## Slide 12: Proposed RTS/CTS Handshaking (5)
NAV Setting Mechanism

## Slide 13: Conclusion
There will be a lot of hidden and exposed node problems in PAC
The original RTS/CTS handshaking solves hidden node problem, but creates more exposed nodes
The proposed RTS/CTS handshaking is a simple way to minimize exposed node problem