## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [A MAC frame format including Information Elements]
Date Submitted: [16th July 2015 ]
Source: [Billy Verso]
Company: [DecaWave]
Address: [Adelaide Chambers, Peter Street, Dublin 8, Ireland]
Voice:[1353 1 6975030] Fax: []
E−Mail:[billy.verso “at” decawave.com]
Re: [A presentation of a MAC frame format including Information Elements]
Abstract: [Presents a MAC frame format proposal for 802.15.8 that includes information elements]
Purpose: [Material for discussion in IEEE 802.15 TG8]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
This document presents a method to include Information Elements (IEs) into the 802.15.8 MAC Frame
It also presents a possible encoding method for the IEs
This is not the same as the IE encoding used in 802.15.4
Introduction

## Slide 3: General MAC frame format with IEs
The above is based generally on 802.15.4 (“2015?”) with the addressing fields sized as per TG8’s current thinking
The difference between Header and Payload IEs is that Header IEs are not encrypted while Payload IEs may be encrypted

## Slide 4: Frame control field (EXAMPLE)

## Slide 5
IE ID value | IE Name | Acronym | Content | Content Length (octets)
1 | Ranging Request Reply Time IE | RRRT IE | NONE | 0
2 | Ranging Reply Time Instantaneous IE | RRTI IE | RX to TX Reply Time | 4
3 | Ranging Reply Time Deferred IE | RRTD IE | RX to TX Reply Time | 4
4 | Ranging Preferred Reply Time IE | RPRT IE | Preferred Reply Time | 4
5 | Ranging Control Double-sided TWR IE | RCDT IE | Control Info | 1
6 | Ranging Round Trip Measurement IE | RRTM IE | TX to RX round trip time | 4
7 | Ranging Time-of-Flight IE | RTOF IE | TX to RX round trip time | 4
IE’s defined for ranging
IE ID value | IE Name | Acronym | Content | Content Length (octets)
0 | IE List terminator IE | TERM IE | NONE | 0
One more IE is needed

## Slide 6
The above is would allow some future flexibility
The short form is a very limited resource and will be prized
If no other use more important IE usage emerges we should use the shortest ones for the Ranging IEs
  Shorter messages are better for higher density networks and reduced power drain
Proposed Payload IE encoding

## Slide 7
The scheme presented here represents some initial thoughts on how 802.15.8 could encode its IEs
This probably need to be developed a little more before we write the text and so is subject to change
Conclusion