## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Proposal for IEEE802.15.3e – Single Carrier PHY]
Date Submitted: [10 September 2015]
Source: [Makoto Noda(1), Ken Hiraga, Jae Seung Lee, Itaru Maekawa, Ko Togashi, (representative contributors), all contributors are listed in “Contributors” slide]
Company: [ETRI, JRC, NTT, Toshiba, Sony1]
Address1: [1-7-1 Konan, Minato-ku, Tokyo 108-0075]
E-Mail1: [MakotoB.Noda at jp.sony.com (all contributors are listed in “Contributors” slide)]
Abstract: This document presents a Single-Carrier PHY of the full MAC/PHY proposal for HRCP.
Purpose: To propose a full set of specifications for TG 3e.
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributors acknowledge and accept that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Contributors
Name | Affiliation | Email
Jae Seung Lee | ETRI | jasonlee@etri.re.kr
Moon-Sik Lee | ETRI | moonsiklee@etri.re.kr
Itaru Maekawa | Japan Radio Corporation | maekawa.itaru@jrc.co.jp
Lee Doohwan | NTT Corporation | lee.doohwan@lab.ntt.co.jp
Ken Hiraga | NTT Corporation | hiraga.ken@lab.ntt.co.jp
Masashi Shimizu | NTT Corporation | masashi.shimizu@upr-net.co.jp
Keitarou Kondou | Sony Corporation | Keitarou.Kondou at jp.sony.com
Hiroyuki Matsumura | Sony Corporation | Hiroyuki.Matsumura at jp.sony.com
Makoto Noda | Sony Corporation | MakotoB.Noda at jp.sony.com
Masashi Shinagawa | Sony Corporation | Masashi.Shinagawa at jp.sony.com
Ko Togashi | Toshiba Corporation | ko.togashi@toshiba.co.jp
Kiyoshi Toshimitsu | Toshiba Corporation | kiyoshi.toshimitsu@toshiba.co.jp

## Slide 3: Proposal for IEEE802.15.3e High-Rate Close Proximity System
September 10, 2015

## Slide 4: Single Carrier (SC) PHY
Extremely high PHY-SAP payload-bit rates outperforming those of 15.3c
Min. 2 Gb/s and Max. 13 Gb/s, using a single channel with 2.16 GHz bandwidth
Reusing the best error-correction code respecting 15.3c
Reusing the rate-14/15 low-density parity-check (LDPC) code
Introducing a new rate-11/15 LDPC code whose decoder compatible with that for the rate-14/15 LDPC code to obtain moderate bit rates
New preamble, comparing 15.3c:
Decrease the length
Double the zero-auto correlation zone of the channel-estimation sequence
MIMO in SC PHY for 100 Gb/s is described in 15-0661/r0.
SC PHY proposal is also described in a draft version.

## Slide 5: Introduction
A full PHY/MAC proposal, as a final version
Extremely high PHY-SAP payload-bit rates outperforming those of 15.3c
Min. 2 Gb/s and Max. 13 Gb/s, using a single channel with 2.16 GHz bandwidth
Max. 100 Gb/s, using MIMO and a channel aggregation
Reusing the best error-correction code respecting 15.3c
Reusing the rate-14/15 low-density parity-check (LDPC) code
Introducing a new rate-11/15 LDPC code whose decoder compatible with that for the rate-14/15 LDPC code to obtain moderate bit rates
Simple PHY/MAC format enabling low-power system
Fulfills TG3e’s requirements in the technical guidance document (TGD)

## Slide 6: Channel assignments
a The start and stop frequencies are nominal values. The frequency spectrum of the transmitted signal needs to conform to the transmit spectral mask as well as any regulatory requirement.
MmWave-PHY channelization
CHNL_ID | Start frequencya | Center frequency | Stop frequencya
1 | 57.240 | 58.320 | 59.400
2 | 59.400 | 60.480 | 61.560
3 | 61.560 | 62.640 | 63.720
4 | 63.720 | 64.800 | 65.880

## Slide 7: Transmit spectral mask
0
1
2
3
–1
–2
–3
(f – fc) (GHz)
0
–10
–20
–30
(same as that in 802.11ad)
(0.94, 0)
(1.2, –17)
(2.7, –22)
(3.06, –30)
(–0.94, 0)
(–1.2, –17)
(–2.7, –22)
(–3.06, –30)
Power (dB)

## Slide 8: Modulation and coding scheme (MCS)
PW: pilot word
PW length/sub-block length = 0.125
MCS identifier | single-carrier modulation | FEC Rate | PHY-SAP payload-bit rate (Gb/s) | 
 |  |  | w/o PW | w/ PW
0 | π/2 QPSK | 11/15 | 2.5813 | 2.2587
1 | π/2 QPSK | 14/15 | 3.2853 | 2.8747
2 | 16QAM | 11/15 | 5.1627 | 4.5173
3 | 16QAM | 14/15 | 6.5707 | 5.7493
4 | 64QAM | 11/15 | 7.7440 | 6.7760
5 | 64QAM | 14/15 | 9.8560 | 8.6240
6 | 256QAM | 14/15 | 13.1413 | 11.4987
Minimum 2 Gb/s and Maximum 13 Gb/s MCSs using a single channel

## Slide 9: Forward Error Correction
Gap between SNRr* obtained by floating point simulation and the Shannon limit in binary AWGN channel for codes employed in standards.
RS(240,224) on GF(28) T J 0.933 9.77 6.51 –3.26
LDPC(1440,1344) 15.3c 0.933 8.46 6.51 –1.96
LDPC(672,588) 15.3c 0.875 7.55 5.27 –2.28
LDPC(672,546) 11ad 0.813 6.96 4.26 –2.70
LDPC(672,504) 11ad 0.750 5.91 3.39 –2.53
LDPC(1440,1056) New 0.733 5.36 3.17 –2.20
SNRr*: signal-to-noise ratio required for a bit-error rate of 10–6
Reuse the 14/15 LDPC code and a new 11/15 LDPC code with the best code efficiencies.
code standard rate SNRr
(dB)
(dB)
(dB)
Shannon
limit
gap
rate
14/15
rate
11/15

## Slide 10: MCS performance, FER v.s. Eb/N0
Frame length = 214 B
Eb/N0 (dB)
Frame-error Rate, FER (dB)
FER = 0.08
Chart: 
| -1.074857 | -0.874857 | -0.67485700000000004 | -0.47485699999999997 | -0.27485700000000002 | -7.4857000000000007E-2 | 0.125143 | 0.32514300000000002 | 0.52514300000000003 | 0.72514299999999998 | 0.92514300000000005 | 1.125143 | 1.325143 | 1.5251429999999999 | 1.7251430000000001 | 1.925143 | 2.125143 | 2.3251430000000002 | 2.5251429999999999 | 2.7251430000000001 | 2.9251429999999998 | 3.125143 | 3.3251430000000002 | 3.5251429999999999 | 3.7251430000000001 | 3.9251429999999998 | 4.1251429999999996 | 4.3251429999999997 | 4.5251429999999999 | 4.7251430000000001
QPSK 11/15 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0.93636 | 0.57222 | 0.17241 | 0.06135
QPSK 14/15 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0.875 | 0.46364 | 0.19057 | 0.053763
16QAM 11/15 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0.98182 | 0.78462 | 0.515 | 0.28857 | 0.12195 | 0.045455
16QAM 14/15 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0.80769 | 0.42917 | 0.20833 | 0.06993
64QAM 11/15 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0.99091 | 0.95455 | 0.80769 | 0.57222 | 0.4 | 0.25641 | 0.15692 | 0.098039 | 0.051795
64QAM 14/15 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0.99091 | 0.90909 | 0.57222 | 0.2439 | 0.11882 | 0.04329
256QAM 14/15 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0.98182 | 0.8 | 0.57222 | 0.34 | 0.16833 | 0.077519
 | 0.08 | 0.08
(incorporating RF impairments and channel model)

## Slide 11: Link budget of SC PHY using a single channel
*incorporating RF impairments and channel model
MCS |  | MCS0 | MCS1 | MCS2 | MCS3 | MCS4 | MCS5 | MCS6
Tx | frequency for CH4 (GHz) | 64.8 | 64.8 | 64.8 | 64.8 | 64.8 | 64.8 | 64.8
 | PHY-SAP bit rate (Gb/s) | 2.5813 | 3.2853 | 5.1627 | 6.5707 | 7.7440 | 9.8560 | 13.1413
 | Tx power (dBm) | -23.54 | -20.55 | -16.4 | -13.71 | -9.82 | -7.61 | -1.7
 | Tx antenna gain (dBi) | 6 | 6 | 6 | 6 | 6 | 6 | 6
channel | distance(m) | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1
 | 1m loss (dB) | 68.67 | 68.67 | 68.67 | 68.67 | 68.67 | 68.67 | 68.67
 | path Loss (dB) | -20.00 | -20.00 | -20.00 | -20.00 | -20.00 | -20.00 | -20.00
 | propagation loss index | 2 | 2 | 2 | 2 | 2 | 2 | 2
 | Rx input level (dBm) | -66.21 | -63.22 | -59.07 | -56.38 | -52.49 | -50.28 | -44.37
 | average noise power per bit (dBm) | -79.88 | -78.83 | -76.87 | -75.82 | -75.11 | -74.06 | -72.81
Rx | Rx antenna gain (dBi) | 6 | 6 | 6 | 6 | 6 | 6 | 6
 | noise figure (dB) | 8 | 8 | 8 | 8 | 8 | 8 | 8
 | implementation loss (dB) | 6 | 6 | 6 | 6 | 6 | 6 | 6
 | shadowing margin (dB) | 1 | 1 | 1 | 1 | 1 | 1 | 1
 | receiving Eb/N0 (dB) | 4.67 | 6.61 | 8.80 | 10.44 | 13.62 | 14.78 | 19.44
required Eb/N0 |  | 4.67 | 6.61 | 8.8 | 10.44 | 13.62 | 14.78 | 19.44
margin |  | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00

## Slide 12: PHY header format
Field Name | Number of bits | Start bit | Description
MCS | 3 | 0 | Index into the Modulation and Coding Scheme table
Pilot word | 1 | 3 | Shall be set to 1 if the pilot word is used
Scrambler seed ID | 4 | 4 | The initial state for payload scrambling
Reserved | 4 | 8 | Set to 0, ignored by the receiver
Frame length | 20 | 13 | Number of data octets in the PSDU

## Slide 13: Frame header construction process
PHY
header
MAC
header
HCS
PHY header
MAC header
Append and scramble
HCS
caluculation
scrambled
Extended Hamming
encode
Spreader
π/2-shift BPSK
mapper
Subblock
builder
PHY
header
MAC
header
HCS
scrambled
coded
scramble
Scrambled
stuff
bits
Stuff bits

## Slide 14: 16-bit Header CRC* for HCS
Bit-error Rate, bER
Undetected Error Probability
generator polynomial: 1A12B (TG3e, dmin*2 = 6), 11021 (ITU-T, dmin*2 = 4)
1-error event/10 years
for 1 G packets/day
*1 CRC: cyclic-redundancy-check code
*2 dmin: minimum Hamming distance
code-word length = 128 bits

## Slide 15: Proposed preamble structure
Frame format
TG3e
Preamble
Header
Payload
–a
b
a
b
a
–b
a
b
–a
b
a
a
a
a
b
first transmitted
last transmitted
transmission order
reference:
IEEE 802.15.3c SC, HR
a
a
a
–a
–a
a
b
a
–b
a
b
a
–b
a
b
a
SYNC
14 GCSs
SFD
4 GCSs
CES
9 GCSs
128*27 = 3456 chips: 1.96 µs
SYNC
14 GCSs
SFD
1 GCS
CES
11 GCSs
128*26 = 3328 chips: 1.89 µs
GCS: Golay complementary sequence, a or b, here 128-bit length
SYNC: synchronization sequence
SFD: start frame delimiter
CES: channel-estimation sequence

## Slide 16: Cross-correlation Properties
(a) 15.3c
Time Slot
(b) TG3e
Time Slot
R = [a128 –a128]
r: a noiseless received sequences
R: a reference sequence
Cross Correlation of
r and R
SYNC
CES
SFD
+256
+14
–16
R = [a128 –a128]
Cross Correlation of
r and R
+22
+256
–26
SYNC
CES
SFD
The last 3 GCS of SFD in 15.3c are used for detection of the header rate, either medium rate (MR) or high rate (HR).
–38 %
–36 %

## Slide 17: Performance of Frame synchronization
CNR dependence of FER due to synchronization or header or payload
Frame-error Rate, FER
Carrier to Noise Ratio, CNR (dB)
Missed detection*1
False alarm*2
*1: the probability of a correlation between a received sequence and a reference sequence being below a threshold at the correct timing position.
*2: the probability of a correlation between a received sequence and a reference sequence being above a threshold at the incorrect timing position.
The threshold of sync. detection: 80
(extrapolated)
(extrapolated)
0.9 dB gain for 15.3c
Estimated > 3 dB margin for header

## Slide 18: Extended Hamming encoder
i0 | i1 | i2 | i3 | p0 | p1 | p2 | p3
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 1 | 1 | 1 | 0
0 | 0 | 1 | 0 | 1 | 0 | 1 | 1
0 | 0 | 1 | 1 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 1 | 1 | 0 | 0 | 1
0 | 1 | 1 | 0 | 1 | 1 | 0 | 0
0 | 1 | 1 | 1 | 0 | 0 | 1 | 0
1 | 0 | 0 | 0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0 | 0 | 1 | 1
1 | 0 | 1 | 0 | 0 | 1 | 1 | 0
1 | 0 | 1 | 1 | 1 | 0 | 0 | 0
1 | 1 | 0 | 0 | 1 | 0 | 1 | 0
1 | 1 | 0 | 1 | 0 | 1 | 0 | 0
1 | 1 | 1 | 0 | 0 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Table for encoding
The frame header shall be encoded with the (8,4) extended hamming code.
For every input 4-bit sequence, denoted as {i0, i1, i2, i3}, the encoder shall outputs the sequence followed by a 4-bit-parity sequence {p0, p1, p2, p3} determined by the table.
input data
output data
input 4-bit seq.
4-bit parity seq.

## Slide 19: Performance of Header Coding
Chart: Carrier to Noise Ratio, CNR (dB)
| -10 | -9.75 | -9.5 | -9.25 | -9 | -8.75 | -8.5 | -8.25 | -8 | -7.75 | -7.5 | -7.25 | -7 | -6.75 | -6.5 | -6.25 | -6 | -5.75 | -5.5 | -5.25 | -5 | -4.75 | -4.5 | -4.25 | -4 | -3.75 | -3.5 | -3.25 | -3 | -2.75 | -2.5 | -2.25 | -2 | -1.75 | -1.5 | -1.25 | -1 | -0.75 | -0.5 | -0.25 | 0 | 0.25 | 0.5 | 0.75 | 1 | 1.25 | 1.5 | 1.75 | 2 | 2.25 | 2.5
MCS0 10 octets | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0.999 | 0.996 | 0.993 | 0.973 | 0.96 | 0.923 | 0.864 | 0.79 | 0.693 | 0.591 | 0.475 | 0.335 | 0.221 | 0.138 | 0.09 | 0.052 | 0.027 | 0.01275 | 0.0068 | 0.002575 | 0.00072993 | 0.00028818 | 0.00012563 | 4.2105e-05 | 1.6767e-05 | 4e-06
MCS0 132 octets | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0.996 | 0.965 | 0.846 | 0.562 | 0.273 | 0.097 | 0.025 | 0.0045909 | 0.00068966 | 0.0001224 | 2.3052e-05
Proposed Header MCS is more robust than the lowest MCS for payload

## Slide 20: A Simple LDPC encoder
A systematic (n, k) quasi-cyclic code, such that every cyclic shift of a codeword by p symbols yields another codeword, can be encoded by using p generator polynomials and an (v = n–k+p–1)-stage shift register*.
D
Select a generator polynomial g(n– i–1)modp*xp–1–{(n–i–1)modp} at time i, where i = 0 is defined as the time that the first v information bits are stored in the v-stage shift registers; v = 96+15–1 = 110 for a rate-14/15 LDPC code and v = 96*4+15–1 = 398 for a rate-11/15 LDPC code.
+
D
+
…
D
+
information bits
parity bits
information bits
…
(for x0)
(for x1)
(for xv– 1)
0
(Zero is selected after k information bits are received)
* H. Yamagishi and M. Noda, Proc. IEEE, pp.78-83, Sep. 2008

## Slide 21: Proposed Overlaid-rate-compatible (ORC) LDPC Codes
A low-rate parity-check matrix, as a simplified example of an 11/15 LDPC code
A high-rate parity-check matrix, as a simplified example of a 14/15 LDPC code
1 0 0 0 0 0 0
0 1 0 0 0 0 0
0 0 1 0 0 0 0
0 0 0 1 0 0 0
0 0 0 0 1 0 0
0 0 0 0 0 1 0
0 0 0 0 0 0 1
0 0 0 0 1 0 0
0 0 0 0 0 1 0
0 0 0 0 0 0 1
1 0 0 0 0 0 0
0 1 0 0 0 0 0
0 0 1 0 0 0 0
0 0 0 1 0 0 0
0 0 0 0 0 0 1
1 0 0 0 0 0 0
0 1 0 0 0 0 0
0 0 1 0 0 0 0
0 0 0 1 0 0 0
0 0 0 0 1 0 0
0 0 0 0 0 1 0
0 0 0 0 0 1 0
0 0 0 0 0 0 1
1 0 0 0 0 0 0
0 1 0 0 0 0 0
0 0 1 0 0 0 0
0 0 0 1 0 0 0
0 0 0 0 1 0 0
0 0 0 0 0 0 1
1 0 0 0 0 0 0
0 1 0 0 0 0 0
0 0 1 0 0 0 0
0 0 0 1 0 0 0
0 0 0 0 1 0 0
0 0 0 0 0 1 0
1 0 0 0 0 0 0
0 1 0 0 0 0 0
0 0 1 0 0 0 0
0 0 0 1 0 0 0
0 0 0 0 1 0 0
0 0 0 0 0 1 0
0 0 0 0 0 0 1
0 0 0 0 1 0 0
0 0 0 0 0 1 0
0 0 0 0 0 0 1
1 0 0 0 0 0 0
0 1 0 0 0 0 0
0 0 1 0 0 0 0
0 0 0 1 0 0 0
0 1 0 0 0 0 0
0 0 1 0 0 0 0
0 0 0 1 0 0 0
0 0 0 0 1 0 0
0 0 0 0 0 1 0
0 0 0 0 0 0 1
1 0 0 0 0 0 0
1 0 0 0 0 0 1
1 1 0 0 0 0 0
0 1 1 0 0 0 0
0 0 1 1 0 0 0
0 0 0 1 1 0 0
0 0 0 0 1 1 0
0 0 0 0 0 1 1
1 0 0 0 1 0 0
0 1 0 0 0 1 0
0 0 1 0 0 0 1
1 0 0 1 0 0 0
0 1 0 0 1 0 0
0 0 1 0 0 1 0
0 0 0 1 0 0 1
0 0 0 0 1 0 1
1 0 0 0 0 1 0
0 1 0 0 0 0 1
1 0 1 0 0 0 0
0 1 0 1 0 0 0
0 0 1 0 1 0 0
0 0 0 1 0 1 0
0 1 0 0 0 1 0
0 0 1 0 0 0 1
1 0 0 1 0 0 0
0 1 0 0 1 0 0
0 0 1 0 0 1 0
0 0 0 1 0 0 1
1 0 0 0 1 0 0
A check matrix of a high-rate code composed of overlay of sub-matrices in a check matrix of a low-rate code. This structure enables to share a belief-propagation decoder for the high-rate and low-rate LDPC codes.

## Slide 22: Simple receiver: advantage of short coded header
DL
MUX
Demod
header/payload mod
Sync &
Header
Dec
header/payload timing
D: delay operator
received signal
received data
Payload
Dec
A block diagram of a receiver
This block can be removed.
(a) conventional
Preamble
MCS
Length etc.
Payload
(b) improved
Timing diagram of header/payload mod
received signal
L
L
L: demod delay