## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Proposal for IEEE802.15.3e – MAC :Aggregation and Retransmission]
Date Submitted: [10 September 2015]
Source: [Itaru Maekawa (1), Jae Seung Lee, Ken Hiraga, Makoto Noda, Ko Togashi, (representative contributors), all contributors are listed in “Contributors” slide]
Company: [ETRI, JRC1, NTT, Sony, Toshiba]
Address1: [Mitaka, Tokyo, Japan]
E-Mail1: [Maekawa.Itaru at jrc.co.jp (all contributors are listed in “Contributors” slide)]
Abstract: This document presents an overview of the full MAC/PHY proposal for HRCP.
Purpose: To propose a full set of specifications for TG 3e.
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributors acknowledge and accept that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
Contributors
Name | Affiliation | Email
Jae Seung Lee | ETRI | jasonlee at etri.re.kr
Moon-Sik Lee | ETRI | moonsiklee at etri.re.kr
Itaru Maekawa | Japan Radio Co., Ltd. | maekawa.itaru at jrc.co.jp
Doohwan Lee | NTT Corporation | lee.doohwan at lab.ntt.co.jp
Ken Hiraga | NTT Corporation | hiraga.ken at lab.ntt.co.jp
Masashi Shimizu | NTT Corporation | masashi.shimizu at upr-net.co.jp
Keitarou Kondou | Sony Corporation | Keitarou.Kondou at jp.sony.com
Hiroyuki Matsumura | Sony Corporation | Hiroyuki.Matsumura at jp.sony.com
Makoto Noda | Sony Corporation | MakotoB.Noda at jp.sony.com
Masashi Shinagawa | Sony Corporation | Masashi.Shinagawa at jp.sony.com
Ko Togashi | Toshiba Corporation | ko.togashi at toshiba.co.jp
Kiyoshi Toshimitsu | Toshiba Corporation | kiyoshi.toshimitsu at toshiba.co.jp

## Slide 3
Proposal for IEEE802.15.3e
High-Rate Close Proximity System
September 15, 2015

## Slide 4
  Block ACK vs Stack ACK
  :Performance Comparison (Homework@Wikoloa)
        HRCP Aggregation
3. Interface space, retransmission with Stack ACK and Recovery Process
Contents

## Slide 5: Block ACK vs Stack ACK :Performance Comparison (Homework@Wikoloa)

## Slide 6
Block ACK
  Effective way to save & share bandwidth among multiple devices, especially under high error or collision environments, however….This method has the following disadvantages:
    Higher complexity
    Larger buffer memory
    Larger potential latency
Stack ACK
  Practical way for HRCP, because …
    Bandwidth saving is not required, thanks to good BER environment
    Lower Complexity , simple hardware requirements
“Simple” Stack ACK
- Key Concept of HRCP MAC -
“Small” benefit versus cost (complexity)
for use cases of HRCP
“Stacked Coin”
FIFO Buffer

## Slide 7
Sub-F#N+4
Sub-F#N+3
Sub-F#N+2
Sub-F#N+1
ACK#M
Sub-F#M+4
Sub-F#M+3
Sub-F#M+2
Sub-F#M+1
ACK#N+4
Sub-F#N+8
Sub-F#N+7
Sub-F#N+6
Sub-F#N+5
ACK#M+4
Data Error
Or Buffer full
Sub-F#M+8
Sub-F#M+7
Sub-F#M+6
Sub-F#M+5
ACK#N+6
Sub-F#N+10
Sub-F#N+9
Sub-F#N+8
Sub-F#N+7
ACK#M+8
Time #1
ACK#M+8
ACK#N+6
Header Error
Time #2
Time #3
Time #4
ACK#N+6
ACK#N+12
ACK#M+10
Time #5
ACK#M+12
ACK#M+12
SIFS
SIFS
SIFS
IIFS
RIFS
IIFS
Sub-F#M+14
Sub-F#M+13
Sub-F#M+12
Sub-F#M+11
ACK#N+12
SIFS
Sync.lost
Dev.A
Dev.B
Dev.A
Dev.B
Dev.A
Dev.B
Dev.A
Dev.B
Dev.A
Dev.B
RIFS
SIFS
Sub-F#M+10
Sub-F#M+9
ACK#N+6
SIFS
SIFS
Sub-F#N+10
Sub-F#N+9
Sub-F#N+8
Sub-F#N+7
ACK#M+10
Sub-F#N+12
Sub-F#N+11
SIFS
SIFS
ACK#N+12
RIFS
ACK#M+12
IIFS
ACK#M+12
IIFS
Time Domain MAC Behavior

## Slide 8: Stack Ack: Performance Estimation Model
Time
Subframe#N+15
PHY Header
HCS
MAC Header
Subframe#N+1
Subframe#N
Subframe#N+31
PHY Header
HCS
MAC Header
Subframe#N+17
Subframe#N+16
SIFS
SIFS
SIFS
MPDU#N
FCS
Subframe#N
MAC
Subheader#N
HCS
PHY Header
HCS
MAC Header
PHY Header
HCS
MAC Header
Tperiod
 |  |  | unit
PHY Preamble | Tpr | 2 | usec
PHY-header+MAC-header +HCS | Lhd | 132 | bit
1760M BPSK, 1/2 ECC. | Rhead | 0.88 | Gbps
 | Thd | 2.15 | usec
16QAM wo pilot, 14/15 LDPC | Rphy | 6.57 | Gbps
 | Tsifs | 2 | usec
mpdu Length | Lmpd | 4 | kB
Sub-Header+HCS+FCS | Lsh | 11 | B
Aggregation Number | N | 16 | 
Tperiod | Tperiod | 86.44429 | usec
Parameters : Example
Simplified Estimation Model
When Frame Error is occurred with probability of FER, 50% of Sub-Frames (Average) are retransmitted.
MAC Throughput (MACtp) vs FER is calculated as below.
  FER=1-(1-BER)Lmpd・N
  :(BER:bit error rate)

## Slide 9: Block-Ack :Performance Estimation Model
Time
Subframe#N+15
PHY Header
HCS
MAC Header
Subframe#N+1
Subframe#N
PHY Header
HCS
MAC Header
Subframe#X
SIFS
SIFS
SIFS
MPDU#N
FCS
Subframe#N
MAC
Subheader#N
HCS
PHY Header
HCS
MAC Header
PHY Header
HCS
MAC Header
Tperiod
SIFS
Tretry
 |  |  | unit
PHY Preamble | Tpr | 2 | usec
PHY-header+MAC-header +HCS | Lhd | 132 | bit
1760M BPSK, 1/2 ECC. | Rhead | 0.88 | Gbps
 | Thd | 2.15 | usec
16QAM wo pilot, 14/15 LDPC | Rphy | 6.57 | Gbps
 | Tsifs | 2 | usec
mpdu Length | Lmpd | 4 | kB
Sub-Header+HCS+FCS | Lsh | 11 | B
Aggregation Number | N | 16 | 
Tperiod | Tperiod | 86.44429 | usec
Parameters : Example
Simplified Estimation Model
When Frame Error is occurred with probability of FER, “ONE” Sub-Frames are retransmitted.
MAC Throughput (MACtp) vs FER is calculated as below.
  FER=1-(1-BER)Lmpd・N
  :(BER:bit error rate)

## Slide 10: Stack ACK vs Block-ACK :Throughput Comparison
 |  |  | unit
PHY Preamble | Tpr | 2 | usec
PHY-header+MAC-header +HCS | Lhd | 132 | bit
1760M BPSK, 1/2 ECC. | Rhead | 0.88 | Gbps
 | Tsifs | 2 | usec
Sub-Header+HCS+FCS | Lsh | 11 | B
mpdu Length | Lmpd | 4 | kB
Common Parameters :
Chart: BER
| 1.0000000000000077E-10 | 1.0000000000000065E-9 | 1.0000000000000075E-8 | 1.0000000000000063E-7
Stack ACK | 99.9974 | 99.9744 | 99.7447 | 97.5044
Block ACK | 99.9992 | 99.9922 | 99.9222 | 99.2452
Chart: BER
| 1.0000000000000077E-10 | 1.0000000000000069E-9 | 1.0000000000000065E-8
Stack ACK | 99.9795 | 99.7956 | 97.9934
Block ACK | 99.9992 | 99.9922 | 99.9222
FER ～ 5%
FER ～ 4%
PHY Rate :6.57Gbps (16QAM, LDPC 14/15 )
Number of Aggregation:16
PHY Rate :52.6Gbps (16QAM x8 MIMO, LDPC 14/15 )
Number of Aggregation:128
As long as FER is less than 10% order, throughput advantage of Block ACK is negligible .
(If FER exceed 10% level, Rate adaptation System should work.)
Conclusion
Low Complexity Advantage of Stack ACK retransmission is significant
Performance Disadvantage of Stack ACK is negligible

## Slide 11: HRCP Aggregation

## Slide 12: HRCP Aggregation
PHY Header
Subframe#1
MSDU#1
MSDU#2
MSDU#3
MPDU#2
Fragment #1
MPDU#1
MPDU#3
Fragment #2
Fragmentation
HCS
MAC Header
Subframe#2
Subframe#3
Subframe#4
MAC Header
MPDU#4
Fragment #1
MPDU#5
Fragment #2
Fragmentation
Number of subframes and Ack Information are shown in MAC Header
MSDU Typ.length
Ether Frame :46～1518B
MTP/OBEX:64kB
MPDU:MAC Protocol Data Unit
MPDU Max length= single block size of TX Buffer
4kB (fixed value)
MPDU#4
FCS
More Fragment = 1
Subframe#4
MAC
Subheader#4
HCS
MPDU#3
FCS
More Fragment = 0
Subframe#3
MAC
Subheader#3
HCS
MPDU#2
FCS
More Fragment = 1
Subframe#2
MAC
Subheader#2
HCS
MPDU#1
FCS
More Fragment= 0
Subframe#1
MAC
Subheader#1
HCS
Subframe#N
N:255 maximum
“Stacked Coin”
FIFO Buffer
Sequence# and MPDU length are shown in Sub Header
More Fragment is set to 1 to indicate the corresponding subframe is not a final frame of fragmentation.
4kB is tentative number.

## Slide 13: HRCP deaggregation
PHY Header
MAC Header
HCS
Subframe#
1
Subframe#
2
Subframe#
3
Subframe#
4
Subframe#
n
MAC Header
MAC
Subheader#4
HCS
MPDU#4
Subframe#4
More fragment=1
FCS
MAC
Subheader#3
HCS
MPDU#3
More fragment=0
FCS
MAC
Subheader#2
HCS
MPDU#2
More fragment=1
FCS
MAC
Subheader#1
HCS
MPDU#1
More fragment=0
FCS
Subframe#3
Subframe#2
Subframe#1
MPDU#1
MPDU#2
(Fragment#1)
MPDU#3
(Fragment#2)
MPDU#4
(Fragment#1)
MPDU#5
(Fragment#2)
MSDU#2
MSDU#1
Defragmentation
Defragmentation
More fragment flag is set to 1 to indicate the corresponding subframe is not a final frame of fragmentation.
MPDU# and MPDU length are shown in Sub Header
Number of subframes and Ack information are shown in MAC Header
MSDU#3
m+n
Sequence Number
m+3
m+2
m+1
m+4

## Slide 14: Interface space, retransmission with Stack ACK and Recovery Process

## Slide 15
One cycle of PPAP
Kiyoshi Toshimitsu(Toshiba)
Beacon
PPAP
Associated
Unassociated
Device
PPC
Beacon
Setup Time < 2ms
Association
Response
Beacon
Stop beacon before sending
association response
PPAP
Beacon
Association
Request
Stk-Ack
Data Transfer Phase
Access Slot
RIFS
SIFS
Disassociation
Request
SIFS
or
RIFS
Unassociated
PPC may send Beacon
with new Next DEVID
Asynchronous Phase
Synchronous Phase
Asynchronous Phase (If recovery is needed)
Asynchronous Phase

## Slide 16: Ping-Pong Transmission in Synchronous Phase
Sub-F#N+4
Sub-F#N+3
Sub-F#N+2
Sub-F#N+1
ACK#M
Sub-F#M+4
Sub-F#M+3
Sub-F#M+2
Sub-F#M+1
ACK#N+4
Sub-F#N+6
Sub-F#N+5
ACK#M+4
Time #1
Time #2
SIFS
SIFS
ACK#N+6
SIFS
DEV.A
DEV.B
DEV.A
DEV.B
ACK#M+4
SIFS
SIFS
Sub-F#M+6
Sub-F#M+5
ACK#N+6
SIFS
Sub-F#N+10
Sub-F#N+9
Sub-F#N+8
Sub-F#N+7
ACK#M+6
Data Error
Sub-F#M+8
Sub-F#M+7
Sub-F#M+9
ACK#N+8
Time #3
SIFS
DEV.A
DEV.B
Sub-F#N+12
Sub-F#N+11
Sub-F#N+10
Sub-F#N+9
ACK#M+9
Buffer Full
Sub-F#M+13
Sub-F#M+12
Sub-F#M+11
Sub-F#M+10
ACK#N+10
Time #4
SIFS
DEV.A
DEV.B
SIFS
SIFS
Buffer Full Flag
“ one”
PHY
Header
MAC
Header
HCS
Sub
Header
Sub
Frame
HCS
FCS
Ping-Pong Transmission with SIFS
CSMA/CA is not used
To distinguish “Data Error”
or “Buffer full”

## Slide 17: Synchronous Phase to/from Asynchronous Phase
Sub-F#N+6
Sub-F#N+5
ACK#M+4
Sub-F#M+8
Sub-F#M+7
Sub-F#M+6
Sub-F#M+5
ACK#N+6
Sub-F#N+10
Sub-F#N+9
Sub-F#N+8
Sub-F#N+7
ACK#M+8
ACK#M+8
ACK#N+6
Header Error
Time #1
Time #2
Time #3
ACK#N+6
ACK#N+12
ACK#M+10
Time #4
ACK#M+12
SIFS
RIFS(A)
RIFS(B)
Sub-F#M+14
Sub-F#M+13
Sub-F#M+12
Sub-F#M+11
ACK#N+12
SIFS
PHY Error
DEV.A
DEV.B
DEV.A
DEV.B
DEV.A
DEV.B
DEV.A
DEV.B
RIFS(B)
SIFS
Sub-F#M+10
Sub-F#M+9
ACK#N+6
SIFS
SIFS
Sub-F#N+10
Sub-F#N+9
Sub-F#N+8
Sub-F#N+7
ACK#M+10
Sub-F#N+12
Sub-F#N+11
SIFS
SIFS
ACK#N+12
RIFS(B)
ACK#M+12
RIFS(A)
ACK#M+12
RIFS(A)
SIFS
PHY
Header
MAC
Header
HCS
Sub
Header
Sub
Frame
HCS
FCS
Recovery Process: Asynchronous Phase
Recovery Process: Asynchronous Phase
SIFS
ACK#N+12
Dev takes recovery process when it lost synchronization
CSMA/CA is not used
RIFS(B) >> RIFS(A)>>SIFS,ACK