## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Secret key agreement protocol for IEEE 802.15.8 PAC
Date Submitted: September 2015
Source: [Byung-Jae Kwak]1, [Sangseok Yun, Sanghun Im, Jeongseok Ha]2
Company [ETRI, Daejeon, Korea]1, [KAIST, Daejeon, Korea]2
Address [218 Gajeong-ro, Yuseong-gu, Daejeon, Korea]1, [291 Daehak-ro, Yuseong-gu, Daejeon, Korea]2
Voice: [+82-42-860-6618]1, [+82-42-350-7524]2
E-Mail: [bjkwak@etri.re.kr]1, [ssyun@kaist.ac.kr]2
Re:
Abstract: Proposal of the secret key agreement protocol in PHY for IEEE 802.15.8 PAC.
Purpose: Approval
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Secret key agreement protocol for IEEE 802.15.8 PAC
Sept. 2015

## Slide 3: Most Popular Passwords
 | 2012 | 2013 | 2014
1 | password | 123456 | 123456
2 | 123456 | Password | password
3 | 12345678 | 12345678 | 12345
4 | abc123 | qwerty | 12345678
5 | qwerty | abc123 | qwerty
6 | monkey | 123456789 | 123456789
7 | letmein | 111111 | 1234
8 | dragon | 1234567 | baseball
9 | 111111 | iloveyou | dragon
10 | baseball | adobe123 | Football

## Slide 4: Introduction
This document presents a secret key agreement protocol using physical layer features
This document proposes a secret key distribution protocol using channel impulse responses
By taking advantage of channel reciprocity and sequential key distillation, a pair of legitimate users can remotely share a secret key without resorting to a key management infrastructure
Specified methods are proposed and expected performances are evaluated

## Slide 5: General Secret Key Agreement Protocol
Maurer proposed a new approach to generate a random sequence achieving the perfect security [1]
  The process of generating a shared secret key consists of 3 phases
Share the common randomness between Alice and Bob
Alice & Bob agree on an identical random sequence
Hash function provides the perfect secrecy
Randomness Sharing
Information Reconciliation
Privacy Amplification
Channel response between Alice & Bob can be seen as the common randomness

## Slide 6: Secret Key Agreement Protocol
Alice (STA1)
Bob (STA1)
Quantizer
Quantizer
Reconciliation
Reconciliation
Channel Probing
Privacy Amplification
(w/ compression)
Privacy Amplification
(w/ compression)
Secret key,
Secret key,
-bits
-bits
-bits
-bits
Syndrome
Agree/Disagree
Channel Estimation
Channel Estimation
Randomness Sharing Protocol
Post Processing Protocol For Key Extraction
-bits
-bits
-bits

## Slide 7: Randomness Sharing Protocol
Mode 1
Mode 2
Stop probing if
Alice
Bob
process
process
process
Gathering Enough -bits
Gathering Enough -bits
Post
processing
: secret key
Probe Request (1)
Probe Response (1)
Probe Request
Probe Response
process
Channel estimation
Extract distinctive feature
(freq. time domain)
Quantization
process
Channel estimation
Extract distinctive feature
(freq. time domain)
Quantization
Alice
Bob
: secret key
process
process
Channel estimation
Extract distinctive feature
(freq. time domain)
Quantization
process
Channel estimation
Extract distinctive feature
(freq. time domain)
Quantization
process
Post
processing
RTS ()
CTS ()
RTS ()
CTS ()
Pass the latest quantized bits
Pass the latest quantized bits
Data Transmission
Data Transmission

## Slide 8: Randomness Sharing
The reciprocity of the propagation channel [2]
  Used as a source of common randomness
Spatial de-correlation assumption
  Channel responses are location-specific feature
  A secret key is extracted by exploiting random fluctuation of the wireless channel
Pilot symbols are used for estimating channel
  For randomness sharing, pilot symbols are located at all subcarriers except DC and guard subcarriers (i.e. 52 subcarriers)

## Slide 9: Channel Correlation Issue (1/2)
Residual channel correlation
  [3] reports there exists a strong correlation in measurements observed by adversaries located greater than a half-wavelength away from legitimate devices.
  However, this work does not consider the effect of the large scale fading on the channel correlation

## Slide 10: Channel Correlation Issue (2/2)
If the large scale fading is included, there exist a strong correlation in RSSI observed by Bob and Eve
  To minimize the channel correlation, eliminating the large scale fading is essential

## Slide 11: Hardware Experiment
Center frequency : 5.2GHz (cm)
The distance between Bob and Eve is 1m
Alice moves arbitrarily around the indoor office

## Slide 12: Hardware Experiment
The channel correlation between the RSSI observed at each node after eliminating the large scale fading
Channel | Correlation
Main channel | 0.9661
Wiretap channel | 0.0839

## Slide 13: Effect of Channel Correlation
Mutual information between correlated random variables
  Let be random variables of normal distribution, and the correlation between and be , then where represents post processing function (by “data processing inequality”)
  Ex) , then

## Slide 14: Randomness Sharing (1/3)
Subcarrier allocation
  Both of channel amplitude and phase can be quantized
  We use BPSK
…
…
52 Pilot subcarriers
Guard subcarriers
DC subcarrier
64 Subcarriers
Left 26
Right 26

## Slide 15: Randomness Sharing (2/3)
ITU Pedestrian B Channel Model
  Channel between Alice and Bob is highly correlated

## Slide 16: Randomness Sharing (3/3)
IEEE 802.11 Channel Model
  Channel between Alice and Bob is highly correlated

## Slide 17: Secret Key Agreement Protocol
Alice (STA1)
Bob (STA1)
Quantizer
Quantizer
Reconciliation
Reconciliation
Channel Probing
Privacy Amplification
(w/ compression)
Privacy Amplification
(w/ compression)
Secret key,
Secret key,
-bits
-bits
-bits
-bits
Syndrome
Agree/Disagree
Channel Estimation
Channel Estimation
Randomness Sharing Protocol
Post Processing Protocol For Key Extraction
-bits
-bits
-bits

## Slide 18: Common Key Extraction Protocol
Information reconciliation
  Random bit sequence for extracting secret key is obtained from channel impulse responses with quantization
  In the quantization process, the random bit sequences at legitimate parities may have discrepancy
  Such discrepancy can be removed by performing the information reconciliation [4, 5]

## Slide 19: Information Reconciliation (1/3)
Error correction code based reconciliation
  1) Determine field size :
  2) Estimated discrepancy between and is determined by SNR, quantization method and margin
  3) Given and , calculate the necessary number of parity
  4) If , concatenate sequence and bit zero-padding sequence (shortening).

## Slide 20: Information Reconciliation (2/3)
Error correction code based reconciliation
  5) Else, repeat from 3) with increased
  6) Encode the extended message with systematic BCH ()
    , ,

## Slide 21: Information Reconciliation (3/3)
Error correction code based reconciliation
  7) Alice sends parity parts of the codeword to Bob using public perfect channel
  8) If the number of discrepancy is smaller than error correction capability, i.e. , the errors in the sequence can be corrected.
  9) Then the legitimate parties have exactly same sequence

## Slide 22: Secret Key Agreement Protocol
Alice (STA1)
Bob (STA1)
Quantizer
Quantizer
Reconciliation
Reconciliation
Channel Probing
Privacy Amplification
(w/ compression)
Privacy Amplification
(w/ compression)
Secret key,
Secret key,
Syndrome
Agree/Disagree
Channel Estimation
Channel Estimation
Randomness Sharing Protocol
Post Processing Protocol For Key Extraction
-bits
-bits
-bits
-bits
-bits
-bits
-bits

## Slide 23: Privacy Amplification (1/9)
Privacy amplification
  The parity part of the codeword is also open to the eavesdropper during public discussion
  There must be an additional procedure aiming to extract secret key of which the eavesdropper is totally ignorant

## Slide 24: Privacy Amplification (2/9)
The number of disclosed bits
  Syndrome vector is determined by column combination of parity check matrix with received codeword
  Since the last bit of the codeword, i.e. the parity is disclosed to Eve, there will be an equivocation of bits
Parity check matrix
Syndrome
Disclosed part
Ambiguous part

## Slide 25: Privacy Amplification (3/9)
The number of disclosed bits
  The parity check matrix of BCH code is full rank (i.e. it can be reduced by row/column permutation)
  The equivocation is reduced from bits to bits, i.e. bits are leaked to Eve
Parity check matrix
Syndrome
Disclosed part
Ambiguous part
Reducible part

## Slide 26: Privacy Amplification (4/9)
Privacy amplification
  The number of disclosed bits during public discussion is
  Moreover, because of the channel correlation, bits are disclosed during randomness sharing process

## Slide 27: Privacy Amplification (5/9)
Privacy amplification
  The leaked information about the shared sequence can be removed by using universal hash function
    Ex) the disclosed bit information is eliminated by binary summation
1
?
?
1 bit equivocation over 2 bit
1 bit equivocation over 1 bit

## Slide 28: Privacy Amplification (6/9)
Privacy amplification
  Privacy amplification can be performed with universal hash function (Toeplitz matrix) [6][7]
    Suppose that Alice and Bob have bits after error correction and Eve knows bits
    Choose as a security parameter
    Applying universal hash function
    The remained mutual information about whole secret key after privacy amplification is less than

## Slide 29: Privacy Amplification (7/9)
Privacy amplification

## Slide 30: Privacy Amplification (8/9)
Privacy amplification
  Alice (or Bob) transmits randomly generated bit sequence
  Alice and Bob generate Toeplitz matrix and eliminating the disclosed bits by calculating
  Then the legitimate parties have exactly same bit secret key

## Slide 31: Privacy Amplification (9/9)
Correlation elimination
  In slow fading channel, channel observation between two adjacent subcarriers are correlated
  To guarantee perfect security, these correlation should be eliminated
  Entropy coding is performed to eliminate the correlation between observed sequence
    Huffman coding with a dictionary generated by empirical distribution of quantized bits
    Let is compression efficiency
  The length of final key is

## Slide 32: Information Leakage
Alice (STA1)
Bob (STA2)
Quantizer
Quantizer
Reconciliation
Reconciliation
Channel Probing
Privacy Amplification
(w/ compression)
Privacy Amplification
(w/ compression)
Secret key,
Secret key,
-bits
-bits
-bits
-bits
Syndrome
Agree/Disagree
Channel Estimation
Channel Estimation
Randomness Sharing Protocol
Post Processing Protocol For Key Extraction
-bits
-bits
-bits
-bits
-bits
The amount of information disclosed to Eve
-bits
-bits

## Slide 33: Performance of Proposed Protocol
Experiment results based on computer simulation

## Slide 34: Experimental Environment (1/2)
Experiment setup
  ITU Ped. B / IEEE 802.11 channel model
  IEEE 802.15.8 Low-mobility PHY parameters
  The target secret key length per 10 packet exchanges (including post-processing) is 128 bits
    Starting with 6 consecutive observations (i.e. )
  Randomness sharing
    Quantizing channel frequency response
    1bit quantization is performed in 1 subcarrier (to be optimized with SNR)

## Slide 35: Experimental Environment (2/2)
Experiment setup
  Information reconciliation
    Shortened BCH code
    Overestimated parity bit (lower bound on secret key rate)
  Privacy amplification
    Universal hash function (Toeplitz matrix) is applied with the security parameter
    Residual channel correlation is assumed 0.3
  Correlation elimination
    Entropy coding (Huffman coding)

## Slide 36: Simulation Results
Target key length
SNR

## Slide 37: Conclusion
It is possible for legitimate terminals to share a 128-bit secret key in fully distributed network by exploiting the channel reciprocity and the post processing within 10 packet exchanges
  128-bit secret key is strong enough to encrypt secret message [8]
It is expected that secret key extraction rate can be further increased when we optimize the proposed method using channel information

## Slide 38: Motion
“Accept the text proposal in DCN 15-15-727-01-0008 to be added to P802.15.8 PAC Draft D0.14.0.”

## Slide 39: References
[1] U. Maurer, “Secret key agreement by public discussion from common information,” IEEE Tans. Information Theory, vol. 39, pp. 733-742, May 1993.
[2] G. S. Smith, “A direct derivation of a single-antenna reciprocity relation for the time-domain,” IEEE Trans. Antennas Propagate., vol. 52, no. 6, pp. 1568-1577, Jun. 2004.
[3] Matthew Edman, Aggelos Kiayias, Bulent Yener, “On Passive Inference Attacks Against Physical-layer Key Extraction,” EUROSEC 11, 2011.
[4] C. H. Bennett, E. Bessette, G. Brassard, L. Salvail and J. Smolin, “Experimental quantum cryptography,” Journal of Cryptography, vol. 5, no. 1, pp. 3-28, 1992.
[5] G. Brassard and L. Savail, “Secret-key reconciliation by public discussion,” In Advances in cryptology EUROCRYPT ‘93, Lecture Notes in Computer Science, vol. 765, pp. 410-423, Springer-Verlag, New York, 1994.
[6] Chi-Hang Fred Fung, Xiongfeng Ma, H. F. Chau, “Practical issues in quantum-key-distribution post-processing,” arXiv:0910.0312
[7] Hui, Qiao, Xiao-yu Chen, “Simulation of BB84 Quantum Key Distribution in depolarizing channel,” proc. In 14th Youth Conference on Communication, 2009
[8] Seagate, “128-Bit Versus 256-bit AES Encryption,” http://www.axantum.com/AxCrypt/etc/seagate128vs256.pdf