## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Synchronization Between Channels Towards Global Synchronization]
Date Submitted: [September 2015]
Source: [Huan-Bang Li, Marco Hernandez, Igor Dotlic, and Ryu Miura] Company [NICT]
Address [3-4 Hikarino-oka, Yokosuka, Kanagawa, Japan]
Voice:[+81 468475104], FAX: [:[+81 468475431], E-Mail:[lee@nict.go.jp]
Re: [Contribution to 15.8 PAC draft]
Abstract: [Synchronization Between Channels Towards Global Synchronization]
Purpose: [This document is to provide a MAC mechanism]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Synchronization Between Channels Towards Global Synchronization
Huan-Bang Li, Marco Hernandez, Igor Dotlić, Ryu Miura
(NICT)

## Slide 3: Background
Group agreements
  All PDs in neighborhood should be synchronized no matter they are in a same RF channel or not.
  Use a common mode to enable quick synchronization.
  Use the approved distributed synchronization.
How to realize global synchronization
for PDs in different RF channels?

## Slide 4: Objective
Propose a method to enable global synchronization among devices
in different RF channels.

## Slide 5: What Is Common Mode?
There shall be one and only one common mode defined at each frequency band.
At least, the common mode shall have a fixed RF channel, and fixed PHY parameters.

## Slide 6: Usage of Common Mode
Any PD enters the common mode shall perform the distributed synchronization as adopted in the draft.
An initiator PD shall first get synchronized in common mode.
A PD attempts to join PAC network should first start synchronization in common mode.

## Slide 7: Synchronization Outside Common Mode
Any PD outside the common mode shall perform the distributed synchronization as adopted in the draft but with the following condition:
Only PDs got synchronized in common mode
are allowed to transmit synchronization signal
in any RF channels.

## Slide 8: Synchronization Outside Common Mode (continue)
A PD got synchronized in common mode and starts to transmit synchronization signal in any other RF channels rather than the common mode shall be re-synchronized in common mode for a minimum interval of time or it shall stop transmit synchronization signal.

## Slide 9: Parameters To be decided
A fixed RF channel and fixed PHY parameters for the common mode at each frequency band.
The minimum interval that a PD shall get re-synchronized in common mode.

## Slide 10
Questions?