## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Sub-GHz Proposal for India for 802.15.4]
Date Submitted: [15 September 2015]
Source: [Phil Beecher] Company [Wi-SUN Alliance]
Address [Hove, UK ]
Voice:[+44-7765-400948], FAX: [], E-Mail:[pbeecher@wi-sun.org]
Re: [For consideration by 802.15]
Abstract: [Description of a proposal for Sub-GHz PHY amendment for India for 802.15.4]
Purpose: [For consideration of a PHY amendment to 802.15.4]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Background
There is no single sub-GHz frequency band suitable for use in all geographic / regulatory regions.
Frequency bands and rules are dependent on region
Therefore we need to explicitly specify PHY for each region.

## Slide 3: IEEE 802.15.4 Sub-GHz history
802.15.4-2003
  PHYs for 868.3 MHz (Europe) and 902-928MHz (North America and others)
802.15.4-2006
  Higher data rate PHYs for 868.3 MHz (Europe) and 902-928MHz (North America and others)
802.15.4c
  780 MHz (China)
802.15.4d
  PHY for 950MHz (Japan)
802.15.4f
  PHY for 433MHz (EU)

## Slide 4: IEEE 802.15.4 Sub-GHz history (2)
802.15.4g summary
  PHY amendment for Smart Utility Networks
  Frame size supporting IPv6
  Improved error detection and error correction
  Defined narrow band sub GHz PHYs for a number of regions including:
    470-510 MHz and 779-787 MHz (China)
    868.3 MHz (Europe)
    902-928 MHz (Americas)
    920 MHz (Japan)
    917-923.5 MHz (Korea)

## Slide 5: Smart Utility and Smart City Networks in India
India Smart Meters market estimated at $460 million (source: Frost and Sullivan 2010)
India Smart City market estimated at $45 billion in next 5 years (source: Sustainability Outlook - SCOAM framework)
Sub-GHz Wireless Mesh is ideal technology for metering and distribution automation as well as other Smart City applications in India
India Regulator has made available spectrum for Smart Utility Networks and Smart Cities: 865 - 867 MHz
India Smart Grid Forum (ISGF) and Bureau of Indian Standards (BIS) are defining specifications for Smart Grid in India. These specifications will also be used for Smart City application domains.
ISGF & BIS will use International Open Standards whenever possible.

## Slide 6
Proposal
  802.15 Working Group starts a project to prepare a PHY amendment to 802.15.4 to define parameters for use of 865 – 867 MHz band in India to support smart utility and smart city network requirements