## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Proposed Resolution on some MCO comments(subclause 5.2.4.3) of LB 110
Date Submitted: Oct., 2015
Source: Sangjae Lee, Jaehwan Kim (ETRI), Jaebeom Kim, Jina Han, Youngbae Ko (Ajou Univ.), Soo-Young Chang (SYCA), and Sangsung Choi (ETRI)
Company: ETRI, Ajou Univ., SYCA
Address:
Voice: +82 42 850 5338, E-Mail: kimj@etri.re.kr
Re:
Abstract:
Purpose: To suggest a comment resolution for Letter Ballot #110
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Comment CID 1186
Commentor
  Verotiana Rabarijaona
Related clause
  5.2.4.3 P 29 line 27
Comment
  "each device transmits a TC IE by using its operation channel as described in 4.3" There is no such description in 4.3
Proposed Change
  double check the cross reference

## Slide 3: Proposed resolution for CID 1186
Accept: Change the sentence
Change the reference 4.3 to 5.4.1.3 and figure 23
Rewrite the Subclause
See page 20

## Slide 4: Comment CID 1187
Commentor
  Verotiana Rabarijaona
Related clause
  5.2.4.3 P 29 line 27
Comment
  "each device transmits a TC IE by using its operation channel as described in 4.3"
  A border device (PAN coordinator) works on two different channels, therefore it will need to transmit a TC IE on each channel. explain how the TC IE are constructed and how the device schedules there transmission on each channel
Proposed Change
  See comment

## Slide 5: Proposed resolution for CID 1187
Accept: related sentence is changed
Rewrite the Subclause
See page 20

## Slide 6: Comment CID 1188
Commentor
  Verotiana Rabarijaona
Related clause
  5.2.4.3 P 29 line 28
Comment
  "In an MCO enabled L2R, each coordinator sends a TC IE with the MCO information that indicates the operation channels of the device."
  Which device is referred to here? Is it the coordinator itself, or the devices that are associated with it
Proposed Change
  Specify which device is referred to

## Slide 7: Proposed resolution for CID 1188
Accept: related sentence is changed
Rewrite the Subclause
See page 20

## Slide 8: Comment CID 1189
Commentor
  Verotiana Rabarijaona
Related clause
  5.2.4.3 P 29 line 28
Comment
  "If MCO is used for US/DS routes, the operation channel information of the neighbor device is stored to the entry of the corresponding neighbor in the NT in order to identify the operation channel of the next-hop device in the routing path."
  A device that is not a "border" PAN coordinator can only receive frames on the channel of the PAN it is associated with. Therefore, a device's neighbors will only be the other devices within the same PAN, except for the PAN coordinator whose neighbors will be its children and the devices in the parent PAN that are 1 hop away.
  This results in a mesh topology within each PAN but a tree topology of sub-meshes overall.
Proposed Change
  State that only PAN coordinators require the operation channel information of a neighbor.
  Modify Figure 3 to have inter-PAN L2R mesh link only between PAN coordinators: reject
  State somewhere in the document that the topology is a tree topology between PAN coordinators and a mesh topology within each PAN

## Slide 9: Proposed resolution for CID 1189
Accept in principle: related sentence is changed
Rewrite the Subclause
See page 20
For commentor’s 2nd suggestion
  Figure 3 shows a single channel multiple PANs environment. Thus, each device between PANs can exchange the TC IE and construct route without specific border PAN coordinator.

## Slide 10: Comment CID 1191
Commentor
  Verotiana Rabarijaona
Related clause
  5.2.4.3 P 29 line 28
Comment
  "channels" Is this a typo or is it really supposed to be plural
Proposed Change
  Double check

## Slide 11: Proposed resolution for CID 1191
Accept: double check is done. It is typo
Change “channels” to “channel”
Rewrite the Subclause
See page 20

## Slide 12: Comment CID 1194
Commentor
  Verotiana Rabarijaona
Related clause
  5.2.4.3 P 29 line 32
Comment
  What is a "DATA-DATA frame procedure"?
Proposed Change
  Rephrase and explain

## Slide 13: Proposed resolution for CID 1194
Accept in principle: the sentence is removed and the paragraph is modified.
Rewrite the Subclause
See page 20

## Slide 14: Comment CID 1195
Commentor
  Verotiana Rabarijaona
Related clause
  5.2.4.3 P 29 line 32
Comment
  "to find a valid packet for data transmission in current operation channel of the device" is unclear. Does this mean that a device buffers frames? This sentence doesn't seem to belong here, since it is not related to route establishment but to routing itself
Proposed Change
  Rephrase to clarify and move to the routing clause

## Slide 15: Proposed resolution for CID 1195
Accept in principle: the sentence is removed and the paragraph is modified.
Rewrite the Subclause
See page 20

## Slide 16: Comment CID 1197
Commentor
  Verotiana Rabarijaona
Related clause
  5.2.4.3 P 29 line 33
Comment
  The US route establishment uses TC IEs but DS route establishment uses L2R Routing, RA, SLR or SRA IEs. It looks like only the US route establishment is described in this clause.
Proposed Change
  Describe the DS route establishment and add a figure

## Slide 17: Proposed resolution for CID 1197
Accept: related sentences about DS route construction are added
For the DS route construction, each device uses the RA/P2P RP-IE with MCO. When a device receives RA/P2P-RP IE MCO, it stores DS channel information of the neighbor. The RA/P2P-RP IE MCO is updated by each forwarder device when a received MCO channel is different from forwarder device.
Rewrite the Subclause
See page 20

## Slide 18: Comment CID 1200
Commentor
  Verotiana Rabarijaona
Related clause
  5.2.4.3 P 29 line 33
Comment
  A figure to describe the route establishment would be helpful, depicting the TC IE exchange from one PAN to another, etc.
Proposed Change
  Add a figure to describe route establishment

## Slide 19: Proposed resolution for CID 1200
Accept in principle: Cross reference figure is added.
The details of multi-channel route establishment procedure is described in 5.4.1.3 and figure 23.
Rewrite the Subclause
See page 20

## Slide 20: Proposed resolution for CID 1186−1189, 1191, 1194, 1195, 1197, 1200
Accept: several comments related to 5.2.4.3 section are resolved
[P 29] When the MCO field in the L2R-D IE is set to 1, the L2R spans more than one PAN operating on different channels and the MCO Descriptor field is present in the TC/RA/P2P-RE/P2P-RP IE for IEEE 802.15.4m TMCTP. If MCO is used for US/DS routes, the operation channel information of the neighbor device is stored to the entry of the corresponding neighbor in the NT in order to identify the operation channel of the next-hop device in the routing path. All devices must aware the Parent PAN channel information to decide whether PAN coordinator can be connected or not at the certain time in TMCTP environment. The details of multi-channel route establishment procedure is described in 5.4.1.3 and figure 23. In the L2R, tree topology will be constructed between PANs through PAN coordinators, but mesh topology is constructed in a PAN.
For the US route construction, each device transmits a TC/P2P-RQ IE by using its operation channel as described in 5.4.1.3. In TMCTP environment, each device duplicates generated TC IE frame for multi-channel TC IE broadcasting and duplicated TC IE can be transmitted to all channels of the device depending on IEEE 802.15.4m TMCTP superframe scheduling. In an MCO enabled L2R, each TMCTP PAN coordinator sends a TC/P2P-RQ IE with the MCO information that indicates the a parent PAN page and channel of a PAN coordinator for US route construction. When a device receives a TC/P2P-RQ IE with a valid MCO descriptor, it stores the channel information of the TC/P2P-RQ IE sender in the NT. Also, each device in the PAN broadcasts TC IE with received parent PAN channel information. For the DS route construction, each device uses the RA/P2P RP-IE with MCO. When a device receives RA/P2P-RP IE MCO, it stores DS channel information of the neighbor. The RA/P2P-RP IE MCO is updated by each forwarder device when a received MCO channel is different from forwarder device.