## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Proposed Resolution on some MCO comments of LB 110
Date Submitted: Oct., 2015
Source: Sangjae Lee, Jaehwan Kim (ETRI), Jaebeom Kim, Jina Han, Youngbae Ko (Ajou Univ.), Soo-Young Chang (SYCA), and Sangsung Choi (ETRI)
Company: ETRI, Ajou Univ., SYCA
Address:
Voice: +82 42 850 5338, E-Mail: kimj@etri.re.kr
Re:
Abstract:
Purpose: To suggest a comment resolution for Letter Ballot #110
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Comment CID 1149
Commentor
  Verotiana Rabarijaona
Related clause
  5.2.1 P 23 line 29
Comment
  "on which the coordinator" Why the coordinator's channel instead of the neighbor's channel? Is this supposed to the "PAN coordinator"?
Proposed Change
  Double check. Same thing in l.34

## Slide 3: Proposed resolution for CID 1149
Accept: double check is done.
[P 23 line 29] Original sentence is correct: PAN device need to get a PAN coordinator's allocated channel information to decide its frame transmission timing. For example, in TMCTP, PAN coordinator and device may not be always connected because the coordinator's channel can be changed. Thus, the device keeps the parent channel information whether the coordinator is connected or not. If the device's channel and allocated channel information of the parent is same, then device can transmit the frame to PAN coordinator while its any active duration. If not, the device need to decide the frame transmission timing depending on parent's operation channel.

## Slide 4: Comment CID 1162
Commentor
  Verotiana Rabarijaona
Related clause
  5.2.2.3 P 26 line 21
Comment
  "This metric reflects the amount of channel resources consumed by transmitting a frame over a particular link and the available time of the link in a multi-PAN environment." This definition is unclear.
Proposed Change
  A new definition has been added before "The expected airtime is represents the airtime considering the inactive time of a device." so delete this sentence if it is not needed anymore. Otherwise explain which part of the equation represents "the resources consumed" and which part represents "the available time". Or rephrase

## Slide 5: Proposed resolution for CID 1162
Accept : remove issued context. P 26 Line 20
[P 26 line 21] The expected airtime is represents the airtime considering the inactive time of a device. This metric reflects the amount of channel resources consumed by transmitting a frame over a particular link.

## Slide 6: Comment CID 1163
Commentor
  Verotiana Rabarijaona
Related clause
  5.2.2.3 P 26 line 22
Comment
  "in a multi-PAN environment". Does this mean that the metric can't be used in a single PAN environment?
Proposed Change
  Delete or also address the single PAN case

## Slide 7: Proposed resolution for CID 1163
Accept: Delete
[P 26 line 22] This metric reflects the amount of channel resources consumed by transmitting a frame over a particular link and the available time of the link in a multi-PAN environment.

## Slide 8: Comment CID 1199
Commentor
  Verotiana Rabarijaona
Related clause
  5.2.4.1 P 29 line 9
Comment
  RA IEs may be used even if the DS Route Required is not enabled, for example to advertise a multicast address
Proposed Change
  insert a sentence stating that RA IEs may be transmitted even if DS route requires is set to 0 when a device needs to advertises its membership in a multicast group

## Slide 9: Proposed resolution for CID 1199
Accept: add a related sentence
[P 29 line 9] When an intermediate hop receives a RA IE, the address of the original source found in the Source Address field of the RA IE is stored in the list of reachable destinations of the neighbor the frame was received from. RA IEs may be transmitted even if DS route required is set to 0 for advertising its membership in a multicast group.

## Slide 10: Comment CID 1367
Commentor
  Verotiana Rabarijaona
Related clause
  6.2.2.8 P 55 line 40
Comment
  Some channel number fields use 9 bits and some use 2 octets in 15.4.
Proposed Change
  Check the size of the Allocated Channel Number. Explain how does one determine the size of the field upon reception

## Slide 11: Proposed resolution for CID 1367
Accept: the size of Allocated Channel Number field is typo. The size is 1 octet. [P 55 line 40]

## Slide 12: Comment CID 1370
Commentor
  Verotiana Rabarijaona
Related clause
  6.2.2.8 P 55 line 46
Comment
  What is the use of the "Associated PAN Coordinator" field?
Proposed Change
  Delete this field or describe in the use and the way to process this field in the functional description

## Slide 13: Proposed resolution for CID 1370
Accept in principle: Name of "Associated PAN Coordinator" field is changed to “Parent PAN coordinator Channel Number”

## Slide 14: Comment CID 1371
Commentor
  Verotiana Rabarijaona
Related clause
  6.2.2.8 P 55 line 50
Comment
  "on which the coordinator" should this be the "PAN coordinator"? See also l.53
Proposed Change
  Double check

## Slide 15: Proposed resolution for CID 1371
Accept:
Change “coordinator” to “the parent PAN coordinator”

## Slide 16: Comment CID 1458
Commentor
  Tero Kivinen
Related clause
  7.1.1.4 P 76 line 21
Comment
  How are the MCO related parameters set to the MAC. If MCO is enabled we need Associated PAN Coordinator, Allocated Channel Number and Allocated Channel Page. How does the higher layer set those?
Proposed Change

## Slide 17: Proposed resolution for CID 1458
Accept in principle:
Proposed L2R is operated with IEEE 802.15.4m TMCTP environment. Thus, the L2R can access the channel information related to superframe scheduling information of the IEEE 802.15.4m.