## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Proposal for IEEE802.15.3e – MAC ]
Date Submitted: [6 November 2015]
Source: [Itaru Maekawa (1), Jae Seung Lee, Ken Hiraga, Makoto Noda, Ko Togashi, (representative contributors), all contributors are listed in “Contributors” slide]
Company: [ETRI, JRC1, NTT, Sony, Toshiba]
Address1: [Mitaka, Tokyo, Japan]
E-Mail1: [Maekawa.Itaru at jrc.co.jp (all contributors are listed in “Contributors” slide)]
Abstract: This document presents an overview of the full MAC/PHY proposal for HRCP.
Purpose: To propose additional protocol for TG 3e full proposal
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributors acknowledge and accept that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
Contributors
Name | Affiliation | Email
Jae Seung Lee | ETRI | jasonlee at etri.re.kr
Moon-Sik Lee | ETRI | moonsiklee at etri.re.kr
Itaru Maekawa | Japan Radio Co., Ltd. | maekawa.itaru at jrc.co.jp
Doohwan Lee | NTT Corporation | lee.doohwan at lab.ntt.co.jp
Ken Hiraga | NTT Corporation | hiraga.ken at lab.ntt.co.jp
Masashi Shimizu | NTT Corporation | masashi.shimizu at upr-net.co.jp
Keitarou Kondou | Sony Corporation | Keitarou.Kondou at jp.sony.com
Hiroyuki Matsumura | Sony Corporation | Hiroyuki.Matsumura at jp.sony.com
Makoto Noda | Sony Corporation | MakotoB.Noda at jp.sony.com
Masashi Shinagawa | Sony Corporation | Masashi.Shinagawa at jp.sony.com
Ko Togashi | Toshiba Corporation | ko.togashi at toshiba.co.jp
Kiyoshi Toshimitsu | Toshiba Corporation | kiyoshi.toshimitsu at toshiba.co.jp

## Slide 3
Proposal for IEEE802.15.3e
High-Rate Close Proximity System
November, 2015

## Slide 4
  1.Aggregation length control
  2.Low latency power saving
  3.Consideration for RIFS length
Contents

## Slide 5
Proposal for IEEE802.15.3e
Aggregation length Control
November, 2015

## Slide 6
Appropriate Number of Frame aggregation is introduced by the magnitude relation of TPair and TPbus.
Add “Buffer empty flag” in Rate adaptation information in ACK, to inform the magnitude relation of TPair and Tpbus.
“Buffer empty flag” shall be “1” if RX FIFO was empty before receiving the latest frame .
  It indicate “BUS “ had idle term.
Aggregation Number Control(1)
802.15.3e Specification
RX
Buffer
TPair
Memory
And
Storage
TPbus
Transmitter

## Slide 7
Rate Adaptation control: should be introduced by FER.
Aggregation Number Control: should be introduced by Status of RX FIFO.
Aggregation Number Control (2)
Implementation Example
RX
Buffer
TPair
Memory
And
Storage
TPbus
 | Buffer full flag | Buffer empty flag | Number of Aggregation | Note
TPair<TPbus | 0 | 1 | up | Bus has tolerance. Aggregation Number should be up to increase TPair
Tpair≒TPbus | 0 | 0 | stay | Good Balanced State
Tpair>TPbus | 1 | 0 | down/(stay) | Should be down in the case of bidirectional transmission.
Tpair>>TPbus | 1 | 1 | down | Buffer full was occurred, but Bus has idle time because discarding “too long data”
Transmitter

## Slide 8
Proposal for IEEE802.15.3e
Low Latency Power Saving
November, 2015

## Slide 9: Low Latency Power Saving -motivation-
File Transfer Application : Power Saving mode is not required.
Wireless Storage (SCSI/MTP over HRCP), Ether over HRCP: Power Saving mode is required.
Power Saving efficiency vs latency is trade off in general.
Large latency (Aggressive power saving) may cause fatal degradation for QoS of real time application.
Very Best Power Saving Setting is very difficult & Complicate.
  However……
Most of Application is running without having power saving term.
    -System has some level of power consumption offset.
    -Risky, fine tuned Power saving can not offer great benefit.
      Power Saving with Low latency (less than 10msec) & Modesty saving ratio : Almighty & Practical Setting

## Slide 10
Sub-F#N+1
Sub-F#N
ACK#M
Sub-F#M+1
ACK#N+1
Time #1
Time #2
Time #3
Time #4
SIFS
PPC
Dev
PPC
Dev
PPC
Dev
PPC
Dev
ACK#M+2
SIFS
PHY
Header
MAC
Header
HCS
Sub
Header
Sub
Frame
HCS
FCS
ACK#M+1
ACK#N+1
ACK#M+1
SIFS
ACK#N+1
ACK#M+1
SIFS
SIFS
SIFS
ACK#M+1
ACK#N+1
RIFS(B)
ACK#M+1
RIFS(A)
ACK#M+1
RIFS(A)
SIFS
Sleep Flag=1
Sub-F#N+3
Sub-F#N+2
ACK#1
Sub-F#M+2
ACK#N+3
SIFS
SIFS
SIFS
LLPS Start Condition
LLPS Period
LLPS Extend Condition
ACK#N+1
ACK#M+1
SIFS
ACK#M+1
ACK#N+1
RIFS(B) x multiple #
ACK#M+1
RIFS(A)
SIFS
ACK#N+1
Sleep Flag=1
ACK#N+1
RIFS(B)
ACK#N+1
Low latency Power Saving(2)

## Slide 11: Low latency Sleep Mode (3)
Power Saving Start Condition
Power Saving Period
Power Saving Extend Condition
 | Ethernet | Wireless Storage | 
Start Condition | 100usec | 100usec | 
Period | 10msec | 100msec | 
Extend Condition | 100usec | 100usec | 
Power Saving Ratio | 90-95% | 99% | Several 10mW order
Three Power Saving Parameters
Setting Example

## Slide 12
Proposal for IEEE802.15.3e
Consideration for RIFS length
November, 2015

## Slide 13: RIFS
Sub-F#N+4
Sub-F#N
ACK#M
ACK#N+4
Time #1
Time #2
Time #3
SIFS
PPC
DEV
PPC
DEV
PPC
DEV
Short RIFS=2SIFS+ACK
Sub-F#N+9
Sub-F#N+5
ACK#M
ACK#N+9
SIFS
SIFS
ACK#M
ACK#N+9
Short RIFS=2SIFS+ACK
Sub-F#M+1
ACK#N+9
SIFS
SIFS
ACK#M
ACK#N+9
SIFS
ACK#M
<SIFS
ACK#M
Sub-F#M+10
Short RIFS=2SIFS+ACK
Long RIFS=2SIFS+2ACK+ShortRIFS
SIFS
SIFS for PPC and DEV in Synchronous Phase
Short RIFS for PPC in Recovery Process
Long RIFS for DEV in Recovery Process