## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [DCN 15-15-0805-01-0llc IETF [intarea] report introducing 802.15.llc]
Date Submitted: [4 November, 2015]
Source1: [Charlie Perkins] Company [Futurewei]
Address [2330 Central, Santa Clara, CA 95050]
Voice:[+1-408-330-45860], E-Mail:[charles.perkins@earthlink.net]
Re: [15-15-0761-00-0llc-llc-proposal-for-802-15-4]
Abstract: [802.15.llc study group is being chartered to simplify the use of 802.15.4 base and extensions]
Purpose: [802.15.llc study group is relevant to IETF 6TtiSCH, and so should be introduced for discussion]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Outline of Presentation
Introduction
Relevant IEEE 802.1, 802.15 efforts
802.15.llc background and description
802.15.llc scope of intended effort
802.15.llc priority and timeline

## Slide 3: IEEE 802.15.llc (Logical Link Control)
A new IEEE 802.15 project is being considered to:
  Make IEEE 802.15.4 easier to use, similar to IEEE 802.11 (WiFi) and IEEE 802.3 (Ethernet)
  Enable IEEE 802.15.4 to use many of the higher layer protocol stacks used by IEEE 802.11 and IEEE 802.3 without changes
  Allow IEEE 802.15.4 to address new applications yet maintain backward compatibility with existing devices and applications

## Slide 4: Other relevant 802.15 and 802.1 efforts
802.15.9 – KMP (Key Management Protocol)
802.15.10 – L2R (Layer 2 Routing Mesh)
802.15.4mc – Revision
  Completed Sponsor Ballot revision
802.15.4t – a new 2.4 GHz PHY
  2.5 GHz band; 2 Mb/s data rate
  backward compatible to original 250 kb/s data rate
802.1CF – OmniRAN Task Group
802.1AS – TSN Task Group

## Slide 5: Target Applications for 802.15.12
Deterministic
  ISA100.11a
  IETF 6TiSCH
  Industrial Internet of Things (IIoT)
Non-Deterministic (best effort)
  Smart Grid (e.g. WiSUN™)
  Internet of Things (IoT)
  Long Range Infrastructure
    e.g., LECIM (Low energy critical infrastructure monitoring)

## Slide 6: General Concept
  Create a Data Link sublayer above the MAC that adapts and configures the 802.15.4 MAC for desired operation, and contains existing and soon to be released sub-layers for 802.15.4 such as 6LoWPAN, Key Management Protocol (KMP), Layer 2 Routing Mesh (L2R), 6top (IETF 6TiSCH)

## Slide 7: Protocol Layers
Transport Layer
Network Layer
Data Link Layer
Physical Layer
UDP, TCP, ICMP
IPv6 (IPv4 with adapter)
LLC (802.15.12)
MAC (802.15.4)
802.15.4 Modulations: O-QPSK,BFSK, FSK, OFDM
802.15.4 Frequency Bands: (433, 890, 915, 2450, et al)

## Slide 8
IEEE 802.15.4 MAC
…
TSCH
CSMA
IEEE 802.15.4 PHY
…
4k
2003
4g
LPWA:
LECIM
other non-IP
IPv4
New LLC work
Deterministic
Best Effort
6TiSCH
ISA100.11a
6LoWPAN
WiSUN
Zigbee
IP
OTF
…
…
…

## Slide 9: 802.15.12 LLC would serve:
KMP
6LoWPAN
IPv6 network adaption standard for 802.15.4 (RFC 6775)
6top
Part of IETF 6TiSCH standard for TSCH (deterministic behavior adapted from WHART and ISA100.11a)
L2R
Layer 2 Mesh routing standard (IEEE 802.15.10)
Key Management Protocol Layer 2 standard (IEEE 802.15.9)

## Slide 10: 802.15.12 would also include
802.15.4 MAC
PAN Configuration
Security Configuration
Channel Configuration
New features, such as: - Duplicate frame detection - Priority operation
- EtherType (indicates protocol)
Information Element (IE) creation/use
-To standardize L2 data handling
- Thus, LLC plays the role of the “upper layer”

## Slide 11: Background
IEEE 802.15.4’s approach has been to keep the MAC simple and the PHY simpler.
Complex decisions determining MAC behaviors were passed to the next higher layer. For example:
  Should the node join a specific network?
  What short address does coordinator allocate to a node?
  What data rates, modulations, et al. should be used?
The above approach resulted in 802.15.4 not being as easily used as 802.11 and 802.3, since the 802.15.4 higher layers must do many additional operations (which may be poorly described).

## Slide 12: Issues
Although IEEE 802.15.4 is extremely popular with vendors and users, each user application needs a specific protocol stack
Older versions of 802.15.4 didn’t address many of the new application needs, hence user application stacks added their own enhancements
Security on older versions of 802.15.4 did not function correctly, hence user application stacks used their own security

## Slide 13: Issues (continued)
802.15.4 couldn’t serve multiple higher layer protocols
Proprietary protocols such as LoRA™ and SigFox™ have arisen due to the complexity of 802.15.4 protocols. There has been misunderstanding about how to use specific 802.15.4 modes and the performance gains they can give.

## Slide 14: 802.15.12 Benefits
802.15.12 will be able to configure the 802.15.4 MAC and PHY with security, network, and channel settings via defaults or settings received using other protocols
Thanks to (a), IC or stack vendors will be able to provide consistent and standardized mechanisms to set up networks and links
Consequently, IEEE 802.15.4 will find use in new applications and will better address existing applications

## Slide 15: PAR for 802.15.12
  Expected Date of submission of draft for Sponsor Ballot: 12/2017
  Projected Completion Date for Submittal to RevCom: 08/2018
  Approximate number of people … actively involved in development: 100
  Scope: Create a Logical Link Control (LLC) sublayer in the Data Link Layer (DLL), above the IEEE 802.15.4 MAC sublayer that … provides operational configuration of IEEE 802.15.4
    Examples of existing and soon to be released functionalities for IEEE 802.15.4 are 6LoWPAN, IEEE 802.15.9 Key Management Protocol, IEEE 802.15.10 Layer 2 Routing Mesh, and IETF 6TiSCH 6top
    Examples of configuration for regulation requirements include: PHY Configuration as per country of operation, Device class, Duty cycle constraints, CCA settings (e.g., time, threshold, and mode)
  Need for the Project: The 802.15.4 LLC is needed to provide to higher layer protocols a useful abstraction for 802.15.4 devices, … integrate DLL protocols … such as Key Management Protocol (KMP) and Layer 2 routing, and to fulfill 802.15.4 MAC configuration needs for operation such as network and channel configuration.
  Stakeholders for the Standard: The stakeholders include (i) chip vendors, (ii) manufacturers and users of telecom, medical, environmental, energy, and consumer electronics equipment and (iii) manufacturers and users of equipment involving the use of wireless sensor and control networks.

## Slide 16: CSD for 802.15.12
CRITERIA FOR STANDARDS DEVELOPMENT (CSD)
Project process requirements
  Managed objects <none>
  Coexistence <no changes to MAC or PHY>
  5C requirements
  Broad market potential <IoT>
    Multiple vendors and numerous users
  Compatibility <Already broad acceptance of 802.15.4>
  Distinct Identity <802.15.4 does not encroach on other efforts>
  Technical Feasibility <Proprietary solutions exist>
  Economic Feasibility <IoT>

## Slide 17: Network Discovery and Selection Support
The functionality of Generic Advertisement Service (GAS) (as specified for 802.11) enables nodes to discover information related to desired network services in a standardized fashion
  e.g., information about services that are provided in a WPAN, local access services, or other external networks

## Slide 18: Network Setup
PAN Coordinator default parameters
  Addressing
  PAN ID (or no PAN ID)
  Mode: Beacon-enabled / Nonbeacon-enabled
Topology
  Mesh or Star
Link set up
  channel(s), modulation parameters, data rate(s), transmit power(s), Low Energy mode(s), FCS size, CSMA settings
Channel Hopping Network
  changing frequencies periodically
Asymmetric Network
  802.15.4 devices are either high or low capability

## Slide 19: Security Set-up
Authentication and encryption
Policy settings (network keys only or link keys, security level by frame type, by IE type, etc.)
Key management protocol, such as 802.15.9
Authorization

## Slide 20: Management / Measurement
Collection of network metrics
Neighbor tables
Information Elements (IEs)
  Build IEs for transmission to other devices
  Decode IEs received from other devices
  Prepare IEs such as ESDUs intended for other device’s higher layers

## Slide 21: Regulatory Matters
Country of operation
Device class
  Duty cycle constraints
CCA settings (time, threshold, mode)

## Slide 22: Dynamic Behaviors
Dynamic behaviors allow a network/device to adapt to changing conditions and maintain performance. IEEE 802.15.12 proposed dynamic behaviors include:
Dynamic Data Rate Selection
  For those PHYs with multiple data rates, data rates could be better set by 802.15.12 on a link-by-link basis
Dynamic Transmit Power Selection
  For PHYs with defined multiple transmit power levels, 802.15.12 could set transmit power level on a link-by-link basis considering CSMA impact, PHY Preambles, PHY FEC, signal strength, failed packets
Dynamic Channel Selection
  For fixed frequency operation maintain current channel status such as coexistence issues and interferers and periodically search other channels for better link quality conditions and change to another channel if advantageous
Dynamic Preamble Selection
  For PHYs with multiple preamble, 802.15.12 will configure the MAC to verify the preamble’s effect on the link and then configure the MAC for the best preamble
Dynamic Modulation Selection
  For PHYs with multiple modulation options 802.15.12 will configure the MAC to test modulation effectiveness and then configure the MAC for the best modulation

## Slide 23: Emulation of standard L2 protocols based upon 802.15.4
802.15.12 could be enhanced with further ISA100.11a behaviors building on TSCH
IETF 6top is already in development
Others?

## Slide 24: Prioritized Functionality (first release)
Protocol differentiation (dispatch)
Align 802.15.9 and 802.15.10 with LLC
Architecture to provide extensibility
Regulatory configuration, e.g. PHY Configuration as per country of operation, Device class, Duty cycle constraints, CCA settings (time, threshold, mode)
L2 protocol extensions from other organizations, e.g. IETF 6TiSCH 6top, Thread™

## Slide 25: Proposed Timeline
Next Week: Study Group (SG) discuss input from IETF, review PAR and CSD
January Interim: SG Submit PAR & CSD
March Plenary: EC approval
  If not in March, then not until July
Projected Date for Sponsor Ballot:12/2017
Projected Completion: 08/2018

## Slide 26: 802.1AS OmniRAN
OmniRAN is another project within IEEE 802 Wireless that aims to provide a broadly applicable LLC to higher level protocols
Originally intended to bridge between 802.16 and 802.11 (and of course to 802.15, 802.21, etc.)
May be considered to reside at a broader level than 802.15.12, which aims mainly to produce convenient interface just for 802.15.4 MAC and PHY layers
Has gotten new interest from 802.11, which also has a number of variations (data rate, MIMO, etc.)

## Slide 27: 802.1CF TSN (time sensitive network)
Responsible for Layer 2 operations, to define a common architecture for both Layer 2 and Layer 3.
Deterministic network applications include professional and home audio/video, multimedia in transportation, engine control systems, and other general industrial and vehicular applications.
Collaborates with Detnet that focuses on deterministic data paths that operate over Layer 2 bridged and Layer 3 routed segments.

## Slide 28: Minimal presentation slides
The following slides are an abbreviated version of the foregoing, for the purposes of discussion within 6TiSCH, 6lo, and roll.

## Slide 29: IEEE 802.15.llc (Proposed work on Logical Link Control)
Study Group meets next week; target acceptance of PAR / CSD in March
  Want input from IETF for the SG meeting
For 802.15.4 to make it as easy to use as 802.11 (WiFi) and 802.3 (Ethernet)
  Enable use of the higher layer protocols used by IEEE 802.11 and IEEE 802.3 without changes
  New applications & backward compatibility
Provide LLC for KMP, L2R

## Slide 30
IEEE 802.15.4 MAC
…
TSCH
CSMA
IEEE 802.15.4 PHY
…
4k
2003
4g
LPWA:
LECIM
other non-IP
IPv4
New LLC work
Deterministic
Best Effort
6TiSCH
ISA100.11a
6LoWPAN
WiSUN
Zigbee
IP
OTF
…
…
…

## Slide 31: Prioritized Functionality (first release)
Protocol differentiation (dispatch)
Align 802.15.9 and 802.15.10 with LLC
Architecture to provide extendibility
Regulatory configuration, e.g. PHY Configuration as per country of operation, Device class, Duty cycle constraints, CCA settings (time, threshold, mode)
L2 protocol extensions from other organizations, e.g. IETF 6TiSCH 6top, Thread™

## Slide 32: Links for LLC information; Proposed Timeline
https://mentor.ieee.org/802.15/dcn/15/15-15-0838-00-0llc-ietf-intarea-presentation-introducing-802-15-llc.pptx
https://mentor.ieee.org/802.15/dcn/15/ - pick SG LLC for all LLC documents
Next Week: Study Group (SG) discuss input from IETF, review PAR and CSD
January Interim: SG Submit PAR & CSD
March Plenary: EC approval
  If not in March, then not until July
Projected Date for Sponsor Ballot:12/2017
Projected Completion: 08/2018