## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Proposal for SRM IE and TPC PIB in Technical Guidance Document]
Date Submitted: [7 November, 2015]
Source: [Hidetoshi Yokota, Ruben Salazar and Chris Calvert] Company [Landis&Gyr]
Address: [1-2-9 Nishi Shimbashi Minato-ku, Tokyo 105-0003, Japan,
30000 Mill Creek Av., Alpharetta, GA 30022, USA ]
Voice: [+81 3-5532-7455, +1 678 258 3165, +1 678 258 1516], E-Mail:[hidetoshi.yokota@landisgyr.com, ruben.salazar@landisgyr.com, chris.calvert@landisgyr.com]
Re: [“TG4s Technical Guidance Document”, IEEE 802.15-14-0555-06-004s]
Abstract: [This contribution proposes Information Elements for SRM and PIB for Transmit Power Control that should be considered in the Technical Guidance Document for measuring spectrum resources in WPAN.]
Purpose: [Discussion and approval]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
Proposal for SRM IE and TPC PIB in Technical Guidance Document
Authors:

## Slide 3: Outline of the proposal
Propose SRM Information Element
Propose TPC for WPAN
Discussion
  Handling of existing MAC metrics IEs
References [1] IEEE802.15.4-REVc-D00

## Slide 4: SRM Information Element in Header IEs (IEEE802.15.4-REVc-D00[1])
Element ID | Name | Subclause
0x2a | SRM IE | 7.4.2.18
Bits:0-5 | 6-7 | Octet: 4
SRM Metric ID | Scope | Value
Format of SRM Metric ID
Attribute name | SRM Metric ID b5b4b3b2b1b0
macED | 000000
MacTxFailTime | 000001
… | …
SRM Metric ID
Measured range | Scope ID b1 b0
Link | 00
Path | 01
Network | 10
Reserved | 11
Scope
on the link of the transmitting device
on the path to/from PAN coordinator
over the entire PAN
Attribute represents the performance:

## Slide 5: Use case (1) Scope-based Performance Metric
Bits:0-6 | 7-14 | 15 | Octets:0-127 |  | 
Length | Element ID=0x2a | Type=0 | Bit:0-5 | 6-7 | Octet:0-126
 |  |  | Metric ID=0x12 | Scope=01 | Value=100
Attribute name | SRM Metric ID b5b4b3b2b1b0
… | …
macTxFailCount | 010010
… | …
SRM Metric ID
device
PAN
coordinator
device
device
device
device
device
device
Link-scope(00)
Path-scope(01)
Network-scope(10)
Enhanced Beacon
Header IE
how path-scope and network scope performance is calculated is outside the scope of the specification

## Slide 6: Transmit Power Control
Benefits
  Enable efficient spatial re-use of the radio spectrum by minimizing interference
  Contributes to network performance-aware applications
  Alleviates the well-known "hidden" and "exposed" node problems that are encountered in wireless mesh networks
Node-by-node and/or communication type-based TPC will provide optimized control
phyBroacastTxPower
phyUnicastTXPower
peersTXPower (for specific peer devices)

## Slide 7: PIB description for Transmit Power Control (IEEE802.15.4-REVc-D00[1])
10.1.5 Transmit power
A compliant device shall have its nominal transmit power level indicated by its PHY parameter, phyTXPower, as defined in 11.3. This value may be a well-known or acquired by joining devices from the Maximum Transmit Power Information Element, phyMaxTxPower,in Enhanced Beacons. The maximum transmit power shall conform with local regulations.
The transmit power can further be set individually according to the communication type indicated by phyBroadcastTxPower, phyUnicastTXPower and peersTXPower.
* Proposed text is in red

## Slide 8: Use case (2) Max Transmit Power in Enhanced Beacon
Bits:0-6 | 7-14 | 15 | Octets:0-127 |  | 
Length | Element ID=0x2a | Type=0 | Bit:0-5 | 6-7 | Octet:0-126
 |  |  | Metric ID=0x06 | Scope=10 | Value=+10(dBm)
Attribute name | SRM Metric ID b5b4b3b2b1b0
… | …
phyMaxTXPower | 000110
… | …
SRM Metric ID
Device
Advertiser
Enhanced Beacon
Header IE
Set phyTxPower, etc.

## Slide 9: PIB attributes for TPC
11.3 PHY PIB attributes
Table 181 - PHY PIB attributes
Attribute | Type | Range | Description
phyTXPower | Signed Integer | － | Nominal transmit power of the device in dBm acquired during the joining process derived from phyMaxTXPower or predefined.
phyMaxTXPower | Signed Integer | － | Nominal transmit power level allowed on a network.
phyBroadcastTxPower | Signed Integer | － | Transmit power in dBm while broadcasting. This value is managed by an upper layer but shall be lower or equal to phyTXPower.
phyUnicastTXPower | Signed Integer | － | Transmit power in dBm while sending a unicast. This value is managed by an upper layer but shall be lower or equal to phyTXPower.
peersTXPower | List of peerTXPower as defined in Table 183? | － | List of exceptions to the phyUnicastTXPower while transmitting to specific peer devices.
Existing

## Slide 10: PIB attributes for TPC (continued)
Table 183? - Elements of PeersTXPower
Attribute | Type | Range | Description
deviceAddrMode | Enumeration | SHORT_ADDRESS, EXTENDED_ADDRESS | 
deviceAddress | As specified by the deviceAddrMode Parameter |  | Address of the peer device.
TXPower | Signed integer |  | Transmit power in dBm while transmitting to this peer. This value is managed by an upper layer but shall be lower or equal to phyTXPower.

## Slide 11: Discussion
Handling of existing MAC metrics IEs
  MAC Metrics IE (Sub-ID=0x1f) and All MAC Metrics IE (Sub-ID=0x20) are defined in Payload IE:MLME IE:Nested IE (7.4.4.1 Table 19)
    10 Attributes (macCounterOctets,…) are assigned Metric Count ID (0x00-0x0a) (7.4.4.7 Table 21)  all reused by SRM
  Should these IEs be obsoleted?